## Slide 1: Status and Commissioning Strategy for the Undulator Systems of the European XFEL
J. Pflüger,
representing WP71: S. Abeghyan, M. Bagha-Shanjani, U. Englisch, S. Karabekyan, F. Preisskorn, F. Wolff-Fabris, P. Li, Y. Li T. Wei, M. Wünschel, M. Yakopov
Betriebseminar 2016
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)

## Slide 2: Overview
The Undulator Systems of the European XFEL
Representative Magnetic Measurements, Re-measurement Campaign
 Startup Strategy for Commissioning
Status of Undulator Control System
  Status & Plan of Tunnel Installation: SASE1, SASE2, SASE3

## Slide 3: The XFEL Undulator Systems in Tunnels XTD1, XTD2 and XTD4
“Naked“ Undulator System
With Air Conditioning Enclosures
SASE2 SASE1/3
Downstream View
 | SASE1/2 | SASE3
0 [mm] | 40 | 68
Operational Gap Range [mm] | 10-20 | 10-25
K-Range | 3.9–1.65 | 9.3-4
Radiation Wavelength Range [nm] |  | 
@ 17.5 GeV | 0.147-0.040 | 1.22-0.27
@ 14.0 GeV | 0.230-0.063 | 1.90-0.42
@ 8.5 GeV | 0.625-0.171 | 5.17-1.15
# of Segments | 35 | 21
System Length [m] | 213.5 | 128.1
WP71 Scope & Responsibility:
Organization , production either in house or through numerous IKCs & installation of the Undulator Systems

## Slide 4: WP71 Hardware Status November 2016
Dec 2014
Feb 2016
WP71 Status of Hardware Production
92 Undulator Segments produced, tuned & commissioned
92 Undulator Segments for SASE1-SASE3 re-measured
56 undulator segments for SASE1+3 installed, 35 for SASE2 RFI
100 Pillars, Granite Bases for SASE1-3 installed
96 Phase Shifters in house; 56 (SASE1+3) installed, rest RFI
91 Quadrupole Movers (CIEMAT IKC) 56 (SASE1-3) installed
91 Intersection Control Racks (CIEMAT IKC) SASE1-3 installed
200 Air Coils, produced, tested, RFI
Air Condition: SASE1 operational, SASE3 in commissioning, SASE2 March 2017
Contributions from Accelerator Consortium
XQA Quadrupoles
Cavity BPMs , DESY WP17, PSI; 97 RFI; 60 SASE1+3 installed, Rest RFI
BLMs, DESY WP17, IHEP Protvino; 97 RFI; 60 SASE1+3 installed, Rest RFI
Vacuum Supports SASE1-3 installed
Intersection Vacuum, DESY WP19, BINP 60 installed SASE1+3 installed, Rest RFI
Undulator Vacuum Chambers, DESY WP19: 62 SASE1+3 installed, Rest RFI
Oct 2016
Hall 36
Message:
All WP71 Hardware is either installed or Ready for Installation (RFI)

## Slide 5: Undulators: Representative magnetic Results: U40-X046
XFEL Specs | U40 | U68
Operational Gap Range [mm] | 10-20 | 10-25
B0 @ 10mm Gap [T] | 1.14 | 1.66
K @ 10mm Gap | 3.9 | 9.0
RMS I2Y [Tmm2] | < 100 | < 210
RMS I2Z [Tmm2] | < 100 | < 100
Phase Jitter [°] | ≤ 8 | ≤ 8
Documentation Data Base in EDMS
Drawings
Tender Material
Production data of all WP71 components
Acceptance Tests
Magnetic data of all Undulator Segments, Phase Shifters, Air Coils
Installation

## Slide 6: Re-Measurement Campaign
Reasons:
  60% of the Undulator Segments were stored outside up to 2 ½ years with no temperature control (8-30°C) Check prior to installation requested!
  Improve accuracy of Hall Probe measurements to K/K =2 x 10-4 using new high stability, low drift, low noise probes (SENIS H3A-0YJ02F-B02T0K5K)
  Apply exactly the same specs and procedures to all segments.
  Precision Air Coil settings for Entrance/Exit Kicks using the Long Moving Wire Method rather than Hall Probes.
Message: Accuracy Limit, K/K ≤ ±2.0x10-4 during the whole re-measurement campaign Fall 2014 – September 2016
Results:
Only minor changes observed (entrance/exit kicks)
Phase Jitter, straightness unchanged
Probe data are much more stable

## Slide 7: Precision Measurement of Entrance &Exit Kick using the Moving Wire
D. Zangrando, R.P. Walker, Nucl. Instr. And Meth, A376 (1996), 275
Undulator
Air coil
Moveable stages
0.1mmØ CuBe Wire
Results on U40-X001, X042, X057
Paralell “P“
Anti-Paralell “A“
Accuracy: I1≤±5μTm; I2≤±20 μTm2;
For Comparison: 1μm ^ 68 μTm2
F. Wolff-Fabris
1st Field Integrals
2nd Field Integrals

## Slide 8: Global Orbit Control in Undulator Systems
Corrector & BPMs Positions
Without
With MW
6.1m
Orbit inside each Undulator segment is straight within specs  Accuracy of Hall probe sufficient
Hall measurements insufficient for End Corrector (Air Coils) setting
Long Moving wire measurements provide accurate data for a straight global orbit

## Slide 9: Phase Shifters with very low 1st Field Intergral errors: Representative Results
Horizontal 1st Field Integral
Vertical 1st Field Integral
Period length: 55mm
Gap range: 10.5 to >100mm
Max. Phase Integral @ gap 10.5mm : 23400 T2mm3
1st Hor/Ver Field Integral
Tolerance: ±0.004 Tmm
Dynamic Operation without retuning!
2nd Hor/Ver Field Integral Tolerance: ±67 Tmm2
Min. Gap precision for 5° SASE1/2 ±15µm
1st Field Integrals: Important for independent operation,
no corrections required (31 Phase Shifters , Huihua Lu, Lingling Gong, Yajun Sun, IHEP)
Phase Integrals: Adjust Phase delay
Y. Li, J. Pflueger, Phys. Rev. STAB 18, 030703 (2015)

## Slide 10: Control System Architecture
Undulator Cell #1
Central Control Node
Machine Control
DOOCS client
Experiment Control
DOOCS client
Ethernet
DOOCS server
TwinCAT System Manager
EtherCAT
Axes and parameters that are coupled to a virtual axis
4 undulator axes
2 quadrupole
mover axes
1 phase shiftrer axis
4 air coil correctors
AMFC
3-way valve
Front-end
Middle Layer
Client Layer
Beckhoff Programmable Logic Controller (PLC)
Local Drive
Motion
Control of
undulator
cell #1
Virtual axis #1; 2 QM axes; PS axis; AMFC; 3-way valve; ACC
Undulator Cell #N
Axes and parameters that are coupled to a virtual axis
4 undulator axes
2 quadrupole
mover axes
1 phase shiftrer axis
4 air coil correctors
AMFC
3-way valve
Local Drive
Motion
Control of
undulator
cell #N
Virtual axis #N; 2 QM axes; PS axis; AMFC; 3-way valve; ACC
…
…
LCN in SASE1
CCN in Balcony
Room in XHEXP
x 35
Based on industrial Beckhoff Hardware using TwinCAT Software and fast EtherCAT Fieldbus
S. Karabekyan
x 1

## Slide 11: Main user interface (S. Abeghyan)

## Slide 12
Undulator Control
Phase Shifter Control
Quadrupole Mover Control
Air Coil Control
S. Abeghyan

## Slide 13: Undulator Control System: Properties
Local Control Node (LCN); Controls an individual cell
  Synchronization of Gap-Motors, Operational Safety, Phase Shifters, Quadrupole Movers, Synchronization with Air Coils, Phase Shifters, Vacuum Chamber Temperature Control, Temperature Monitoring
  Well tested during magnetic measurements
S. Karabekyan, S. Abeghyan, M. Yakopov
Central Control Node (CCN); Controls all cells of a SASE System :
  Based on TwinCAT
  Controls 35/21 LCNs using redundant ring architecture with optical fibers, length 2km
  Manages/archives Hardware specific data: Lookup tables, operational parameters, offset bias values
  Centralized data storage in Oracle Database, Backups
  Automated procedures
    IDA (Image Deployment Automation): Software Version control, updates, parameter uploads.
    Functional tests of Hard/Software
  Interface with DOOCS: Control of all system properties
  CCN of SASE1 + SASE3 fully operational and under remote control
  User Interface with JDDD (Java Doocs Data Display)
  Future upgrades: Global synchronization of all undulators (Lasing on the Fly, synchronization with monochromators)  Make full use of hardware capabilities – Only new software needed.

## Slide 14: Temperature Distribution in SASE1 System measured Sep.3 – Oct. 3 (Holidays)
Temperature along SASE 1
Time Dependence at Cells 3, 19,37
SASE1 PKG
e-
Air

## Slide 15: Phase Matching --- Look up table for Und & PS
Complex On-Axis vector potential
from magnetic measurements:
U40-X005 PS073 U40-X006
Und, 2
Und, 1
Y. Li
Pairing Needed for Undulator Phase Shifter combination  Lookup Table in control system
Phase Shifter Gap vs. Undulator K
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 16: SPECTRA results using measured field data
Phase Matching: On axis intensity from two Undulators is 4 times that of one.
Rough K Estimate:
All six undulators within this limit
Y. Li
Message: Undulators behave perfect, Phase Matching works

## Slide 17: SASE1 Status & Plans November 2016
Status
Undulator Hardware installed, including XQAs, Magnet Power, Cooling Water, QMs, Phase Shifters,
Undulator Control System commissioned, operational
Interlock installed
Air Conditioning System installed & commissioned
SLRS installed & commissioned
Plan
Re-alignment of Undulator System using SLRS: Total 6 weeks End: Dec 9
Commissioning of 35 Undulator Segments: Removal of Safety covers, Safety Precautions
Fine alignment of the vacuum chambers, closing the gap to 10.000mm, Fine adjustment of limit switches, CALs, Hardstop, Installation of Radfets, Air Coils: 8 weeks; End: Feb 8, 2017
Ready For Beam: Beginning of February 2017
Enclosure closed
Sep 2016
Re-opened for SLRS alignment 22.10.2016

## Slide 18: SASE3 Status & Plans November 2016
Status
Undulator Hardware installed, including XQAs, Magnet Power, Cooling Water, QMs, Phase Shifters,
Undulator Control System commissioned, operational
Air Conditioning System installed, commissioning in progress
Interlock not yet installed
SLRS in installation
Enclosure closed
Plan
Commissioning of SLRS
Re-alignment of Undulator System using SLRS: Total 6 weeks End: Jan 31, 2017
Commissioning of 35 Undulator Segments: Removal of Safety covers, Safety Precautions:
Fine alignment of the vacuum chambers, closing the gap to 10.000mm, Fine adjustment of limit switches, CALs, Hardstop, Installation of Radfets, Air Coils: 8 weeks; End: March 21,, 2017
Ready For Beam: End of March 2017

## Slide 19: SASE2 Status & Plans November 2016
Status
SASE2 has low priority
Pillars, Granites, Floor Mounts installed
Air Conditioning: Enclosure + Unit installed
25 out of 35 undulator control units installed
Posts and adjustors for vacuum system installed
QMs and XQAs mounted
Plan
Instal & align vacuum system, BPMs, BLMs undulator chambers : Pre-Condition: Baustromversorgung needs to be removed first
SLRS installation and commissioning
Installation/Completion of Infrastructure (Interlock, cooling water, magnet power)
Phase Shifter Installation(1 week)
Undulator Installation (3 weeks)
Cabling and connecting of 35 cells, first commissioning of undulator controls (3 weeks)
Final alignment using SLRS (3 weeks)
Install panels for Air Conditioning Enclosure (3weeks)
Commissioning of Air Conditioning System (2 weeks)
Commissioning of Undulator System guarantee safe operation for Gap 10.000mm (8weeks)
Ready For Beam: June 2017
SASE2 26.10.2016

## Slide 20
The End