## Slide 1
High-resolution tracking and timing based on HADES scCVD diamond sensors for detector tests - test of PADI for straw tube readout
J. Pietraszkoa, T. Galatyuk b, W. Koeniga, M. Trägera, M. Kisa, C.J.Schmidta
a GSI Helmholtz Centre for Heavy Ion Research GmbH Planckstrasse 1, D-64291 Darmstadt, GERMANY
b Technische Universität Darmstadt, Darmstadt, Germany
Outline
A short introduction to the HADES experiment
ScCVD diamond detectors used for MIPs in HADES
Performance of a segmented scCVD diamond utilized as a reference detector
in a straw tube test setup

## Slide 2
Geometrical acceptance: 2π in φ; 18 0 < θ < 85 0
Di-electron pair acceptance  35 %
low mass spectrometer
─ RICH: X/X0 < 1%
─ MDC: X/X0 ≈ 0.42%
  M()  2.0%
  Systematic di-electron and strangeness measurements in heavy ion, proton and pion induced reactions. Beams from SIS18 and SIS100 at FAIR (GSI Darmstadt, Germany)
Experimental apparatus: HADES (The High-Acceptance Di-Electron Spectrometer)
p(3.5 GeV) + p
/M≈2%
Eur.Phys.J. A48 (2012) 64
e+e–
Diamond T0 detector
Notes: 2

## Slide 3
scCVD diamond start detector for MIPs
The key features:
4.5 mm x 4.5 mm x 0.3 mm scCVD high purity diamond material
Thickness of 300 µm , low Z
In vacuum operation, without cooling, noise free ...
Superposition of about 50 waveforms
Jülich (COSY), p@2.95 GeV
single plate of scCVD diamond
 excellent ADC capabilities and S/N ratio
Diamond T0 detector for pion beam – active area 1.2 cm x 1.2 cm
Notes: 3
nucleus

## Slide 4
Aim of the test: can the PADI chip be used for straw tube readout ?
PADI6 ASIC for straw tube readout
(M. Ciobanu, m.ciobanu @ gsi.de)
4 channel per ASIC, differential inputs 8 channel on FEET-PADI6_Hda
conversion gain: 35(17.5*)mV/fC
voltage gain: 244
BW: 416MHz
time constant in setup: ~20ns
Straw tube detector
CBM MUCH prototype 6mm diameter, ~22cm length
detector gas: Ar/CO2 (70/30)
gas pressure: 1bar
HV: 1800V
AC coupling to PADI input: 400pF(straw), 2.2nF(PCB)
Needed a reference detector:
Position resolution below 50 µm
Time resolution better 100 ps
Single particle mode for MIPs
scCVD diamond utilized as a reference detector

## Slide 5
Experimental setup – reference detector
Reference, tracking, scCVD detector
four channels – metallization
100µm space between electrodes
time resolution below 100 ps
scCVD diamond signal for MIPs
Used threshold: 7mV on each channel
AND condition between 2 channels
 position resolution better than 50µm
100 µm
4.3 mm
4.3 mm
 ≈ 90 ps
p@ 2.95 GeV

## Slide 6
Experimental setup
Reference, tracking, scCVD detector
Four channels – metallization
100µm space between electrodes
Time resolution below 100 ps
Attached to a movable table,
(µm step precision)
p beam
Straw tubes,
Φ = 6mm
scCVD diamond
100 µm
DAQ /Trigger:
Oscilloscope used as a DAQ (R&S 1044)
Correlated signal in two diamond electrodes used as a trigger
Trigger: protons in the 100µm gap between electrodes.
Straw tubes connected to the PADI v6
Straw diameter: 6 mm
Ar/CO2: 70%/30%
HV: 1800 V
www.tinkercad.com
4.3 mm
4.3 mm
beam pipe
p@2.95GeV
Straw tubes
Diamond detector

## Slide 7
Experimental setup
p beam
Real beam spot – Jülich beam time
www.tinkercad.com
p beam
Straw tubes,
Φ = 6mm
scCVD diamond
www.tinkercad.com
beam pipe
p@2.95GeV
Straw tubes, Φ=6 mm
scCVD diamond detector
mounted on movable table (±1µm)

## Slide 8
Drift time measurement
+0.0mm
+0.5mm
+1.0mm
+1.5mm
+2.0mm
Time difference between the scCVD diamond detector
and Straw Signal from the PADI discriminator.
 Drift time spectra (example for 5 positions)
www.tinkercad.com
Straw tube
beam particles

## Slide 9
Drift velocity estimation

## Slide 10
Summary
Simple, segmented scCVD diamond with precise timing and positioning of MIPs
  Rate capability up to 10 7 particles / s
  Time precision < 100 ps (sigma) for both MIPs and HI
  Position information better then 50 µm, can be improved by increasing the bias voltage
  Simple construction and robust device
  Powerful device for detector tests – timing and tracking

## Slide 11
Thank you