## Slide 1: DAΦNE BTF improvements of the transverse beam diagnostics
Bruno Buonomo1, Luca Foggetta1, Claudio Di Giulio1, Paolo Valente2
1 INFN Laboratori Nazionali di Frascati
2 INFN Sezione di Roma
http://www.lnf.infn.it/acceleratori/btf/

## Slide 2: BTF in the DAΦNE
The BTF (Beam Test Facility) is part of the DAΦNE accelerator complex:
it is composed of a transfer line driven by a pulsed magnet allowing the diversion of electrons or positrons

## Slide 3: LINAC
TITAN Beta (Ca,USA) 1995
S band LINear ACcelerator ~60 m long
Termoionic gun, 4x45 MW klystrons SLED 15 waveguide 2/3π SLAC type section 3m long.
 | Design | Operational
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
RF frequency | 2856 MHz | 
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 1 to 50 Hz | 1 to 50 Hz
Beam macropulse length | 10 nsec | 1.4 to 40 nsec
Gun current | 8 A | 8 A
Beam spot on positron converter | 1 mm | 1 mm
norm. Emittance (mm. mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
electron current on positron converter | 5 A | 5.2 A
Max output electron current | >150 mA | 500 mA
Max output positron current | 36 mA | 85 mA
Trasport efficiency from capture section to linac end | 90% | 90%
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4 x 45 MWp sledded klystrons TH2128C | 
Upgrade pulse width: ~ 150 ns

## Slide 4
e-/e+
Linac
Energy [MeV]
1010
510
#
∫∫
The primary beam collide ≈2x0, Cu produce a secondary beam
Sim. 108
BTF
Exp. Hall
How the BTF works:

## Slide 5: The Beam-Test Facility
  The users in BTF are able to know in real time the beam parameter (type of particle, energy, intensity, dimension and position).
  They have the accelerator complex services available for their setup: power supply, network, gas, DAQ, Vacuum staff, cryogenic.
Usually BTF works in parasitic way respect to DAFNE collider.
Parametri | Parasitic |  | Dedicated | 
 | With Cu target | Without Cu target | With Cu target | Without Cu target
Particle | e+ or e- (User ) | e+ or e- (Dafne status) | e+ or e- (User ) | 
Energy (MeV) | 30–500 | 510 | 25–700 (e-/e+) | 250–730 (e-) 250–530 (e+)
Energy Resolution | 1% at 500 MeV | 0.5% | 0.5% | 
Repetition rate (Hz) | Variable from 10 to 49 (DAFNE status) |  | 1–49 (User) | 
Pulse lenght (ns) | 10 |  | 1.5–40 (150) (User) | 
Intensity (particle/bunch) | 1–105 (Energy dependence) | 107–1.5 1010 | 1–105 Energy dependence | 103–3 1010
Max # of partic. | 3.125 1010 part./s |  |  | 
Beam size σ(mm) | 0.5–25 (y) × 0.6–55 (x) |  |  | 
Divergence (mrad) | 1–1.5 |  |  | 

## Slide 6: BTF products:
e-
e+
γ
E
n
Electron o positron:
  Single particle
  High Intensity
“Tagged” photon
Neutrons
BTF

## Slide 7: BTF: Low Intensity
Secondary beam
2cm2 MEDIPIX
Energy spread mesured by(LYSO Calorimeter)
[Mambo BGO]
Single particle
Primary beam attenuated by a Copper target
Energy of Secondary beam from 500 up to 30MeV
The multiplicity follow the Poisson distribution and user can select the mean value.
Positron and electrons independent from the primary beam.
Best beam
(σx x σy):
440x420μm2
Transverse beam monitoring

## Slide 8: Transverse Monitoring
FITPIX Kit Detectors: sensors have a square pixel of 55 µm side in a 256×256 pixels (overall side length 1.4 mm) layout
for a square sensitive
area of about 2 cm²
and 300 µm of
Thickness.
Programming solutions:
starting with the python scripting capability of the provided software kit;
low-level programming, which required some interaction with ADVACAM® for a full exploitation of the Linux libraries;

## Slide 9: Transverse Monitoring Data Access
User
Expermental
DAQ
access to live data at the maximum frame-rate within the BTF duty cycle.
software architecture with a typical producer-consumers layout.
data caching on MEMCACHED server, to allow more than one different consumers at the same time.
Cross Check Multiplicity with calorimeter or user detectors.

## Slide 10: Low-Level programming
Develop of three possible data structures:
Array, sparse, ultra sparse mode
All of these cases are headed by the following values:
Case and FitPIX configuration identifier;
Time tag (resolution 0.1 ms);
number of fired pixel;
frame number;
Callback
frame by frame
on dev interrupt N

## Slide 11: Transverse Monitoring
Consumer Code in LabView allow:
Beam spot bunch per bunch
Cumulative spot image
Multiplicity distribution from FitPIX.
Multiplicity vs time

## Slide 12: Transverse Monitoring
Bunch position vs time
Consumer Code in LabView allow:
Beam position monitoring bunch per bunch
Beam size monitoring bunch per bunch.

## Slide 13: Transverse Monitoring
Consumer Code in C++ allow:
Root Data Files
  (UTC time, pix, count, frame)
Cross Check with User detectors
Client code available for the users by svn.
Bunch X position [mm]
(UTC time – ref. Time) [s]
e- for Dafne
(UTC time – ref. Time) [s]
Bunch X position [mm]
20 ms -> 50Hz
40 ms:
Bunch in the spectrometer transfer line.

## Slide 14: Low-Level programming
The software architecture is tested for:
GEMPIX
Multiple FITPIX
Tracker with 2 FitPIX
A consumer software rejection function senses a single event jitter delay of 5ms (the minimum time-tag difference between two synchronized FitPIX MC keys) after 100000 calls, mainly due to producer thread time jitter.
This guarantees a complete software data alignment within the user DAQ cycle, even for the data coming for two FitPIX devices in the BTF typical tracking setup

## Slide 15: Conclusions
The transverse monitoring bunch per bunch allow a more precise beam characterization.
BTF Users requires precise beam information to test their devices to reduce the uncertainty in their measurements and reducing the time-to-problem solution during their tests.
BTF staff will follow to develop the improvements following the requirements identified by the user.

## Slide 16: BTF: Single particle
Cu 2X0 target
< 4 mrad
Maximum input divergence:
Energy resolution:
d≈0.25 mm
D=60 mm
Out of target
10-1
10-3
10-5
10-7
10-7
10-6
10-5
10-8
10-7
10-6
10-5
10-8
1 (E0)
0.8
0.6
0.4
0.2
0
1 (E0)
0.8
0.6
0.4
0.2
0
1 (E0)
0.8
0.6
0.4
0.2
0
Target
Energy spread misurato
(Calorimetro LYSO)

## Slide 17: Timing
DAFNE reference Ø4 for the injection systems
Conditioned Ø4 -> DELAYED LINAC SYS SIGNAL moves all the LINAC stuff together to match ACCUMULATOR phase)
  DELAYED GUN SIGNAL -> LINAC SYS REFERENCE (once optimized, not moved for months)
  BTF REFERENCE -> USER needs DELAYED LINAC SYS
  → WE ARE WORKING in STATIC LINAC+BTF TRIGGERING SCHEME
Some Jitter contribution (see also AMY and UA9 experiences)
LINAC SYS reference jitter (rms, 10ps, our best measure)
LINAC GUN jitter (100ps)
BTF STANFORD DDG535m single channel jitter (rms, 60ps + 0.01ppm of the channel delay) .

## Slide 18: n@BTF
At 1.5 m distance:
Total neutron flux: 8×10-7 n/cm2/pr ±3%
Flux = 4.5×105 n/cm2/s @ full beam
Equivalente dose = 45 mSv/h
d (m) | ×10-7 n/cm2/pr
0.5 | 58
1 | 15
1.5 | 8
d (m) | ×10-5 g/cm2/pr
0.5 | 63
1 | 5.7
1.5 | 1
At 1.5 m distance
Total photon flux = 1×106 g/cm2/s
With 1.1×1011 n in the target:
8.8×108 n/cm2/s exiting from the target
1.87×1010 g/cm2/s exiting from the target

## Slide 19: Neutron electro-production
Evaporation peak + fast neutrons shoulder
Tungsten target
At full linac power: 1013 e/s
  to be compared e.g. with nELBE, N=6·1015 e/s
Swanson estimate
  9.3·1010 Z(0.73±0.05) n/s kW-1
  2.15 ·1012 n/s kW-1 for Tungsten
Optimizing the target configuration can (slightly) improve the yield:
  n@BTF optimized target: 2.75 ·1012 n/s kW-1
  0.218 n/pr (over 4p and all spectrum)
In our case the main limitation will always be the intensity delivered onto the target