## Slide 1: Update: Analogue daughterboard and ABCN’ 25 October 2016
J. J. John and T. Huffman
with help from many colleagues

## Slide 2
CHESS-2-AMS analogue daughterboard
Arrived – 100 daughterboards.
Since then, have been preparing for irradiation at PS (see later).
Many thanks to Paul Booker and
everyone at RAL for
wire-bonding these.
edge connector taped to short together all pads during proton irradiation

## Slide 3
Final specs for analogue daughterboard
pads for passive devices
disable top and middle arrays
bottom array: disable readout but enable SACI
It was not feasible to include 320 MHz readout of bottom array, in the end.
test array: configure and read out
dual capacitor footprints:
wire-bondable on front, conventional on back
6 layers

## Slide 4
Irradiation at PS this week (starting Weds)
24 boards in all:
Daughterboard serial numbers | Wafer | Resistivity (Ω-cm) | Target dose
1 - 5 | w 1-2 | standard | 0.5 x 1015 n eq/cm2
6 - 10 | w 1-2 | standard | 1 x 1015 n eq/cm2
11- 15 | w 13-14 | 200-300 | 0.5 x 1015 n eq/cm2
16-20 | w 13-14 | 200-300 | 1 x 1015 n eq/cm2
21 - 22 | w 19-20 | 600-2000 | 0.5 x 1015 n eq/cm2
23 - 24 | w 19-20 | 600-2000 | 1 x 1015 n eq/cm2
Boards mounted on cards and packed
mounted on standard CERN cards
Thanks to Roy Wastie for preparing the cards.
beam centred as discussed:

## Slide 5
Next steps for analogue work
Motherboards will need 1 IC changing (voltage reference, to be able to produce 3.6V from DACs).
    I am ordering these ICs for all institutes with CHESS-1 motherboards.
Ship analogue daughterboards and these ICs to institutes who requested analogue daughterboards.
        Will reconfirm people’s requests shortly.
Modify CHESS-1 motherboard, document steps -> TWiki
Add bonding diagrams and other documents -> TWiki
Update Atlys firmware for CHESS-2 including SACI – merge from UBC’s SACI code for ABCN’
Characterise

## Slide 6
ABCN’ update
1) Data path:
UBC (Vancouver) have successfully completed the data path of the ABCN’
Tested via an FMC loopback cable on the Nexys Video FPGA board:
Emulated CHESS-2 data out of FPGA, across FMC loopback, back into FPGA, handled by ABCN’, read out by SCTDAQ software.
2) Next steps:
UBC is currently working on SACI code to talk to CHESS-2

## Slide 7
CHESS-2 to FMC adaptor board
Status: design completed after many checks.
UBC is ordering 20 boards. Planning to assemble 10 boards to start.
ETA of boards ~2 weeks, then assembly.
Key features:
Connects a CHESS-2 digital d/b to the Nexys Video via FMC connector
Allows the Nexys Video to read 1 of 3 strip arrays
Provides voltage supplies, HV connection and external bias DACs
FMC connector wired so that the other 2 strip arrays are connected to the High Pin Count pins
  Could be connected to various high pin count FMC evaluation boards if need be.
Daughterboard connector
FMC connector
regulators
and bias DAC
mounting holes
HV
4mm sockets
LV
ground
Adaptor board sketch:

## Slide 8
Things that happen along the way
The La Poste envelope reads: "customer service - doing everything so that your post arrives, no matter what happens."