Alignment with beam halo tracks
Andrea Parenti (DESY)
CMS Hamburg/DESY Meeting
03/06/2009

---
The CMS tracker
In this talk I will focus on alignment of the endcaps: TEC & TID
Tracker Endcaps:
9 disks, 4-7 rings
Tracker Inner Disks:
3 disks, 3 rings

---
Track based alignment: samples
High pT muons (Z, W decays):
  - small multiple scattering
  - will become available after collisions start
Cosmic muons:
  - already available
  - ok for barrel, not very useful for endcaps
Minimum bias:
  - high-rate, available since first collisions
Beam Halo muons:
  - already available with single beams, high-rate
  - useful for end-caps (~ horizontal tracks)
...

---
Beam Halo (BH) events
Simulation of a beam halo event in CMS detector:
The event contains a muon plus low momentum hadrons
We must apply cleaning cuts to select good tracks
A beam halo event, with no hadrons simulated

---
Alignment with beam halo
Based on 60k beam halo Monte Carlo events
  - larger sample will be available soon
After requirements on minimum # of hits and chi2 of track fit, 30k good tracks are left for the endcap alignment
Due to the small number of usable tracks, only alignment of high-level structures has been studies
  - TID rings:	18 subdetectors x 3 parameters
  - TEC disks:	14 subdetectors x 3 parameters (2 disks are fixed to avoid global displacements or deformations)
An initial misalignment is applied (in the so-called 10pb scenario)
  - TID rings:	185 mm (u,v),	850	mrad (g)
  - TEC disks:	70 mm (u,v),	30 mrad (g)

---
Alignment with BH + Minimum Bias
Also Minimum Bias (MB) events will be abundant since the beginning
Expected similar rate as Beam Halo... using 175k events
Tighter track selection (pT>1.5 GeV, # of track hits)
After that, # of selected tracks: 300k (10x beam halo tracks)
Selected tracks are then used to evaluate alignment parameters

---
Alignment: TEC results
Minimum bias tracks only
u/v/g residuals after realignment:
Min. Bias + Beam Halo
<Du> = 2 mm
<Dv> = 10 mm
<Dg> = 4 mrad
<Du> = 9 mm
<Dv> = 11 mm
<Dg> = 30 mrad

---
Alignment: TID results
Minimum bias tracks only
u/v/g residuals after realignment:
Min. Bias + Beam Halo
<Du> = 13 mm
<Dv> = 13 mm
<Dg> = 140 mrad
<Du> = 7 mm
<Dv> = 2 mm
<Dg> = 13 mrad

---
Comparison of the results
TID: BH+MB results are much better than BH and MB only (especially for angular parameter)
TEC: results are dominated by BH but anyway the angular parameter benefits from combination with MB

---
Conclusions
A study of the alignment of high-level structures in the tracker endcap has been done with MC events.
Minimum bias and beam halo have been used (mixed according to the expected rate).
Beam Halo events improve a lot alignment of endcaps with respect to minimum bias only.
Now waiting for bigger BH MC sample in order to study effect on smaller-level structures

---
Backup Slides

---
Alignment Parameters

---
Initial geometry and parameters
Alignment is done of High level structures: 'TIDRingsLayers13,110001', 'TrackerTECDiskLayers11,cc000c', 'TrackerTECDiskLayers24,110001', 'TrackerTECDiskLayers55,cc000c', 'TrackerTECDiskLayers69,110001'
Start from ideal geometry + custom misalignent
  - TIDRings & TECDisks as in 10pbScenario
    - TIDRings:	185 mm (u,v),	850	mrad (g)
    - TECDisks:	70 mm (u,v),	30 mrad (g)
  - no misalignment applied on smaller structures, and on the barrel sub-detectors

---
Alignment with beam halo
Based on 20X beam halo Monte Carlo
  - the available statistics is limited: ~60k events
Track collection: ALCARECOTkAlBeamHalo
Track selection:
  - ptMin = 0.
  - etaMin = -999.	/ etaMax = +999.
  - nHitMin = 6	/ nHitMin2D = 2
  - chi2nMax = 50.
  - minMultiplicity = 1
Nb. of selected tracks: ~31200

---
Alignment with BH: TEC results
Initial and remaining misalignment:
Correlation of remaining and initial misalignment:

---
Alignment with BH: TID results

---
Alignment with Minimum Bias
Based on 20X Monte Carlo
  - expected similar rate as Beam Halo... using 175k events from CSA08 MC
Track collection: ALCARECOTkAlMinBias
Track selection:
  - ptMin = 1.5
  - etaMin = -10.	/ etaMax = +10.
  - nHitMin = 8	/ nHitMin2D = 2
  - chi2nMax = 50.
  - minMultiplicity = 1
Nb. of selected tracks: ~302200 (10x beam halo tracks)

---
Alignment with MB: TEC results

---
Alignment with MB: TID results