## Slide 1: Chess2 measurements

## Slide 2: Status
-CHESS2 amplifiers don’t seem to produce an output pulse.
-CHESS2 amplifier are internally and externally biased.
IFB
1.8
3.3
InSF
Injection
In
Casc
Load
Comp
Th
1/2/4/8
RowENB
ColENB
RAMWrEn
Baseline

## Slide 3: Chess2 internal bias
- Chess2 uses internal current source to control all 4096 pixels of an array.
Prog. res. 4 values
current
out
Current attenuator
32 steps of 2dB.
to cells

## Slide 4
Cuurent (A)
7bit adjustable
Logarithmic behavior
desirable for feedback
current adjustment
Here 0 current.

## Slide 5: Status
- CHESS2 on the Oxford motherboard seems to be running hot.
- Motherboard only current = 0.149mA
- Function implemented that turns off:
  Amplifier
  Comparator
  DACs
- We should see current on the motherboard ~ 0.149mA
- We measure 0.462mA ???

## Slide 6: Thermal imaging of CHESS2

## Slide 8
vdd pad of bottom array was grounded

## Slide 9
vdd pad of bottom array was grounded

## Slide 10: Status
- Done late last night – didn’t want to try pulling the wirebong
- Forest we will pull the wire and make sure the hot spot disappears

## Slide 11: Further investigation
- The SLAC chip seems to be running hot too. We will look at it with the IR cam as well.
- Before this finding I had measured completely the current of the amplifier iN.
- Every other current source was shut off
IFB
1.8
3.3
InSF
Injection
In
Casc
Load
Comp
Th
1/2/4/8
RowENB
ColENB
RAMWrEn
Baseline

## Slide 12: Bias current measurement
- In the test array (the one that we are looking at on the Oxford setup) the 512 test pixel bias is shared with the bottom array.
- We have 4096 + 512 – 4608 times the current.

## Slide 13: Measurement results

## Slide 14: In log scale

## Slide 15: About the current
- The current source is not temperature compensated.
- With more heat than expected in the chip we are underbiasing the amplifiers.
- Will remove hot spot
- Put some cooling capabilities on the back side of the chip to control precisely the temperature.
- More test results to come.

## Slide 16: More information
- There is indeed an error in the CHESS2 datasheet about the amount of charge injected.
- Comparison of the big arrays of nwells between Chess1 and Chess2 (For Igor):
 | Chess1 | Chess2
Nwell width | 24.3u | 24.3u
Nwell length | 148.175u | 90.2u
Individual Nwell area | 148.175ux24.3u | 90.2ux24.3u
Number of rows | 44 | 32
Number of columns | 10 | 12
Total Nwell area | 1.58mm2 | 0.84mm2
Total big array size | 1.985mm x 2.029mm | 1.283mm x 1.263mm