## Slide 1: Novel X-band TDS at SINBAD
Daniel Marx
Diagnostics Mini-Seminar
DESY, 27 March 2017

## Slide 2: A new design
Give bunch time-dependent kick => convert longitudinal to transverse
High frequency ~12 GHz (X-band) allows 3-4 times higher resolution than S-band
Variable polarization allows deflection at any angle
Fig. Credits: D. Malyutin PhD thesis

## Slide 3: Outline
The technology
Who’s involved?
Applications at SINBAD

## Slide 4: New RF technology
Phase difference between port 1 and port 2:
0 degree -> vertical polarization
180 degree -> horizontal polarization
Courtesy of A. Grudiev
A. Grudiev, CLIC-note-1067 (2016).
Variable Polarization Circular TE11 Mode Launcher
Very precise azimuthal symmetry required!
 Tuning free assembly procedure at PSI
Notes: Rotator combines two radially polarized modes and produces one linearly polarized mode with direction depending on phase difference between the two input modes.

## Slide 5: Who’s involved?
Ongoing efforts towards an international collaboration to build and test the first prototype
Collaboration
  FLASH2: measurement of the energy spread induced by FEL lasing
  FLASHForward: characterization of driver and witness electron beams in PWFA
  SINBAD: characterization of ultra-short (fs / sub-fs) electron bunches for injection on novel high gradient acceleration techniques
  SwissFEL
  Potentially also XFEL

## Slide 6: SINBAD-ARES linac
ARES linac
Magnetic compressor
Dogleg to second experimental area
TDS + diagnostics beamline and experimental area
E=100MeV
Temporary experimental area
Space for future possible energy upgrade
SINBAD overview –
Cfr: U. Dorda et al. “SINBAD – The accelerator R&D facility under construction at DESY”, NIM A 829, p. 233-236 (2016).
Planned delivery: 2019

## Slide 7: Possible Measurements
Bunch Length
2D charge density profile in one plane
3D charge density profile using tomographic reconstruction (real space)
Slice emittance measurement (transverse phase space)
Energy measurement using dipole (longitudinal phase space)
6D phase space reconstruction

## Slide 8: Production and measurement of ultra-short probe for LWPA (1/2)
Beam shape at the TDS
Q=2.7 pC
Energy = 100 MeV
Transverse Normalized Emittance = 0.2 mm mrad
σt=0.461 fs

## Slide 9: Production and measurement of ultra-short probe for LWPA (2/2)
Beam parameters at the TDS
Simulated Measured Streaked Beam @ Screen
V = 40MV
β(s0) = 6m (as from bunch compression)
Δφ = π/2
Beam optics between TDS and screen
t [fs]
Longitudinal Resolution = 0.42 fs
Calibration done at reduced voltage
Jitter effects non included
Code used: Elegant (Space Charge OFF)
x [mm]
Notes: S=560 (from calibration ….)
σt=0.461fs
St calculated 0.464fs
(resol 0.42 fs)
Assumptions:
No jitter
Screen resolution:
…..

## Slide 10: Tomographic reconstruction
Aim: to reconstruct the 3D charge density distribution
Relies on streaking at multiple angles => completely new measurement
Principle:
  Streak beam at different angles and measure intensity at screen
  Slice profiles in time
  Combine 1D profiles from different streaking directions to form a 2D transverse profile for each temporal slice
  Stack slices together to form complete 3D charge profile reconstruction

## Slide 11: Tomographic reconstruction
Beam parameters:
Lattice: TDS (two 0.8-metre cavities + 5-metre drift)
Four streaking angles:
No space charge
No jitter
No misalignments

## Slide 12: Tomographic reconstruction
Input beam used for test simulations at the TDS
Input beam production simulated by J. Zhu
Example of correlation x-z that we wish to detect

## Slide 13: Tomographic reconstruction
Four xy screen profiles [2D]
  Convert y to t and divide into slices (0.85 fs) [2D]
  For each slice, take projection on x axis [1D] and combine using tomographic reconstruction (SART algorithm) [2D]
  Stack slices [3D]

## Slide 14: Tomographic reconstruction
Actual
Reconstruction

## Slide 15: Tomographic reconstruction
Bunch length decreases with TDS off
Bunch length increases with TDS on
Slices don’t match up

## Slide 16: Induced Energy Spread
Panofsky-Wenzel Theorem:
  Transverse deflection only possible if there is a transverse gradient of the longitudinal electric field present
Relative momentum gain:
Ez present
C. Behrens and C. Gerth, DIPAC09. TUPB44

## Slide 17: Tomographic reconstruction
Further work:
  Test best possible case using matrix calculation
  Possibly investigate modes (how good is RFDF element in elegant)?
  Add space charge, timing jitter, misalignments…
  (Investigate using other reconstruction algorithms, e.g. MENT)

## Slide 18: Applications
SINBAD will provide short bunches for use as a witness beam in LWFA experiments and for testing dielectric structures
TDS will allow characterization of 3D charge density profile of input beam
Dielectric structures
  Inject asymmetric beams
  Characterizing beam important for matching & aperture considerations
LWFA experiments
  Plasma fields (and matching conditions) have longitudinal dependence in certain regimes
  Accelerating fields also influenced by beam offsets so charge profile can help, e.g. for beam loading
Could potentially use for testing beam output by taking many measurements for each streaking direction

## Slide 19: Summary
New X-band TDS being developed for use at DESY & PSI facilities
Allows streaking of bunch at all angles
Opens up possibility of doing a 3D charge profile reconstruction using tomographic techniques
Induced momentum spread is a problem
Further studies needed
Applications for LWFA and dielectric experiments
Conference submissions to IPAC’17 being prepared

## Slide 20: Acknowledgements
In addition, we are supported by colleagues from CERN & PSI, including:
A. Grudiev, W. Wuensch, N. Catalan Lasheras, G. Mcmonagle (CERN)
P. Craievich, M. Pedrozzi, H. Braun (PSI)
Present team working on application of X-band technology at DESY:
B. Marchetti (DESY coordinator), R. Aßmann, R. Bacher, B. Beutner, J. Branland, F. Christie, R. D‘Arcy, W. Decking, U. Dorda, B. Faatz, C. Gerth, J. Herrmann, M. Hoffmann, M. Hüning, G. Kube, O. Krebs, S. Lederer, F. Ludwig, F. Marutzky, D. Marx, J. Osterhoff, I. Peperkorn, J. Rothenburg, S. Pfeiffer, H. Schlarb, M. Scholz, S. Schreiber, J. Rönsch-Schulenburg, M. Vogt, A. Wagner, T. Wilksen, K. Wittenburg.

## Slide 21: Defining Shear Parameter, S
This is just ratio between transverse and longitudinal energy
Assuming TDS operated at zero-crossing
Defining matrix transformation between cavity and screen (TDS off)
-dependent vertical shift due to TDS
Definition of shear parameter

## Slide 22: Finding Shear Parameter, S
If we keep in our equation, we get:
.
Considering the bunch centre:
.
So can use gradient of vs. graph to determine .

## Slide 23: Resolution
When TDS is off ( is unnormalized emittance)
Transfer matrix element
Second equality is simply the result of using equations above and rearranging (equivalent to Eq. 10 of Emma et al. (2000)).
Using and , .
Longitudinal resolution,
RMS spot size on screen is due to nominal beam size plus TDS-induced beam size
This equation defines longitudinal resolution,

## Slide 24: Induced Energy Spread
Panofsky-Wenzel Theorem:
  Transverse deflection only possible if there is a transverse gradient of the longitudinal electric field present
Relative momentum gain:
Ez present