## Slide 1: Chess2 measurements

## Slide 2: Schematics
IFB
1.8
3.3
InSF
In
Casc
Load
Comp
Th
1/2/4/8
RowENB
ColENB
Baseline
3.3
Injection
3.6
Inj_EN
3.3

## Slide 3: Schematics – FIB points
IFB
1.8
3.3
InSF
In
Casc
Load
Comp
Th
1/2/4/8
RowENB
ColENB
Baseline
3.3
Injection
3.6
Inj_EN
3.3

## Slide 4
FIBing points on the pixel

## Slide 5: Charge injection behavior
Our pulser seems to emit ”chirps” when it is turned ON.
Our amplifiers seems to respond to these ”chirps”.

## Slide 6: Response of amplifier to pulser chirps

## Slide 7: Detail of amplifier to pulser chirps

## Slide 8: Summary
When we enable or disable our pulser it has a feature of sending chirps of high frequency ripples ~1ns period.
The amplifier responds to the high frequencies
Adding a DC – to 48MHz to the ouput of the pulser remove the behavior.
Will check is modifying the amplifer biases changes the behavior.

## Slide 9: Leakage current during injection setup
Pulser
CHESS2 motherboard
Keithley
HV
GND
Inj
Filtering DC- 48MHz doesn’t make a difference
Current measurement on Keithley with pulser ON

## Slide 10: Description of leakage current observed
Pulser high value: above ~2V
Effect observed with pulse height as low as 40mV (couldn’t go lower)
Pulse width from 1.6ns to 499ms
The effect is not observed with a DC power supply (e.g. Keithley)
The effect is observed even with a 48MHz filter on the pulser output
Leakage
No leakage
Leakage

## Slide 11: Summary
When using a pulser with a DC level higher than 2.0V we see an increase of current during the high phase of the pulse.
The value of this leakage current doesn’t change for pulse width between 1ns to 499ms. But doesn’t exist for a pure DC supply.
Will use an other pulser capable of lower repetition rate.
Will make a plot of the leakage current vs pulse amplitude.
Will see if the leakage current has a decay time and try to measure it.

## Slide 12: Separate observations
HV node on the motherboard is very sensitive to noise pickup.

## Slide 13: HV node noise
22kHz noise from pulser power supply

## Slide 14: HV noise
Turning off the pulser removes the pickup
Putting the pulser in a metal cage helps
Seems that having a grounded connector for HV supply on mother might help too.

## Slide 15: HV node noise
22kHz noise from pulser power supply

## Slide 16: Summary
Will try to modify the motherboard HV connector to reduce pickup loop present when using banana plug cables.