## Slide 1: CHESS-2-AMS encoding and data out 10 May 2016
P. Caragiulo, H. Grabas, J. J. John

## Slide 2
Outline
Reminder of how CHESS-2-AMS processes and encodes hits
How the Serializer works and the data out format of CHESS-2-AMS

## Slide 3
CHESS-2-AMS Architecture (reminder)
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
This is the block diagram for a single array (1 array out of the 3 in total)
Acquisition
Encoding
Configuration and Calibration
Read-out
Reminder, pixels are organised as:
128 strips, containing 32 pixels each
or 128 rows x 32 columns

## Slide 4
CHESS-2 Data Flow – 1/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
This is a basic reminder of the high-level data flow.
Later slides will review the details of the data format at each step.

## Slide 5
CHESS-2 Data Flow – 2/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
2) strip encoding represents the hits occurring on each strip

## Slide 6
CHESS-2 Data Flow – 3/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
2) strip encoding represents the hits occurring on each strip
3) hit encoding reduces the data to the first 8 hits among the 128 rows and identifies which strips were hit

## Slide 7
CHESS-2 Data Flow – 4/4
128 x 32
pixels
Column Decoder
Half Comparator,
Latch & Strip encoding
Hit Encoding
Row Decoder
SACI
Control Logic
Global Registers
Matrix
Pointers
Global DACs
LVDS TX/RX
Serializer
1) the pixels detect hits which are over a threshold
2) strip encoding represents the hits occurring on each strip
4) the hit encoding is serialized, then transmitted off-chip using LVDS
3) hit encoding reduces the data to the first 8 hits among the 128 rows and identifies which strips were hit

## Slide 8
hit
Strip encoding
hit
This first stage of encoding represents the state of each of the 128 strips (rows) as 7 bits in all:
The first hit in a strip appears as a 5-bit column address. First means the column with the lowest column address, or left-most column containing a hit.
This is followed by a 1-bit flag to indicate if there were any more hits within a strip.
There is also a 1-bit hit/no hit indicator – this is an internal signal to the next block.
32 columns = 32 pixels in each strip
128 rows = 128 strips
column 0
column 1
column 2
…column 31
column
address
(5 bits)
Multiple hit flag
no hits
no hits
1 hit in col 2
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
no hits
1 hit in col 31
* = 1st hit was in col 0, + there was at least 1 more hit in this row
see * below
interpretation:
Hit/no hit (internal signal)
msb
lsb
mean 0
mean 1
An example with 4 hits in the array of pixels:
hit
hit
row 0
row 1
row 2
row 3
row 4
row 5
row 6
row 7
row 8
row 9
row 10
row 11
(etc.)
column 3…

## Slide 9
The second stage of encoding sparsifies the strip data:
The strip-encoded data is checked for each of the 128 strips
The first 8 hits seen within the array, starting from row 0 at the top of the array, down to row 127 at the bottom, are encoded to output as 13 bits: multiple hit flag (1 bit) + column address (5 bits) + row address (7 bit)
Hit encoding
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
add
skip
or
1
3
2
Output bus 8x13 bits
Memory
row 0
row 1
row 2
row 3
row 4
row 5
row 6
row 7
row 8
row 9
row 10
row 11
row 12
row 13
(etc.)
row 2 had 1 hit in col 2
= 1st write to memory
row 9 had 1 hit in col 31
= 2nd write to memory
row 10 had its 1st hit in col 0,
+ there was at least 1 more hit within row 10
= 3rd write to memory
interpretation:
Multiple hit flag
Hit/no hit (internal signal)
column address (5 bits)
strip (row) address (7 bits)
Multiple hit flag
column
address
(5 bits)
msb
lsb
msb
lsb
lsb
msb
These bits are ordered to match the Serializer’s memory.
mean 0
mean 1
Multiple hit flag
column address (5 bits)
strip (row) address (7 bits)

## Slide 10
Storage and output of encoded hits - 1/3
The hit-encoded data is placed in a memory for the Serializer to stream out.
The memory format is 8 bits x 13 bits/hit as shown below. There is also a 14th internal bit for each hit, Data Valid. This is effectively 14 rows x 8 columns.
The Serializer’s memory operates as follows:
  During an initial reset phase, all 14 x 8 bits are cleared to zero, including the Data Valid bits.
  Then, as the first 8 hits are identified, for each of the 8 hit memories, Data Valid is set to 1 when the hit encoding circuit writes to that memory.
  Each row is served by an LVDS driver. The memory is emptied (clocked out) using a 320MHz clock.
Data Valid’s purpose is to distinguish between these two cases:
Internal Data
Valid bit
Data Valid is 0 => this hit memory does not contain a real hit. So this memory is empty and there were fewer than 8 hits for this cycle.
interpretation:
Data Valid is 1 => row 0 had 1 hit in column 0
column address (5 bits)
strip (row) address (7 bits)
Multiple hit flag
mean 0
mean 1

## Slide 11
Storage and output of encoded hits – 2/3
Continuing with the example of the 4 hits shown on earlier slides, the hits are written to memory and serialized as follows:
First write to memory
Second write to memory
Third write to memory
In this example, there are only 3 strips which are reporting hits, so the remaining 5 memory slots are not written and their Data Valid bits are 0.
Internal Data
Valid bit
column address (5 bits)
strip (row) address (7 bits)
Multiple hit flag
msb
lsb
lsb
msb
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Driver
LVDS Receiver
320 MHz clock
Serializer
Outs<0> = Sync/Data Valid
Outs<1> = Multiple hit flag
Outs<2> = Col<4>
Outs<3> = Col<3>
Outs<4> = Col<2>
Outs<5> = Col<1>
Outs<6> = Col<0>
Outs<7> = Row<0>
Outs<8> = Row<1>
Outs<9> = Row<2>
Outs<10> = Row<3>
Outs<11> = Row<4>
Outs<12> = Row<5>
Outs<13> = Row<6>
LVDS clock, 320 MHz
mean 0
mean 1

## Slide 12
these just summarise the values of the Outs<*> outputs
Multiple hit flag
3.125ns
Storage and output of encoded hits – 3/3
column address (5 bits)
strip (row) address (7 bits)
Internal Data Valid bit
msb
lsb
lsb
msb
Serializer memory contents:
Outs<0>
Outs<1>
Outs<2>
Outs<3>
Outs<4>
Outs<5>
Outs<6>
Outs<7>
Outs<8>
Outs<9>
Outs<10>
Outs<11>
Outs<12>
Outs<13>
Clock (320 MHz)
2
31
0
0
0
0
0
0
2
9
10
0
0
0
0
0
Col addr
Row addr
25ns – one complete readout cycle
Output waveforms:
first hit
second hit
third hit
fourth hit
fifth hit
sixth hit
seventh hit
eighth hit
mean 0
mean 1