## Slide 1: CHESS-2 Test Mode v2 with more examples 19 May 2017
J. J. John

## Slide 2
Introduction
Test Mode is used to test the CHESS-2 data out interface. It creates a fixed pattern of hits, so that no external stimulation of the sensor is required.
Test Mode has two possibilities:
  Set up one hit in column zero of a specified row, in every 25ns bunch crossing period.
  Set up one hit in column zero of each of the 128 rows, in every 25ns bunch crossing period.
Note, since the Test Mode circuit uses the row pointer (address 1) to store the row to be hit, it is only possible to select 1 row or all 128 rows. There is no way to set up hits on 2 to 127 rows.

## Slide 3
SACI commands to configure Test Mode
From the CHESS-2 spec v1.6, pp.17-18:
Send this sequence of SACI commands to set up 1 hit on a specified row:
  Read/Write = 1, Cmd = 1, address = 10, data = 0x8000 // enter test mode
  Read/Write = 1, Cmd = 1, address = 1, data = <row number> // activate 1 row
  Read/Write = 1, Cmd = 1, address = 10, data = 0x0 // exit test mode
Send this sequence of SACI commands to set up 1 hit on all 128 rows:
  Read/Write = 1, Cmd = 1, address = 10, data = 0x8000 // enter test mode
  Read/Write = 1, Cmd = 3, address = any, data = any // activate all 128 rows
  Read/Write = 1, Cmd = 1, address = 10, data = 0x0 // exit test mode
  (When activating all rows, the values of the address and data are ignored, so can be set to any value).

## Slide 4
Detailed examples
Examples of the output are shown on the following slides.
For a general explanation of the readout format for CHESS-2, please see: https://indico.desy.de/getFile.py/access?contribId=0&resId=0&materialId=slides&confId=17949
Although the outputs are shown as single-ended outputs, they in fact represent LVDS pairs (so represent the logical state, not physically accurate).
CHESS-2’s output encoding reports the first 8 hits seen on the array in a given beam crossing period. So when hits are configured on all 128 rows, the output will encode hits on only the first 8 rows.

## Slide 5
these just summarise the values of the Outs<*> outputs
Multiple hit flag
3.125ns
Output for Test Mode with Row 0
column address (5 bits)
strip (row) address (7 bits)
Internal Data Valid bit
msb
lsb
lsb
msb
Serializer memory contents:
Outs<0>
Outs<1>
Outs<2>
Outs<3>
Outs<4>
Outs<5>
Outs<6>
Outs<7>
Outs<8>
Outs<9>
Outs<10>
Outs<11>
Outs<12>
Outs<13>
Clock (320 MHz)
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Col addr
Row addr
25ns – one complete readout cycle
Output values (note, outputs are in fact LVDS):
first hit
second hit
third hit
fourth hit
fifth hit
sixth hit
seventh hit
eighth hit
mean 0
mean 1

## Slide 6
these just summarise the values of the Outs<*> outputs
Multiple hit flag
3.125ns
Output for Test Mode with Row 103
column address (5 bits)
strip (row) address (7 bits)
Internal Data Valid bit
msb
lsb
lsb
msb
Serializer memory contents:
Outs<0>
Outs<1>
Outs<2>
Outs<3>
Outs<4>
Outs<5>
Outs<6>
Outs<7>
Outs<8>
Outs<9>
Outs<10>
Outs<11>
Outs<12>
Outs<13>
Clock (320 MHz)
0
0
0
0
0
0
0
0
103
0
0
0
0
0
0
0
Col addr
Row addr
25ns – one complete readout cycle
Output values (note, outputs are in fact LVDS):
first hit
second hit
third hit
fourth hit
fifth hit
sixth hit
seventh hit
eighth hit
mean 0
mean 1

## Slide 7
these just summarise the values of the Outs<*> outputs
Multiple hit flag
3.125ns
Output for Test Mode with all rows hit
column address (5 bits)
strip (row) address (7 bits)
Internal Data Valid bit
msb
lsb
lsb
msb
Serializer memory contents:
Outs<0>
Outs<1>
Outs<2>
Outs<3>
Outs<4>
Outs<5>
Outs<6>
Outs<7>
Outs<8>
Outs<9>
Outs<10>
Outs<11>
Outs<12>
Outs<13>
Clock (320 MHz)
0
0
0
0
0
0
0
0
0
1
2
3
4
5
6
7
Col addr
Row addr
25ns – one complete readout cycle
Output values (note, outputs are in fact LVDS):
first hit
second hit
third hit
fourth hit
fifth hit
sixth hit
seventh hit
eighth hit
mean 0
mean 1
Note, Sync / Outs<0> is always high, could be challenging to synchronise