## Slide 1: FIB instructions

## Slide 2: Technology information
4 sets of modifications
Total number of modified chips: xxx
Technology: AMS 0.35µm 4metals
Layer map provided (see file layermap.txt)

## Slide 3: Origin
Definition of origin

## Slide 4: Origin
Origin (x=0, y=0) is at the bottom left corner of the GDS. PAD layer

## Slide 5: Fibing operation #1
First operation
Connect Nwell

## Slide 6: Nwell monitoring | Cut & connect
Connect M3 to M1
Cut M3
Connection line: [x1, y1] – [x2,y2] = [1482um, 5429um] – [1482um, 5425.6um]
Cut line: [x1, y1] – [x2,y2] = [1503um, 5430um] – [1503um, 5428um]

## Slide 7: Fibing operation #2
Second operation
Monitor VPFB

## Slide 8: VPFB monitoring | Cut & connect
Create via M3 to M2
Cut M3
Via position: [x1, y1] = [1432.65um, 5508.975um]
Cut line: [x1, y1] – [x2,y2] = [1436um, 5510um] – [1436um, 5508um]

## Slide 9: Fibing operation #3
Third operation
Connect amplifier input

## Slide 10: Amplifier input monitoring | Cut & connect
Cut M3
Connection line: [x1, y1] – [x2,y2] = [1425.2um, 5639.775um] – [1425.2um, 5635.75um]
Cut line: [x1, y1] – [x2,y2] = [1437um, 5641um] – [1437um, 5639um]
Connect M3 to M1 – avoid M2

## Slide 11: Fibing operation #4
Fourth operation
Connect amplifier output

## Slide 12: Amplifier output monitoring | Cut & connect
Cut M3
Connection line: [x1, y1] – [x2,y2] = [1410um, 5719.8um] – [1410um, 5708.8um]
Cut line: [x1, y1] – [x2,y2] = [1425um, 5720.5um] – [1425um, 5719um]
Connect M3 to M1 – avoid M2

## Slide 13: End
End of file