## Slide 1: Progress and next steps 1 June 2017 this version is the minutes of the meeting
J. J. John on behalf of the team

## Slide 2
Agenda
Discuss progress and steps for next week:
  ABCN’ testing
  CHESS-2 news
  ABCStar/HCCStar news
  TWiki page for CHESS and its test hardware: https://twiki.cern.ch/twiki/bin/view/Atlas/CHESSStripTestChip

## Slide 3
ABCN’ testing
Status:
  Isaiah reconfigured the code. He and Robin have successfully verified setting the DACs and SACI commands (write and read back).
  The ABCN’ is responding to triggers.
  Not seeing expected data yet when Test Mode enabled on CHESS-2: all zeroes all the time, including the Data Valid bit. However when the CHESS-2 board was powered down, saw random data from the ABCN’.
    We concluded that the inputs to the FPGA are connected up correctly, so this looks like an issue with configuring CHESS-2.
    Also Isaiah and Robin verified the connections within the FPGA with the Technology Schematic in the Xilinx tools.
  Added ChipScope inside ABCN’ just where data received, but seeing all zeroes there too.
  So far only the first 2 commands in the Test Mode sequence were issued: Enter Test Mode and select row. Jaya John understood you need to also Exit Test Mode to exit the setup/programming mode, to enable Test Mode (was poorly worded in slides, sorry).
  Pietro suggested to run the clocks at half speed (20 MHz and 160MHz instead of 40 and 320). This will no doubt break the rest of the ABCN’ firmware but might allow the LVDS data to reach the ABCN’?

## Slide 4
ABCN’ testing
Next steps:
  Try these 4 possibilities, both with normal and half-speed clocks:
    Issue first two commands only ([addr 10, data 0x8000], [addr 1, data = row])
    Issue first two commands, but with the default values for the rest of register 10 ORed in with data 0x8000.
    Issue all 3 commands ([addr 10, data 0x8000], [addr 1, data = row], [addr 10, data 0x0]) – on the theory that Test Mode is enabled by the third command, “exit test mode.”
    Issue all 3 commands but with but with the default values for the rest of register 10 ORed in with data 0x8000 and data 0x0.
  If none of these work, please e-mail Pietro and Su Dong at SLAC requesting advice on the additional commands they needed to send, in order to see data out of CHESS-2.
    There may be some LVDS configuration needed to make the outputs work.
  Setting up the SLAC carrier board and software and learning what is done to bring up the interface is another way, but there is some learning curve to get there.