## Slide 1: CHESS-2 BUG REPORT

## Slide 2: Power Supply On: 0.232 A

## Slide 3: Provide Global Reset: 0.351 A

## Slide 4: Set DAC Voltages: 0.837 A

## Slide 5: Enable Comparator on All Pixels: 0.758 A
All Data goes to zeroes, which is what we expect

## Slide 6: Enable Test Mode: 0.758 A
However, test mode doesn’t appear to work

## Slide 7: Disable Comparator on All Pixels: 0.830 A
If we disable comparators, we begin to get back data

## Slide 8: Enable Test Mode: 0.775 A
Row 0 gets “hits”, multi-hit is always valid which isn’t supposed to happen, column data is random (should be 0); also hits not on every ‘event’

## Slide 9: Test Mode Enable Row 3
Row data is correct, column data is still bad and multi-hit is still on

## Slide 10: Test Mode Enable Row 4
It looks like rows can be selected, however other data is wrong

## Slide 11: End Test Mode: 0.843 A
Random data again

## Slide 12: Disabling Rows Sequentially
Data begins being picked up by the chipscope after 66 rows have been disabled