## Slide 1
Integrated phase locked loop design
Nina Parkalian
Forschungszentrum Jülich GmbH
Central Institute for Engineering, Electronics and Analytics
IC Design
18-19 September 2017

## Slide 2
Phase locked loop (PLL)
Generating sampling clocks for ADC and digital circuitry
High frequency clock synchronizes with a low frequency reference clock
Programmability to get best performance
Phase locked loop

## Slide 3
Design specifications
Loop bandwidth: The optimum quantity is selected to guarantee stability and low
noise operation
Phase noise: Noise requirements are considered to prevent signal to noise
degradation in ADC
Increasing reliability: Due to the long term performance of the design
Power consumption
Area
The parameters of every block is determined to fulfill the requirements of the design:

## Slide 4
Chip fabrication in 65nm CMOS
The default values for the design parameters include:
Reference frequency: 31.25MHz
Oscillator frequency: 4GHz
Sampling clock frequency: 1GHz
Divison ratio: 128
Programmable options provide the following ranges:
15.625 MHz ≤ reference frequency ≤ 62.5MHz
128 ≤ division ratio ≤ 1008
62.5MHz ≤ sampling clocks ≤ 1GHz
3.6GHz ≤ VCO frequency range ≤ 4.28GHz
Power consumption: 30mW
Area: 0.72µm×0.5µm
Chip micrograph and PLL layout

## Slide 5
Measurement results
The results of tuning range of oscillator is compatible with the expectations from simulations
Measurements approve the functionality to generate a VCO frequency of 4GHz for sufficient
temperature range
Locking process of PLL
Tuning range of oscillator

## Slide 6
Phase noise
Effect of clock jitter on signal to
noise ratio (SNR) in ADC
PLL phase noise
The maximum tolerable jitter for the ADC to prevent SNR degradation is 10 psrms
The measurements show 1.4 psrms jitter for the PLL

## Slide 7
ZEA-2 – System-house for the Science