## Slide 1
The Vulcan Chip
Analog
Ugur Yegin, Nina Parkalian, Pavithra Muralidharan, Christian Roth
Hamburg
18 September 2017

## Slide 2
3 identical input channels sensing different signal ranges, all independently adjustable
1 amplification stage (TIA), power supplies, DAC’s and 4 6-bit ADC’s (8-bit if combined) per channel
All clock signals provided by on chip PLL
Smart data selection by digital core, buffers available for short term storage
Data output by 16 LVDS pairs
4.7mmx4.7mm (ca 22mm²) with TSMC65 GP, QFN88 double row package
VULCAN: basics and introduction
4.7 mm
Layout of second Vulcan prototype
TIA, power supply, DAC‘s, TRG
4x6 bit ADC‘s
PLL
Digital core
Digital core
LVDS

## Slide 3
1 test chip (all units as stand-alone blocks) and 2 prototypes (full signal chain) successfully tapeouted
Test chip and 1st prototype measured, verified. Christian Roth will present.
1st prototype served as platform for debugging errors, all mended before 2nd prototype
2nd prototype is production ready version, will arrive at CW 45-47
Verification plan being assembled now
Production run (dedicated mask set) due in 2018
VULCAN: Overview of current status

## Slide 4
 | 2017 |  |  |  |  |  |  |  |  |  |  |  | 2018 |  |  |  |  |  |  |  |  |  |  | 
 | Q1 |  |  | Q2 |  |  | Q3 |  |  | Q4 |  |  | Q1 |  |  | Q2 |  |  | Q3 |  |  | Q4 |  | 
Vulcan | Verification Pt1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | FAB & Packaging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | Verification Pt2 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fab & Packaging |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TEST |  |  |  | 
Vulcan Schedule
07.08.2017: TO PT2
4.4.2018: Start Production
CW45-47: Silicon back
31.08.2017: Silicon back
NOW

## Slide 5
All functional blocks already included on 1st prototype
Minor bugs preventing plug&play operation, solved by FIB
Improvements implemented on 2nd prototype
  Digital
    Timing of clocktree (for both digital circuits and ADC) and LVDS improved significantly
    Scanchain test implemented
    Power routing improved significantly
  Power
    Capless LDO‘s improved to serve different current consumption windows
    Improved power supply for TIA to match for low input impedance over bandwidth
    Optional 1-supply voltage only operation implemented
  TIA
    Improved measurability and power supply strategy for biasing
  PLL
    Improved linearity of amplitude
    Output buffer made bypassable
VULCAN: 1st  2nd prototype

## Slide 6
Capless regulators to reduce risk of external component failure during long term operation
Regulators comprise of regular LDO structure assisted by NMOS diodes
Current output range adjustable (up to 50mA for LDO‘s, 200mA for linear regs)
Digital structures, LVDS cells powered by typical linear regulators
TIA stages powered by adjustable diodes for bandwidth reasons
EM&IR test conducted using Voltus
Featuring: Power management
AMP
Act. tr
Act. tr
Diode
Diode
VOUT_in (2.5V or 1V)
VDD_ext (3.3V or 1.8V)
VREF (1V)

## Slide 7
Implemented to compensate the overshoot effect at the TIA input
Excess current generated by input bias resistor generated by OSC instead of TIA
For low gain channel, OSC performs as ADC input stage
Versatile switching structure allows OSCOUT to perform as test input for ADC
Featuring: Overshoot

## Slide 8
Independent trigger structure signalling events
Dedicated LVDS output to bypass ADC and digital core
Dynamic comparator with 250MHz, operable with up to 1GHz
Less than 350ps propagation delay, overall reaction time limited by operating frequency
Output single pulse or long pulse, depending on preference and external FPGA
Featuring: Analog Trigger
Dyn. Comp
IN
REF
CLK
Delay
Latch
DFF
LVDS

## Slide 9
Thank you very much for your attention!

## Slide 10
Backup slides

## Slide 11
Highly linear, fully integrated circuit – Vulcan
  Sampling ADC with approx. 80 dB linearity (3 signal chains with 3 different gains)
  No external components required
  On-chip clock generation from ref. clock
Precise signal reconstruction
  No analog delay line (reducing noise & distortion)
  Control loop to suppress DC variations
  Optional overshoot compensation
Further key parameters of Vulcan:
  ADC with 9.5 bit (3x 8 bit), 1 Gsample/s
  Input impedance of < 10 Ohm
  Power consumption ~ 1.2 Watt
VULCAN: Overview of current status
Key Parameter of Vulcan | 
Process | 65 nm CMOS
Active Area | 22 mm2
Power | ~ 1.2 W
Input Impedance | < 10 Ohm
Input Bandwidth | 500 MHz
Sampling Rate | 1 Gsample/s
Dynamic Range | 80 dB
ADC Resolution | 3x 8 bit
High Gain | 0.06 p.e./bit
Medium Gain | 0.4 p.e./bit
Low Gain | 8 p.e./bit

## Slide 12
Signal Modes – Small & Medium Signals
First two signal chains
Parallel TIA input
Programmable gains
Combined input resistance
small & medium signal mode
large signal mode
patent pending

## Slide 13
Signal Modes – Large Signals
Third signal chain
Current > 20 mA
TIA input saturates, ESD diodes open
Voltage over diodes measured
Combined input resistance
small & medium signal mode
large signal mode
patent pending

## Slide 14
Major tasks of digital processor:
  Data selection (3 ADC  1 sample)
  Meta data generation (ADC source, system events)
  Data buffering (Deal with meta data overhead)
Data suppression for noise
  Determined by threshold
  Cut off 4 MSBs
Buffer size based on supernova simulation
Data Processing System
Simulation in cooperation with F. Lenz (RWTH Aachen)

## Slide 15
Dedicated Trigger Lines
Fast response on signals
  One LVDS line per ADC
Source selectable during runtime
  Analog or digital threshold trigger
  Two integral triggers
Additional Digital Features
Baseline Regulation
Feedback loop to correct baseline
  Regulation only in noise mode
Configurable during runtime
  Enable
  Threshold
  Speed

## Slide 16
Generally: Product failures in different phases:
  Infant mortality due to manufacturing defects
  Normal life & ware-out due to electromigration
    Electromigration covered by design & simulation
Manufacturing defects due to process variations
  Varying between wafers and with position on wafer
  Goal: Filter out all unreliable ICs, only stable survive
Extensive verification plan for product tests
  Structural scan test and IDDQ test for digital circuits
  Stress test to verify electro migration
  Functionality test and performance selection
Reliability Measures
Bathtub curve, source: Wikipedia
Strong Defects
Not operational transistors/wires
Immediate impact on functionality
Weak Defects
Weakened wire, wears out over time
Fails with stress on circuit

## Slide 17
Material transport by gradual movement due to electron collisions
  Dependent on current density in the conductor
  Degradation of the metal over time
  Leads to connection faults in the design
Prevent by design methods
  Use wider/multiple conducting wires
  Use multiple vias instead of single vias
Perform electromigration studies to estimate degradation prior tapeout
  Based on IR drop simulation
  Detailed power consumption analysis
  Critical areas are easily visible
Electromigration-Aware Design
IR drop analysis
Electromigration effect

## Slide 18
Digital part composed of combinatorial and sequential logic
  Goal: Test the functionality of digital gates
  Method: Include a scan chain to determine faulty gates
Flip flops (FFs) exchanged by scan FF
  Two modes for operation: regular and scan
  Scan data loaded through scan chain, representing logic state
  Data is processed through combinatorial logic
  Data shifted out to scan output
Scan pattern generated by ATPG tool
Detects single stuck-at-fault gates and delay faults
Structural Scan Tests
ATPG = automatic test pattern generator
Vulcan: 140,000 FFs

## Slide 19
 | 2017 |  |  |  |  |  |  |  |  |  |  |  | 2018 |  |  |  |  |  |  |  |  |  |  | 
 | Q1 |  |  | Q2 |  |  | Q3 |  |  | Q4 |  |  | Q1 |  |  | Q2 |  |  | Q3 |  |  | Q4 |  | 
Vulcan | Verification Pt1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | FAB & Packaging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | Verification Pt2 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fab & Packaging |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | TEST |  |  |  | 
JUNO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Vulcan Schedule
07.08.2017: TO PT2
4.4.2018: Start Production
1.10.2018: First set of final electronics ready for potting
Engineering Samples
15.11.2017: 2nd prototype JUNO electronics
15.1.2018: Verification Review
First Samples
CW45-47: Silicon back
31.08.2017: Silicon back
2.4.2018: Production Readiness Review
NOW
PCU
Integration Measurements:
Base
GCU
27.3
24.4
Mid June