Integral Interface
Low-Level Drivers for PCI Express Endpoint
Grzegorz Jabłoński
Adam Piotrowski
Dariusz Makowski
DMCS, TUL

---
Overview
- Low-level drivers for PCI Express Endpoint provide a bridge between a PCI Express bus and registers in the user logic
- The drivers also allow for generation of MSI interrupts from the user logic to the root complex
- Integral Interface is a set of VHDL functions and code generators, allowing easy access to a set of registers and memory blocks in an FPGA code

---
Block Diagram

---
User Logic Interface

---
II Input File
@version "1.0"
@mapFileName "DAC001_32.map"
reg id=reg1 width=14 attr=rw type=u impl=rw comment="Register 1"
area id=area1 width=12 attr=rw type=f impl=r count=234 addr=0x400 comment="Array 1"
Address
Register name
Array size
Number of bits
Attributes implemented
automatically
Attributes
Type (float, signed, unsigned...)

---
Generated Files
- VHDL code for accessing the registers (ii_constants.vhd, ii_custom.vhd, ii_functions.vhd)
- VHDL template for user code (ii_template.vhd)
- C header file (ii_constants.h), containing information about registers and memory blocks
- MAP file containing information about registers and memory blocks in textual form

---
Example 1 - ii File
@version "1.0"
@mapFileName "DAC001_32.map"
reg id=reg1 width=32 attr=rw
area id=SAMPLES1 width=32 count=512 attr=rw

---
Example 1 - Generated Entity
library IEEE;
use IEEE.Std_Logic_1164.all;
use ieee.std_logic_signed.all;
use ieee.std_logic_arith.all;
use work.ii_constants.all;
use work.ii_functions.all;
use work.ii_custom.all;
-- synthesis translate_off
library UNISIM;
use UNISIM.VComponents.all;
-- synthesis translate_on
entity userIP is port
  (
    ii_addr : in std_logic_vector(31 downto 0) ;
    ii_data_in : in std_logic_vector(31 downto 0) ;
    ii_data_out : out std_logic_vector(31 downto 0) ;
    ii_irqN : out std_logic;
    ii_irq_ackN : in std_logic;
    ii_ackN : out std_logic;
    ii_strobeN : in std_logic;
    ii_writeN : in std_logic;
    ii_resetN : in std_logic;
    iclk : in std_logic
  );
end userIP;

---
Example 1 - Defined Registers
- Signals s and v are most important to us - they contain all registers we have defined in the .ii file
- We can access them using notation like
  s.reg
  v.samples1
architecture synthetised of userIP is
-- ii signals
   signal ii_data_i: std_logic_vector(II_DATA_SIZE-1 downto 0);
   signal laststrobeN, laststrobeN_d : std_logic;
   signal ii_addr_i: std_logic_vector(II_USED_ADDR_BITS-1 downto 0);
   signal s: ii_scalar_data;
   signal v: ii_vector_data;
   signal v_addr1, v_addr2: ii_vector_addr;
   signal BRAMackN_r,BRAMackN_rd,BRAMackN_w: std_logic;
-- end of ii signals block
package ii_custom is
type ii_scalar_data is record
  reg1 : std_logic_vector(getRegisterSize(reg1)-1 downto 0);
end record;
type SAMPLES1_memory is array (integer range 0 to shiftLeft(1,ii_c(SAMPLES1).indexing_bits) -1) of
        std_logic_vector(ii_c(SAMPLES1).reg_bits-1 downto 0);
type ii_vector_data is record
  SAMPLES1 : SAMPLES1_memory;
  dummy_field_to_make_ise_71i_happy: std_logic;
end record;

---
Example 1 - Bus Control Code
begin
-- prepare short version of address
ii_addr_i <= ii_addr(II_USED_ADDR_BITS-1 downto 0);
ii : process(iclk,ii_resetN) -- interface with the bus
  begin
    if ii_resetN = '0' then
     laststrobeN<='1';
     laststrobeN_d<='1';
     BRAMackN_w<='1';
     BRAMackN_r<='1';
     BRAMackN_rd<='1';
  else
    if iclk'event and iclk = '1' then
-- shift in strobe
      laststrobeN <= ii_strobeN;
      laststrobeN_d <= laststrobeN;
-- prepare BRAM addressses
      v_addr1 <= assignVectorAddresses(ii_addr_i);
      v_addr2 <= v_addr1;
-- generate BRAM acknowledge -
-- delayed one or two cycles
      BRAMackN_w <= genVectorAck(
        ii_addr_i, ii_writeN)
        or ii_strobeN or ii_writeN;
      BRAMackN_r <= genVectorAck(
        ii_addr_i, ii_writeN)
        or ii_strobeN or (not ii_writeN);
      BRAMackN_rd <= BRAMackN_r;
      if ii_strobeN = '0' and laststrobeN = '1'
        and ii_writeN = '0' then
-- save data from bus to registers
        s<=save_scalar_data(s,ii_addr_i,ii_data_in);
      end if;
      if laststrobeN = '0' and laststrobeN_d = '1'
        and ii_writeN = '0' then
-- Saving vector data
    v.SAMPLES1(getIndex_SAMPLES1(v_addr1))
        <=saveReg(v.SAMPLES1(getIndex_SAMPLES1(v_addr1)),
        SAMPLES1,ii_addr_i, ii_data_in);
-- End of saving vector data
    end if;
  end if;
end if;
end process ii;
-- read data from registers to bus
ii_data_i <= extractScalars(s, ii_addr_i);
-- Reading vector data
ii_data_i<=
      extractVec(v.SAMPLES1(getIndex_SAMPLES1(v_addr2)),
        SAMPLES1,ii_addr_i);
-- End of reading vector data
ii_data_out <= filter_valid(ii_data_i);
      --workaround for problems with PCIe endpoint model
-- generate acknowledge
ii_ackN <= (genScalarAck(ii_addr_i, ii_writeN)
        and BRAMackN_w and BRAMackN_rd) or ii_strobeN;
ii_irqN<='1'; --no interrupt
end synthetised;

---
Example 1 - Testbench
-- write the value of the cell with address 4
PROC_II_WRITE(expandTo32Bits(ii_c(SAMPLES1).a(0)) or x"00000004",
        x"deadbeef", ii_addr, ii_data_in, ii_writeN, ii_strobeN,
wait for 300 ns;
PROC_II_READ (expandTo32Bits(ii_c(SAMPLES1).a(0)) or x"00000004",
        data, ii_addr, ii_data_out, ii_writeN, ii_strobeN, ii_a
wait for 300 ns;
PROC_II_WRITE(expandTo32Bits(ii_c(reg1).a(0)),x"5555AAAA", ii_addr,
        ii_data_in, ii_writeN, ii_strobeN, ii_ackN, sys_clk);
wait for 300 ns;
PROC_II_READ (expandTo32Bits(ii_c(reg1).a(0)), data, ii_addr,
        ii_data_out, ii_writeN, ii_strobeN, ii_ackN, sys_clk);
wait for 300 ns;

---
Example 1 - Testbench (cont.)
do simulate_mti.do

---
Example 2 - Interfacing The World
@version "1.0"
@mapFileName "DAC001_32.map"
reg id=leds width=2 attr=rw
reg id=switches width=2 attr=r

---
Example 2 - Interfacing The World
entity userIP is port
  (
    ii_addr : in std_logic_vector(31 downto 0) ;
    ii_data_in : in std_logic_vector(31 downto 0) ;
    ii_data_out : out std_logic_vector(31 downto 0) ;
    ii_irqN : out std_logic;
    ii_irq_ackN : in std_logic;
    ii_ackN : out std_logic;
    ii_strobeN : in std_logic;
    ii_writeN : in std_logic;
    ii_resetN : in std_logic;
    iclk : in std_logic;
    leds_out : out std_logic_vector(1 downto 0);
    switches_in : in std_logic_vector(1 downto 0)
  );
end userIP;
-- read data from registers to bus
ii_data_i <= extractScalars(s, ii_addr_i);
-- Reading vector data
-- End of reading vector data
ii_data_out <= filter_valid(ii_data_i); --workaround for problems with PCIe endpoint model
-- generate acknowledge
ii_ackN <= (genScalarAck(ii_addr_i, ii_writeN) and BRAMackN_w and BRAMackN_rd) or ii_strobeN;
ii_irqN<='1'; --no interrupt
leds_out<=s.leds;
s.switches<=switches_in;
end synthetised;

---
Example 3-7
See ii_examples_1.05.tgz

---
Building Complete Project
- The example project for the ML506 Carrier Board is enclosed
- Have to take care of the appropriate constraints
-- xilinx_pci_exp_ep.vhd
attribute keep: string;
attribute keep of pci_ii_addr: signal is "TRUE";
attribute keep of pci_ii_data_in: signal is "TRUE";
attribute keep of pci_ii_data_out: signal is "TRUE";
attribute keep of pci_ii_writeN: signal is "TRUE";
--project.ucf
NET "pci_ii_addr*" TPSYNC="endp";
NET "pci_ii_data_in*" TPSYNC="endp";
NET "pci_ii_data_out*" TPSYNC="endp";
NET "pci_ii_writeN" TPSYNC="endp";
INST "userIP_inst/*" TPSYNC = "user_gwj";
INST "pi/*" TPSYNC = "ep_gwj";
TIMESPEC "TS_1" = FROM "user_gwj" TO "endp" 4 ns;
TIMESPEC "TS_2" = FROM "ep_gwj" TO "endp" 4 ns;
TIMESPEC "TS_3" = FROM "endp" TO "user_gwj" 4 ns;
TIMESPEC "TS_4" = FROM "endp" TO "ep_gwj" 4 ns;