## Slide 1: Tests on Chess 2 ASIC
Dionisio Doering, Yubo HanIHEP , Pietro Caragiulo, Larry Ruckman, Camillo Tamma, Mazin KhaderUIUC, Murtaza Safdari, Su Dong

## Slide 2: Outline
Tests with delayed Qinj :
->daughter board 01-carrier board 23
->daughter board 19-carrier board 28
Qinj: pulse width: 15μs
pulse delay: 35μs

## Slide 3: Pixel description

## Slide 4: Running the test with Qinj delayed
5 pixels were chosen
2 “hot ” pixel and 3 “quiet ” pixels
(20,5) (80,24) (10,2) (61,6) (15,5)
PIXTH=1.2V, default configuration
Carrier Board 192.168.3.23
Daughter board: 01(std resistivity)
Carrier Board 192.168.3.28
Daughter board: 19(high resistivity)
7 pixels were chosen
4 “hot ” pixel and 3 “quiet ” pixels
(15,5) (20,20) (120,30) (110,3) (80,2) (11,5) (61,3)
PIXTH=1.2V,Default configuration
->first results didn’t show any “delay”
->change the firmware and add delay on both Qinj0 and Qinj1

## Slide 5: Pulse delay
Pixel (15,5)
Carrier Board 192.168.3.28
Daughter board: 19(high resistivity)
Default configuration
PIXTH: 1.2V
Matrix 1
Matrix 0
No delay
with delay
Pluse Delay: 35μs

## Slide 6: Pulse delay
Pixel (20,20)
Carrier Board 192.168.3.28
Daughter board: 19(high resistivity)
Default configuration
PIXTH: 1.2V
Matrix 1
Matrix 0
No delay
with delay
Pluse Delay: 35μs
Matrix 2

## Slide 7: Summary
The structure will move with delayed Qinj on carrier board 28-daughter board 19. and the Qinj on that board doesn’t work properly.
carrier board 23-daughter board 01 didn’t show big difference with delayed Qinj.
Still didn’t see any strong evidence of signal.