## Slide 1: SCS Optical Laser Delivery
Laurent Mercadier and Robert Carley
Instrument Scientists
SCS Group
Schenefeld, 21-22 February 2018

## Slide 2: Overview
Pump-probe laser at European XFEL
  Laser system
  Burst mode operation
  Sample heating
SCS optical delivery
  Instrument laser hutch
  Frequency conversion (nHG, OPA, THz)
  Laser in-coupling (LIN)
  THz in-coupling
Temporal diagnostics
  Pulse arrival monitor
  X-ray – optical cross-correlator
Day 1 solution

## Slide 3: SASE 3 Experimental Area
PP Laser
SCS
ILH
SCS
EXP
SQS
ILH
SQS
EXP
Open
Port
SCS
CTRL

## Slide 4
Pump-probe laser properties
Synchronized seed laser-oscillator and delay stage for X-Ray – OL overlap
Burst-mode Yb-all-fiber CPA front-end: 2 synchronous outputs, 100kHz, 200kHz, 1MHz and 4.5MHz
White light seed generation in YAG (Δλ ≥ 700 – 900 nm) & variable pre-chirp
Burst-mode 3-stage Yb:amplifier chain (Innoslab-technology): up to 40 mJ, 100kHz – 4.5MHz
Arbitrary pulse and burst selection for „pulse-on-demand“ (PoD)
NOPA with 3 working points
1030nm
Soliton
seeder
Dt =
0-5ns
burst-mode
all-fiber CPA
front-end
super-
continuum
variable
prechirp
AOM
PC
NOPA 1+2
NOPA 3a
Compressor
SHG
SHG
SHG
NOPA 3b
sync via fiber
and OBC
x-ray-optical
laser overlap
sub-ps
1030nm, 1 … 40mJ, 4.5 … 0MHz
400 ps
800nm,
0.05 … 2mJ,
4.5 ... 0MHz,
15 … 300fs
Yb-booster 1
(burst-mode)
5 kW
Yb-pre-amp
(burst-mode)
400 W
4.5MHz
1MHz
100kHz/
200kHz
4W @
4.5, 1, 0.2, 0.1 MHz
20W @
4.5MHz
Compressor
Guido Palmer (XFEL Optical Laser Group)

## Slide 5: The pump-probe laser
20 Hz burst mode operation possible
10 Hz to each instrument
No changeover time
SCS
SQS
Moritz Emons (XFEL Laser Group)

## Slide 6: Pump-probe laser operating modes
EXFEL X-ray burst
0.6% duty cycle at 10 Hz
1 to 2700 pulses
PP laser burst
 |  |  |  | 800 nm | 1030 nm
Mode | F_rep / MHz | Δt / ns | F_eff / kHz | E_pulse / mJ | E_pulse / mJ
1 | 4.5 | 222 | 27 | 0.05 | 1
2 | 1 | 1000 | 6 | 0.2 | 4
3 | 0.2 | 5000 | 1.2 | 1 | 20
4 | 0.1 | 10000 | 0.6 | 2 | 40
 |  | Pulse duration |  | 15-300 fs | <1ps or 400 ps
Lower Frep possible at any pulse energy
Actual data rate
Sample heating

## Slide 7: Sample Heating Example: FeRh
0.2 MHz
1 MHz
DT
5mJ/cm2
Alexander Yaroslatsev

## Slide 8: Sample Heating Example: FeRh
Driving an AFM-FM phase transition in FeRh
Pump beam size at 1 MHz and 0.2 kHz
Heat sink and initial temperature selection important to stay below a target temperature
Room Temp.
LN2 Temp.
Room Temp.
LN2 Temp.

## Slide 9: Sample Heating Example: FeRh
The pump beam size is restricted by:
  At high repetition rates – beam size becomes too small (<10µm)
  At low repetition rates – by heating the sample holder and prevention of heat removal
repetition rate | 0.15 MHz
pump beam size (FWHM) | 200-350 µm
probe beam size (FWHM) | 70-120 µm
sample size | 200 µm
pump fluence (800 nm) | 5 mJ/cm2
probe fluence (707 eV) | 0.5 mJ/cm2
Sample dimension 200 µm diameter
Layers: Fe 40 nm, SiN 100 nm, Al 600 nm

## Slide 10: SCS Instrument Laser Hutch
Beams from pp laser hutch
Beams to Open Port
800 nm
1030 nm
Beams to SCS EXP hutch
1030 nm beam for THz streaking (XOX)
800 nm beam for PAM
1030 nm beam for THz pump
800 nm beam for sample pump, SHG & THG and OPA pump
800 nm, 1030 nm, OPA output
800 nm
1030 nm
Detailed design and procurement are ongoing
Start installation Q2/18

## Slide 11: Pump-probe laser tuning properties
800 nm NOPA pulses and immanent tuning capabilities
M. Pergament et al, Opt. Express 22, 22202-22210 (2014)
M. Pergament et al, Opt. Express 24, 29349-29359 (2016)
Autocorrelation
Spectrum
Tuning

## Slide 12: Conversion results with 800 nm at 100 kHz
SHG = 400 nm, THG = 266 nm
delay: 800nm
λ/2: 400nm
Separator I
Combination mirror
Switch:
SHG/THG
SHG-BBO
THG-BBO
Input
SHG Output
THG Output
300 x 300 mm

## Slide 13: Conversion results with 800 nm at 100 kHz
SHG
THG
15 fs – pump pulses with 2.37 mJ:
  400 nm: ESHG = 475 µJ, ηSHG = 20%
  266 nm: ETHG = 28 µJ, ηSHG = 1.7%
55 fs – pump pulses with 1.76 mJ:
  400 nm: ESHG = 760 µJ, ηSHG = 43%
  266 nm: ETHG = 255 µJ, ηSHG = 17%

## Slide 14: Conversion results with 800 nm at 100 kHz
Development in collaboration with Light Conversion Ltd.
TOPAS-prime with extensions: NirUVIS and NDFG
TOPAS results with pump:
  E = 1.8 mJ, Ø = 8 mm (1/e²) , 55 fs

## Slide 15: Frequency Conversion: Terahertz
1030 nm, 850 fs
0.1 – 30 mJ
100 kHz x 600 μs x 10 Hz
Wu et al., Opt. Lett. 39, 5403 (2014)
Grating
Lens 1
f1 = 150 mm
Lens 2
f2 = 75 mm
Mirror
LiNbO3
THz beam
λ/2

## Slide 16: Frequency Conversion: Terahertz
13.3 uJ @ 10 mJ
0.133 %
  0.2% conversion in cooled LiNbO3 → 80 μJ
J. Liu, P. Zalden, R. Carley, L. Mercadier, G. Palmer et al.

## Slide 17: SCS Laser In-coupling
PP Laser
SCS
ILH
SCS
EXP
SQS
ILH
SQS
EXP
Open
Port

## Slide 18: SCS Laser In-coupling (LIN)

## Slide 19: SCS Laser In-coupling
Beams from ILH
800 nm (+ SHG & THG)
1030 nm (+ SHG & THG)
OPA
Beams to PAM & XOX
800 nm
1030 nm
Quasi-collinear beam delivery to sample
Mirror elevator
Vacuum chamber attached to steel frame
(not granite)
Steel frame
Grouted granite

## Slide 20: SCS Laser In-coupling
X-ray beam

## Slide 21: SCS Laser In-coupling
34 mm
1015 mm
Interaction point 1
Beam line end: Gate Valve (DN 160)
Laser in-coupling mirror
FEL
Line of sight for a 2" mirror

## Slide 22: THz In-coupling
THz generation in lithium niobate
  1030 nm, 40 mJ, 800 fs drive
  0.2% conversion in cooled LiNbO3 → 80 μJ
Separate in-coupling near the experiment
  Also for other wavelengths
Off-axis parabolic mirror in vacuum on 6-axis manipulator
FEL beam
Laser in-coupling
THz generation

## Slide 23: Temporal Diagnostics
Transient reflectivity: Photon arrival time monitor
  Spatial encoding
  Spectral encoding
THz streaking: x-ray – optical cross correlator

## Slide 24: Spatial encoding
Beye et al., App. Phys. Lett. 100, 121108 (2012)
Notes: Before you start editing the slides of your talk change to the Master Slide view:
Menu button “View” > Slide Master:
Edit the following items:
1. On the Title slide (second master slide)
a) Click to add title of your talk
b) Click to add subtitle (conference, location, name of the speaker, date)
2. On the Slide Master (first master slide)
a) The 1st row in the violet header: Delete the existent text and write the title of your talk into this text field b) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area.
Close Master View

## Slide 25: Spectral encoding
B. Li, X-Ray Photon Temporal Diagnostics for the European XFEL, Technical Report TN-2012-002-01 (2012.)

## Slide 26: Temporal Diagnostics: Photon Arrival Monitor
J. Liu, F. Dietrich, J. Grünert: “Technical Design Report: Photon Arrival Time Monitor (PAM) at the European XFEL”, XFEL.EU TR-2017-002 (2017)

## Slide 27: X-ray pick off mirror
Pick off edge of x-ray beam
Focus to increase intensity at low X-ray pulse energies

## Slide 28: THz streaking of photoelectrons
Grguraš et al., Nat. Photonics 6, 852 (2012)
Pick off x-ray beam
Solid target
  No residual gas
  High target density
R&D project with WP74 (X-ray photon diagnostics, Jan Grünert, Jia Liu)

## Slide 29: Day 1 pump-probe laser
PP-laser not available during the first run
We work on a solution with an AFS fiber laser…
  wavelength: 1030 nm
  max. pulse energy: 200 µJ
  pulse duration 340 fs
  average power: 70 W
…with possibility to couple to an OPCPA to produce:
  wavelength: 1.4 – 1.6 µm
  max. pulse energy: 20 µJ
  pulse duration: 30 - 50 fs
This solution could be offered beginning of 2019

## Slide 30: Acknowledgements
WP 74 X-ray Photon Diagnostics
  Jia Liu
WP 78 Optical Lasers
  Guido Palmer, Moritz Emons
SCS
  Andreas Scherz
  Jan Torben Delitz
  Carsten Boers
Sample Environment
  Manuel Izquierdo
Thank you!
  Alexander Yaroslavtsev
  Justine Schlappa
  Loic Le Guyader
  Alexander Sorin
  Hazem Bamaga
  Naman Agarwal

## Slide 32: SCS Instrument Tours
Group A: Go now to the reception desk
Group B: Go at 15:15 to the reception desk
Group C: Go at 15:30 to the reception desk
Group D: Go at 15:45 to the reception desk