Alignment with beam halo MC
Andrea Parenti
05/05/2009
Outline:
Alignment with Beam Halo (BH) only
Alignment with Minimum Bias (MB) only
Alignment with BH + MB

---
Initial geometry and parameters
Alignment is done of High level structures: 'TIDRingsLayers13,110001', 'TrackerTECDiskLayers11,cc000c', 'TrackerTECDiskLayers24,110001', 'TrackerTECDiskLayers55,cc000c', 'TrackerTECDiskLayers69,110001'
Start from ideal geometry + custom misalignent
  - TIDRings & TECDisks as in 10pbScenario
    - TIDRings:	185 mm (u,v),	850	mrad (g)
    - TECDisks:	70 mm (u,v),	30 mrad (g)
  - no misalignment applied on smaller structures, and on the barrel sub-detectors

---
Alignment with beam halo
Based on 20X beam halo Monte Carlo
  - the available statistics is limited: ~60k events
Track collection: ALCARECOTkAlBeamHalo
Track selection:
  - ptMin = 0.
  - etaMin = -999.	/ etaMax = +999.
  - nHitMin = 6	/ nHitMin2D = 2
  - chi2nMax = 50.
  - minMultiplicity = 1
Nb. of selected tracks: ~31200

---
Alignment with BH: TEC results
Initial and remaining misalignment:
Correlation of remaining and initial misalignment:

---
Alignment with BH: TID results

---
Alignment with Minimum Bias
Based on 20X (CSA08) Monte Carlo
  - expected similar rate as Beam Halo... using 175k events
Track collection: ALCARECOTkAlMinBias
Track selection:
  - ptMin = 1.5
  - etaMin = -10.	/ etaMax = +10.
  - nHitMin = 8	/ nHitMin2D = 2
  - chi2nMax = 50.
  - minMultiplicity = 1
Nb. of selected tracks: ~302200

---
Alignment with MB: TEC results

---
Alignment with MB: TID results

---
Alignment with Beam Halo + Minimum Bias

---
Alignment with BH+MB: TEC results

---
Alignment with BH+MB: TID results

---
Comparison of the results
For TID BH+MB results are much better than BH and MB only (especially for angular parameter)
For TEC, results are dominated by BH but anyway the angular parameter benefits from combination with MB
Combining BH+MB, there are no more outliers and no shifts in the mean of parameter residuals