## Slide 1: DHH in the ATCA shelf
Stefan Huber
24.01.2018

## Slide 2: DHH in the ATCA module
DHC
DHE1
DHE2
ł
ł
ł
ł
ł
DHE
DHI

## Slide 3: DHH in the ATCA module / RTM

## Slide 4: DHC Features
  Hardware Link to EPICS, ONSEN and FTSW
  Jitter cleaned clock via SiLabs-chip, has to be programmed after power cycle Used as reference clock on all DHEs
  Interface to all connected DHEs via UCF protocol (Up to 5 DHEs)
    Distribute Trigger and Clock Phase synchronous to all DHEs
    IPBus hub for all connected DHEs Multiplex Ethernet packages
    Buffer Data from DHEs

## Slide 5: DHE Features
  Operates on the recovered UCF clock
  Phase synchronous to the B2TT clock
  Controlled via IPBus 2
  DHP data-interface as used in PERSY
  Limited trigger rate
  No overlapping triggers Not surprisingly limit of 12 kHz trigger rate

## Slide 6: Installation at KEK
  One ATCA shelf
  Two ATCA carriers
  Each houses one DHC and two DHEs
  Control connection to the DHPT via DHI prototype
  Data interface via optical fibers
  Accessible via shroud computer

## Slide 7: Status KEK
  Status
    All modules accessible by IPBus
    UCF link stable over long periods
    Possible to take data at 12kHz over long time period

## Slide 8: Issues at KEK
  Issues
    IPBus looses packages
    Trigger number in DHE/DHC mismatch requires manual reset Simon implemented IOC
    After powering up: Reprogram DHC to get stable UCF clock
    Memory dump data: Sometimes one additional word
    Not full trigger number transferred to DHE

## Slide 9: Issues at KEK
  DHC has to be reprogrammed after switching on power
  Explanation:
    High speed transceivers need toggling reference clock during startup
  Resolution: Boot with oscillator clock Program SiLab chip Switch reference clock
    IPBus looses packages
    Trigger number in DHE/DHC mismatch requires manual reset Simon implemented IOC
    After powering up: Reprogram DHC to get stable UCF clock
    Memory dump data: Sometimes one additional word
    Not full trigger number transferred to DHE

## Slide 10: Issues at KEK
  IPBus looses packages
  Explanation:
    Multiplexer logic on DHC
  Resolution: Rewrite that logic

## Slide 11: Issues at KEK
  Trigger number in DHE/DHC mismatch requires manual reset
  Explanation:
    Runreset not propagated to all necessary places
  Resolution: Propagate reset to DHE Keep reset high for ~1us at DHC (distance to first trigger should be at least 1us)
  Memory dump data: Sometimes one additional word
    Not full trigger number transferred to DHE

## Slide 12: Issues at KEK
  Memory dump data: Sometimes one additional word
  Explanation:
    Not understood yet
  Resolution: ??? Memory dump data: Sometimes one additional word
    Not full trigger number transferred to DHE

## Slide 13: Issues at KEK
    Not full trigger number transferred to DHE
  Explanation:
    Only 16 bit transferred from DHC to DHE
  Resolution: Transfer 32 bit

## Slide 14: Recent firmware improvements
    Startup with oscillator instead of B2TT clock
    UCF stability improvements
    Full 32 bit trigger information to DHE
    Reset DHC for 1us after runreset signal
    Tested last week, not able to get good data

## Slide 15: Last missing item: Support of overlapping triggers
FIFO1 SOE
Buffer first-row information
FIFO1 EOE
Buffer first-row information
FIFO2 SOE
Start pointer
first frame
FIFO2 EOE
Start/End pointer
second frame
Data
Trigger
Trigger
Hit row boundary
Dual ported Memory
Assemble one frame per trigger
Firmware developed, tested during the next weeks

## Slide 16: Conclusion
    Phase2 DHH system is installed at KEK
    Possible to take data at trigger rates <= 12kHz
    Some issues identified, no showstoppers
    High rate firmware to be tested