## Slide 1
DHPT Temperature Sensing
For Phase 2
Leonard Germic
University of Bonn

## Slide 2: Why we cannot use the DHP Temp Sensor?
The DHP Temp Sensor needs a reference voltage
  Nominal VDD=1.2V
Problem: Sensing not working properly; value of VDD?
Per design: The temperature has a linear dependency on VDD
[mV]
[C]
VDD?

## Slide 3: Measurements
Hybrid5.0.10 (DHPT1.1, DCDBv2)
Temp Sensor has not changed since DHPTv1.0
PT100 4-wire sensing
  100Ω @ 0°C
  T(R) dependency

## Slide 4: Measurements
Set chiller temperature from 0C to +50C (increment in 5K steps)
  Measured TDHP(VDD) with Hybrid5 and ‘true’ TPT100 with PT100
  For each TDHP-curve one ‘true’ temperature is assigned
VDD [mV]
TPT100
DHP temp higher than chiller temp
DHP temp lower than chiller temp
TDHP [C]

## Slide 5: Measurements
Curve parameters
  Intercept b does not supply any information since real VDD unknown
  Slope m does supply information, but errors are to large!
TPT100 [C]
Intersept b
m(TPT100)
b(TPT100)

## Slide 6: Measurements
Calibration curve for TDHP vs TPT100 @VDD=1.2V
  TDHP(TPT100) = 12.0(3) + 1.07(3) x TPT100
  Offset of +12C : DHP temperature measurement returns higher values
TDHP [C]
TPT100 [C]

## Slide 7: Conclusion
DHP temperature read-out withou VDD sensing not possible
DHP temperature calibration yields offset of +12C @ VDD=1.2V
DHP temperatures measurements returns higher values
  Due to voltage drop the DHP temperature measurement returns significantly higher values than the real temperature.
  Overestimation ->
VDD [mV]
TDHP [C]
Voltage drop