## Slide 1: XFEL-Gun Operator Training
F.Brinker
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Content
Overview Gun system
Typical measurements
Critical parts
  RF-window
  Cathode holder
Diagnostics and interlock systems
RF-operation

## Slide 3
Actual view to the XFEL gun
4 circulators to the 10MW Klystron
UV Laser beamline
cathode- exchange system
gun body
Water distribution

## Slide 4
Actual view to the XFEL gun diagnostics
Faraday cup
Toroid
Dark current monitor
RF-Vacuum window (Thales)
BPM
screens
Optics table
Darc current kicker
Darc current collimator

## Slide 5
Cathode laser
Laser profile before the aperture
and on the virtual cathode

## Slide 6
RF-phase [deg]
Charge [nC]
Phase scans at different laser intensities
First measurements with beam:
Phase scan for different laser intensities
Famous „Zero crossing“
„Han bump“

## Slide 7: Measurement of dark current

## Slide 8: Beam energy measurement with spectrometer magnet

## Slide 9
16.2. :
Measurement of beam momentum depending on RF-power
First measurements with beam:
Energy measurement
MeV/c

## Slide 10: critical parts
Cathode plug and RF-spring
RF-Window

## Slide 11
Short History of the XFEL Gun in HH
1. RF operation Dezember 2013
  Successful test of RF-system
  5.5 MW, 650 us reached
  Limit : light at the window
  Massive damages on the cathode RF spring
2. RF operation September 2014
  Successful test of the improved cathode spring system
  4.8 MW, 400us reached
  Limit : vacuum leak at the window
3. RF operation Dezember 2014
  Short test of glued window
  4.8 MW, 400us reached
  Limit : vacuum leak at the window
1. Beam operation February 2015
2. Beam operation April/May 2015
( See last years talk )

## Slide 12: View from the backside into the cathode holder with the spring ( still under vacuum )
No signs of damage so far after 88-days of operation
Assumption: the trouble came from a bad contact between the holder, spring and plug.
The cathode spring system had been replaced by a system where all contact surfaces had been polished and/or gold plated. ( same geometry )

## Slide 13: Cathode plug without any damages or marks after the December run

## Slide 14: Examination of the leakage after September run 2014 ( typ. 4.8MW, 400 us ):
While the cathode spring test had been successful the RF-window developed a leakage after some days
Since a new Thales window was not available at that time it has been tried to localize and fix the leakage
Surprisingly it was not the brazing but the ceramics which got leaky
Ceramic disk from air side

## Slide 15: Test run on the window test stand with the Thales6 and one Gamp-window
Test with 6.5 MW, 900 us travelling wave
Test with full reflection:
  20 μs pulse length ( + 35% )
  10 Hz
  2-6 MW RF-power
  Distances to the reflector were varied
Simulation for the test stand configuration: M.Bousonville
After about 1.5 weeks the conditioning was stopped – no vacuum break outs, no light from Thales, still continuous light from Gamp

## Slide 16: Dependance of field strength and vacuum activity on window Position [ D.Kostin, M.Bousonville ]
Actual position
  field strength on the ceramics is nearly at maximum
  medium vacuum activity
with 100mm shift:
  field strength on the ceramics is minimal
  bit less vacuum activity

## Slide 17: Exchange of RF-window, March ’15 with 100mm insertion
Massive reduction of field strength on the ceramic
Significant improved pumping speed with additional IGP
100mm vacuum waveguide between Thales RF-window and coupler

## Slide 18: Gun signals and interlocks

## Slide 19: Gun signals and interlocks

## Slide 20: Gun signals and interlocks

## Slide 21: LLRF fast protection – looking at the reflected power

## Slide 22: Limits of fast protection

## Slide 23: Fast Gun Ramp Up – new FSM version
1) FSM On
2) Choose targets: gradient and pulse width
Estimation for the start temperature
3) Set start temperature and wait until it’s reached (~0.2 C )
4) Start ramp by switching FSM RF On
FSM messages

## Slide 24
The FSM sets the Gun frequency on the actual resonance frequency defined by the temperature
Gradient and pulse length are ramped up
  The temperature set point tracks the actual temperature which rises with RF power
  The frequency is kept on resonance to avoid reflections
After reaching the target values, the FSM is waiting for the temperature to stabilize before setting the frequency to nominal.
When Set points for amplitude and phase are close to the measured values the feedback and learning feed forward are started plus the pulse width modulation
From now on the gun parameters can be changed by hand as usual
Fast Gun Ramp Up – new FSM version

## Slide 25: Water temperature regulation
Precise,fast temperature regulation by adding cold water
Heating by adding hot water ( slow )

## Slide 26
Heating up by adding hot water from the tanks

## Slide 27
Cooling down with cold water

## Slide 28
Pulse width modulation
Fast measurement of gun temperature (0.1sec vs. 7 sec)
compensate temperature deviations with the RF pulse width

## Slide 29: Strong temperature ( detuning ) dependance of light emission
Below 2200 Hz
Much less activity.
200Hz = 0.01°C!

## Slide 30: Charge delivered from Gun 4.3 since Jan 2016:
3.5 C
2700 bunches, 0.5 nC (July 2016)
Practically no interlocks since 2 years during the runs
Light interlock at the window vacuum side was disabled – but the vacuum threshold stood at 3·10-10 mbar

## Slide 31: December 2017: Exchange of the gun
This December the gun will be exchanged with the Gun 4.6, which has been conditioned at PITZ
The two guns are identical beside a different cathode spring design ( watchband reloaded at 4.6 )
The goal is to have two identical guns available which proved to deliver beams for SASE
Before the installation the two Gamp windows have been exchanged by one Thales window
Reconditioning will be necessary at beginning of next year for one week

## Slide 32: ( re- ) conditioning starting ~Jan 4th
  Startup without frequency detuning
  Starting with short pulses, low rep rate and high power
  Encreasing the rep rate and the pulse length while reducing the peak power
  Restart with short pulses after interlocks
  Exact parameters will be defined
Restart after vacuum >1E-7
reflected power IL
Spark detected
Procedure after last window exchange

## Slide 33
Thank you !