## Slide 1: Sub-femtosecond Injector Design and X-Band TDS
Dr Barbara Marchetti
Center Evaluation DESY, 5 – 9 February 2018
Helmholtz Program: Matter & Technology (MT)
PoF III Topic: Accelerator Research & Development (ARD)
DESY Research Unit: MPY1

## Slide 2: Outline
SINBAD-ARES Photo-Injector
X-band TDS Project

## Slide 3: Outline
SINBAD-ARES Photo-Injector
X-band TDS Project
ARD Team MPY-1 in DESY-M:
R. Assmann, U. Dorda, J. Zhu, D. Marx, G. Vashchenko, T. Vinatier, F. Burkart, Y. Sumera, P.A. Walker, F. Lemery
and R. Brinkmann, K. Floettmann, W. Hillert
Essential support of DESY technical groups
Production of sub-fs e-bunches with conventional RF technology

## Slide 4: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Photo-injector goal:
Production of high brightness fs long e-bunches for injection into novel compact high gradient accelerators (LWFA, DLA, THz driven accelerators etc.)
PL: U. Dorda. LS: R. Assmann
ARES linac

## Slide 5: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Photo-injector goal:
Production of high brightness fs long e-bunches for injection into novel compact high gradient accelerators (LWFA, DLA, THz driven accelerators etc.)
Photo-injector parameters:
  2.998 GHz normal conducting linac
  10-50 Hz rep. rate, single bunch mode
  Energy: 100 MeV (compressed beam)
  Typical final bunch charge : 0.5-30 pC
  Typical final bunch length : sub-fs to few fs
  Arrival time jitter < 10fs RMS
  Normalized transverse emittance < 0.5mm*mrad
PL: U. Dorda. LS: R. Assmann
ARES linac

## Slide 6: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Why a “conventional” photo-injector for studying novel accelerators?

## Slide 7: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Why a “conventional” photo-injector for studying novel accelerators?
Conventional RF technology allows to produce a stable and reproducible e-bunch

## Slide 8: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Why a “conventional” photo-injector for studying novel accelerators?
Conventional RF technology allows to produce a stable and reproducible e-bunch
The quality of the acceleration in novel accelerators depends on the quality of the injected beam (e.g. bunch length, emittance, arrival time stability, energy)  flexible widely tunable Working Points

## Slide 9: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Why a “conventional” photo-injector for studying novel accelerators?
Conventional RF technology allows to produce a stable and reproducible e-bunch
The quality of the acceleration in novel accelerators depends on the quality of the injected beam (e.g. bunch length, emittance, arrival time stability, energy)  flexible widely tunable Working Points
Well known beam dynamics codes have not yet been benchmarked with experiments in this special beam parameter range  extending our understanding of beam dynamics

## Slide 10: SINBAD-ARES photo-injector
ARES = Accelerator Research Experiment at Sinbad
Why a “conventional” photo-injector for studying novel accelerators?
Conventional RF technology allows to produce a stable and reproducible e-bunch
The quality of the acceleration in novel accelerators depends on the quality of the injected beam (e.g. bunch length, emittance, arrival time stability, energy)  flexible widely tunable Working Points
Well known beam dynamics codes have not yet been benchmarked with experiments in this special beam parameter range  extending our understanding of beam dynamics
Characterization of ultra-short (~fs), low charge (~sub-pC) bunches is challenging  test novel diagnostics devices  see also second part of this talk.

## Slide 11: Technical Highlights
The conceptual design of the accelerator has been completed.

## Slide 12: Technical Highlights
The conceptual design of the accelerator has been completed.
The technical design of the accelerator and its procurement is ongoing. It will proceed in stages.

## Slide 13: Technical Highlights
The conceptual design of the accelerator has been completed.
The technical design of the accelerator and its procurement is ongoing. It will proceed in stages.
Infrastructure ready.
RF gun installation ongoing.
Commissioning foreseen to start soon this year.

## Slide 14: Outline
SINBAD-ARES Photo-Injector
X-band Transverse Deflectance Structure (TDS) Project
Joint Project involving different teams from DESY:
FLASHForward
FLASH2
SINBAD
possibly XFEL
+ external collaboration with CERN and PSI
Essential support of DESY technical groups
Longitudinal Diagnostics for
ultra-short e-bunches

## Slide 15: Measuring e-Bunches with sub-fs Resolution
State of the Art of X-Band TDS Systems
Measurement of the energy spread induced by the FEL process at SLAC
Achieved temporal Resolution < 1fs for soft X-rays
C. Behrens et al., „Few-femtosecond time-resolved measurements of X-ray free electron laser“ , Nat. Comm. 4762 (2014).

## Slide 16: Novel X-band TDS Concept with Variable Polarization
Variable Polarization Circular TE11 Mode Launcher
Very precise azimuthal symmetry in manufacturing required!
Phase difference between port 1 and port 2:
0 degree -> vertically streaking field
180 degree -> horizontally streaking field
A. Grudiev, CLIC-note-1067 (2016)

## Slide 17: Novel Applications in Beam Diagnostics
3D Charge Distribution Reconstruction in the Real Space
Exciting new opportunities for e-bunch characterization e.g.:
slice emittance measurement on different planes
3D charge reconstruction
efforts towards 6D beam phase space reconstruction
Example of beam reconstruction
(simulation) for the ARES linac
Real beam at the screen
(TDS off)
Reconstructed beam at the screen
Reference: D Marx et al 2017 J. Phys.: Conf. Ser. 874 012077

## Slide 18: Collaboration DESY-CERN-PSI
Goal: build and test the first prototype
Common Mechanical Design of the Structure fulfilling the requirements of many experiments:
  FLASHForward, FLASHII, SINBAD at DESY. XFEL observer of the project.
  ATHOS beamline at SwissFEL
The cavities are realized using PSI tuning free assembly procedure
First Review Meeting (October 2017) about Tolerances Evaluation gave positive feedback
Test of the prototype cavity with beam at DESY (FLASHForward beamline)
If the test of the prototype is successful, six other cavities will be produced for the experiments
Reference: “X-Band TDS Project”, MOPAB044, Proc. IPAC 2017
Status of the Project:
Collaboration Agreement under Signature by Directorates of the three Parties

## Slide 19: Summary and Conclusion
The ARES linac at SINBAD has been designed to produce ideal ultra-short high brightness bunches to
  Test and fully characterize novel acceleration techniques aiming for stable and reproducible acceleration;
  Perform beam dynamics studies and R&D on novel beam diagnostics.
  The installation of the RF gun is ongoing and its commissioning will follow soon this year.
The X-band TDS Project is an example of R&D project in the direction of novel diagnostics techniques
  A novel TDS design with possibility of changing the streaking direction of the field is being realized thanks to a collaboration with CERN and PSI
  Studies on applications of the novel feature of the cavity for e.g. allowing 3D charge reconstruction of an electron bunch have been performed and DESY will provide the infrastructure for testing the prototype cavity with e-beam.
Thank you for your attention.