## Slide 1: Ultra-short bunches at FLASH
Juliane Rönsch-Schulenburg, Siegfried Schreiber
Center Evaluation DESY, 5 – 9 February 2018
Helmholtz Program: Matter & Technology (MT)
PoF III Topic: Accelerator Research & Development (ARD)
DESY Research Unit: Accelerator Research & Development (ARD, ST3)

## Slide 2: Introduction
User frequently asks for short FEL pulses
Reducing the length of the electron bunch reduces the length of the SASE-FEL pulse
Drive this reduction of FEL pulse length to its limits, which is a so-called single-spike

## Slide 3: FLASH
6500 fs
≈ 100-200 fs
Compression Factor C
C ≈ 32-65
Q ≈ 1000 pC
2000
→ 3 fs
15 pC
RF tolerances limit possible compression
130 - 220
→ 30 - 50 fs
250-150 pC
Space charge forces require to reduce the charge
(~ 100-120 fs pulses)
(~ 40 fs pulses)
The minimum radiation pulse duration :

## Slide 4: Short bunches at FLASH
6500 fs
≈ 100-200 fs
Compression Factor C
C ≈ 70
Q ≈ 1000 pC
1000 fs
30 fs → 3 fs
C ≈ 50 → 330
Q ≈ 100 pC → 15 pC
2000
→ 3 fs
15 pC
RF tolerances limit possible compression
130 - 220
→ 30 - 50 fs
250-150 pC
Space charge forces require to reduce the charge
Chart: time (ps)
Streak camera measurement of injector laser

## Slide 5: Ultra-short bunches at FLASH
In 2010, when short pulse studies started, FLASH was typically operating in a charge regime from 0.5 nC to 2 nC
Requirements
  Beam diagnostics for low charge and short bunch operation
  Especially important: beam-arrival time, bunch length
  Precision controls of RF accelerator tolerances & femtosecond synchronization
Proof of principle experiment has been performed in 2014
Benefit for general accelerator research
  beam-arrival time monitor (BAM) prototypes are used also at XFEL in a modified version
  Development of IR-spectrometer for measurement of a few fs pulses together with FLASHForward
7+/-1 fs (FWHM)
→ ~3 fs (rms)

## Slide 6: Single-spike operation
For 6.8 nm XUV radiation at FLASH1
(2016)
>50% of the shot were pure single spikes
M = 1.6
M = 1.6
frequency
GMD energy

## Slide 7: Ultra-short pulses
For 6.8 nm XUV radiation at FLASH1
The minimum radiation pulse duration :
  6.8 nm
  = 35 m +/- 3 m
= 4 fs +/- 0.4 fs
M = 1.6
~ 3 fs +/- 1.7 fs (rms)
Bunch Compression factor
180
115

## Slide 8: FLASH2: single-spike
Results:
maximum fluctuation: 97%
→ number of modes: 1.05
FEL pulse duration: 6 fs (rms)
For 41 nm XUV radiation at FLASH2
Time (fs)
Wavelength (nm)
number of undulators

## Slide 9: Summary
The ultra-short pulse studies started in 2010
Proof-of-principle experiment successfully finished in 2014
Ultra-short pulses with single-spikes could be produced in FLASH1 & FLASH2
  FLASH1: pulse duration: 3 fs +/- 1.7 fs (rms), 1.6 modes in average @ 7nm
  FLASH2: pulse duration: 6 fs (rms), 1.05 modes in average @ 41nm
Most diagnostics have already been upgraded to low charge operation
Upgraded beam-arrival time monitors (BAM) will be installed this summer
Ultra-short pulses available for users operation since end of 2016
  Thus the ARD topic has been transformed into MML topic