## Slide 1: Design considerations of the LUXE beamline
Laser Und XFEL.EU Experiment
Florian Burkart
Hamburg, 23/08/2018

## Slide 2: Agenda
01 Location at the XFEL
02 Experimental Scenarios and Beam Parameters
03 Beam line design and Integration
04 Conclusion and Outlook

## Slide 3: Location at the XFEL
XS4
XTD5
XTD3
XTD7
XTD8
XS1
(480 m)
(595 m)
(263 m)
(301 m)
(204 m)
(137 m)
(660 m)
(365 m)
(546 m)
(221 m)
UN1
UN2
End of UN2 Begining of Dump
3039 m – 3145 m

## Slide 4: Dump Area – XTD5, XSDU1

## Slide 5: How it looks like in the tunnel...

## Slide 8
Nice location, but:
In case of a severe beam dump failure (dump exchange), the full
experimental setup has to be removed.

## Slide 9: Experimental Scenarios and e- Beam Parameters
Option 1: collide electron beam with laser pulse
Option 2: collide electron beam with foil  photon generation  collide photons with laser pulse
Electron beam parameters:
Electron energy: 17.5 GeV
Bunch intensity: 1 nC ( 6.25E9 e-)
Spotsize @ IP: s = 5 mm
Repetition Rate: 1 – 10 Hz

## Slide 10: Option 1: Electron - Laser
Dipole
PDET
EDET
E < 16 GeV
e−
e+
γ
γCAL
Photon converter
Dipole
e+
e−
γ
CAL
Laser
pulse
IP
Mirror
Mirror
Dump
Dump
17.5 GeV e−
XSDU1
XTD5
Collimation
Dipole
Triplet
Kicker & Septa
Dipole
1bunch
Single bunch kicker helps machine protection.
Space efficient design.
Kicker and Septa design can be copy-pasted.

## Slide 11: Option 2: Photon - Laser
Dipole
PDET
EDET
E < 16 GeV
e−
e+
γ
γCAL
Photon converter
Dipole
e+
e−
γ
CAL
Laser
pulse
IP
Mirror
Mirror
Dump
Dump
17.5 GeV e−
XSDU1
XTD5
Collimation
Dipole
Triplet
Kicker & Septa
Dipole
1bunch
Photon converter

## Slide 12: Electron distribution downstream of IP
Electron energy distribution simulation parameters:
Ee- : 17.5 GeV
sx,y : 30 mm
Laser Intensity: 1E20 W/cm2
Wavelength: 800 nm
Spotsize: 100 mm2
Transversal distribution
Energy intensity distribution
Courtesy: A. Hartin
New simulation with updated parameters running…

## Slide 13: Energy – Intensity distribution, Zoom
~ 5 % of the bunch is below nominal energy.
Down to 5 GeV.

## Slide 14: Optics in XTD5
UN2
Bends

## Slide 15: Optics in XTD5 with extraction to LUXE
Kicker
Septa

## Slide 16: Kicker and Septa parameters
 | Kicker
Pulse Form | Burst
Pulse Width | 30 ns
Rise / Fall Time | 10 ns
Kick angle per element | 6.25 mrad
Number of elements | 10
Aperture | 30 mm
Active length | 2 m
Pulser Voltage | 5 kV
Pulse Current | 100 A
 | Septum
Type | Lambertson
Deflection angle | 35 mrad
Active length | 1 m
Septum bar width (incl. beam pipe) | 5 mm (10 mm)
Number of elements | 4
FOTOS

## Slide 17: Final focus optics – downstream of Septum
Beam size at the IP: s = 5.4 mm

## Slide 18: Final focus optics - Zoom
Beam size at the IP: s = 5.4 mm
Distance to first Quad: 9 m

## Slide 19: Triplet Magnet Parameters
Gradient: 100 T/m
Length: 10 cm
Aperture: 16 mm

## Slide 20: Schematic CAD Integration
Kicker/Septa
Bend
Triplet
IP
Dump
Downstream of IP design to be studied.

## Slide 21: Single Bunch Beam Dump
First design considerations
~ 200 W power deposition
Al-Cu design, size and dimensions to be discussed.
In vacuum – Design of the beam window to be studied.
Shield dimensions to be discussed with radiation protection
Injector Beam Dump Design

## Slide 22: Outlook - next steps
Optics design
  Beam quality after UN2?
  Spectrometer design
  Collimator design
  Beam Instrumentation requirements
Detector design
Laser beamlines and interaction region design.
Evaluate required shielding
  Single Bunch Dump
  General Radiation protection
Background to Detectors
Safety and Integration

## Slide 23: Conclusion
First design considerations.
Possible location of the experiment with space constraints found in XTD5 / XSDU1
Re-use or copy existing design of magnets and elements.
Input from various groups.
IP, spectrometer and detector design ongoing.
Integration studies ongoing.
Layout and achievable parameters look feasible.

## Slide 24: Acknowledgements
R. Assmann, R. Brinkmann, W. Decking, N. Golubeva, A. Hartin, I. Hartl, B. Heinemann,
J. List, E. Negodin, M. Schmitz, M. Wing, …
Thank you

## Slide 25
Dr. Florian Burkart
Department: MPY1
Florian.Burkart@desy.de
Phone: 040-8998 3039

## Slide 26: Foil survival
Tungsten, 0.035 cm, 5 mm e- spot size
beam direction (cm)
Transversal (cm)
Edep (GeV/cm3/e-)
T: 80 K
Pressure waves, to be studied

## Slide 27: Optics in XTD5 with extraction to LUXE
Kicker
Septa

## Slide 28: Dump Area