## Slide 1
Natalia Kuzminchuk - Feuerstein
Bernd Voss, Oleg Bogdanov, Elena Rozhkova,
Christoph Scheidenberg
Matter and Technologies AM, Berlin June 12 – 14, 2018
Liquid Cherenkov detector as a
diagnostic tool for relativistic heavy ions (TOF measurements)

## Slide 2: TOF focal plane detectors
High rate and radiation dose detector
time resolution σ < 50 ps, path length 60 - 80 m
active area 380 / 200 mm x 80 / 50 mm
particle rate up to 107 ions / spill
radiation dose @FMF2 1Gy / h

## Slide 3: Motivation: Cherenkov Radiation
Cherenkov radiation (ChR) – is an electromagnetic radiation emitted when a charged particle passes through a medium at a velocity greater than the phase velocity of light in that medium: is emitted at a specific angle θC with respect to the strait-line trajectory (or to velocity direction)
At Super FRS @ FAIR:
heavy ions at E=300 MeV/u÷1.5 GeV/u  β=0.65 ÷ 0.92
The number of Cherenkov photons created at threshold velocity
Required material with high reftactive index n!
(including energy loss in the radiator)
Altapova V.R., Bogdanov O.V., Pivovarov Yu.L.,
NIM B 256 (2009) pp.109-113
Cherenkov angle:
Cherenkov light is a promt event and therefore ideal for timing measurements

## Slide 4: Material for Cherenkov Radiator: Solid, Gas or Liquid?
Gas
Contra
Solid:
  Particle rate resistance
Liquid:
  With > n increases toxicity, presence of color centers and viscosity
Gas:
  very low refractive index: ntyp.=1.0003 (β≈0.99)
  Pressure dependency of n
n(420 nm)=1.00029 (P0=1 atm)
 not suitable
Threshold velocity:
β=1/n≈0.9999 (55 GeV/u)

## Slide 5: Liquid radiator: Iodine Naphthalene
Iodine Naphthalene (C10H7I):
nD =1.7001 @ 589 nm
ρ=1.738 g/cm3
Dispersion curve
Otto Schott Research Centre Mainz-Marienborn
Threshold velocity:
β=1/n≈0.59  E ~ 220 MeV/u
Application of liquid radiator allows
the circulation of the active material
and therefore to greatly reduce the effects of the degradation of the optical performance expected after exposure to the high ion rates at the Super-FRS

## Slide 6
Ion beam
1160 mm
420 mm
Light tight box
Prototype detector design
Light guides
PMT L
PMT R
[1160 x 420 x 140 mm]
N. Kuzminchuk-Feuerstein et. al., NIM A 866 (2017) 207
Cuvette filled with C10H7I
Windows: borosilicate glass;
Side: N-SF10 glass plates;
Araldite 2020
Coating: Aluminium [0.15 µm]

## Slide 7: TOF Measurements with 124Xe ions at CaveC
New cuvette construction:
T263 borosilicate glass [0.1 mm]
L:W:H 170 x 5.2 x 85 mm
Higher number of Cherenkov photons
Bigger signal amplitude
Better coupling between cuvette and light
guides
(S) (Ch)
vacuum
4 x PMTs
Su (d,l,r)
124Xe
[600 MeV/u]
PMT L PMT R
PMT Assembly:
HAMAMATSU H6610 (R5320)
Detector arrangement Data Acquisition

## Slide 8: Time-of-Flight Spectra (124Xe ions)
=<>-<>

## Slide 9: New modular design of a prototype of a TOF - Cherenkov detector
16 PMTs
Active
media
Beam
16 LEDs
Light tight
housing
LED driver
circuit boards
HV supply
732 mm
ø 560 mm
PMT1
PMT9
36 mm
Overall ø 560 mm
ø 18 mm active media disk
1 – 5 mm thickness
16 PMTs XP1918 Photonis [ø 15 mm]
16 LEDs for calibration
Driver circuit boards to control LEDs

## Slide 10: Calibration and DAQ
To correct the difference in signal transit path
To monitore the temporal resolution (σ)
LEDs pulse width in ns range
To trigger 16 LEDs in sequence
Requirements :
Data Acquisition
LED1
PMT1
PMT2
LED2
Circuit board
to control LED
in progress
VFTX TDC [16 Ch.] is read
out by GSI DAQ MBS
running on RIO4
R. Siegert, Bachelor Thesis,
Hochschule RheinMain, Rüsselsheim.

## Slide 11: Summary and Outlook
For the future TOF measurements a Cherenkov detector employing a liquid radiator (C10H7I) is proposed, designed and constructed
Principal operation was approved in the beam time with 58Ni ions at SIS18 (CaveC) (2014)
First TOF measurements was performed at SIS18 (CaveC) with 124Xe ions (600 MeV/u) using improved construction: σ = 63 ps
So far, we have not reached any limitation in the particle rate, which has shown any degradation of the optical properties of the liquid: accumulated number of particles ~ 11 x 1011
A new modular design to increase the timing intrinsic resolution and not to limit to a certain application (different active media, thickness)
New measurements with 107Ag, 208Pb - ions possible in 2018 to test the rate capabilitity of the detector (up to 107 /s), TOF measurements and DAQ

## Slide 12
Thank you
for your attention!

## Slide 13: First proof of principle experiment with 58Ni ions at CaveC
58Ni
700 MeV/u
Pb-targe
Particle
detectors
Detector arrangement Scheme diagram of the electronic arrangement
S1R S1L
S2R S2L
ChR ChL
at ~0.3 MHz scintillators reached saturation level
I~103 ions/spill E= 1.5 GeV/u
Ch
Ch
N. Kuzminchuk-Feuerstein et. al., NIM A 866 (2017) 207