## Slide 1: Optical Modules.
for the IceCube Upgrade and IceCube-Gen2
Timo Karg
4th Annual MT Meeting, Berlin, 13 June 2018

## Slide 2
http://icecube.wisc.edu
~300 scientists, 48 institutions, 12 countries

## Slide 3
JINST 12 (2017) P03012

## Slide 4
Up-going track: Muon from muon-neutrino interaction
time
early
late
charge
Measure Cherenkov light from charged particles in the ice

## Slide 5: The IceCube Digital Optical Module (DOM)
Requirements
Single p.e. to few hundred photons (instantaneous)
Good Timing (all DOM clocks synchronized to < 2 ns)
  Data/timing/power over 3.3 km copper pair
Low noise (MeV supernova neutrinos)
  Dark noise dominated by radioactivity in glass pressure housing
Withstand > 550 bar freeze-in pressure
Survive shock vibration; ships, planes, sleds
Features
Records PMT waveform of every “hit”
  300 MHz sampling switched capacitor array + 40 MHz ADC
Power consumption ~3 W
98.4% of deployed modules operational!
NIM A 601 (2009) 294
13 inch (33 cm)
10-inch PMT

## Slide 6: Our Vision: The IceCube-Gen2 Facility
Gen2
High-Energy Array
PINGU
Gen2 Surface Veto
IceCube
DeepCore
Multi-component observatory:
Surface air shower detector
Gen2 High-Energy Array
Sub-surface radio detector
PINGU
A wide band neutrino observatory (MeV – EeV) using several detection technologies – optical, radio, and surface veto – to maximize the science
J. Phys. G 44 (2017) 054006
Gen2 High-Energy Array
~120 strings
80 OMs per string
~9600 optical modules
PINGU
26 strings
up to 192 OMs per string
up to 4992 optical modules
up to 15k optical modules will be required
arXiv:1412.5106 [astro-ph.HE]

## Slide 7: A First Step: IceCube-Upgrade
Science goals
  νµ disappearance
  ντ appearance
  Precise calibration of IceCube optical properties and DOM response
Baseline sensor design: mDOM
Proposals pending – News expected soon!

## Slide 8: Improving the In-Ice Detector With New Sensors
Event resolution, overall sensitivity and cost effectiveness can be improved with new sensors, hence a dedicated R&D effort was started
More photons per muon/cascade
  Increase photocathode area per module
  Increase UV sensitivity
More information per photon
  Segmented instrumentation
More modules per unit construction cost
  Narrower modules → narrower boreholes

## Slide 9: New Sensor Designs for Improved Performance
This presentation
directional information
more sensitive area / module
mDOM
36 cm
PoS(ICRC2017)1047
(U Erlangen, U Münster, DESY)
D-Egg
directional information
more sensitive area / module
smaller geometry
30 cm
PoS(ICRC2017)1051
(Chiba)
LOM
small diameter
directional info.
more sens. area / module
(UW Madison)
13 cm
WOM
more sensitive area / module
small diameter
lower noise rate
(HU Berlin, U Mainz, DESY)
11 cm
PoS(ICRC2017)1052

## Slide 10: The mDOM (multi-PMT Digital Optical Module)

## Slide 11: mDOM: multi-PMT DOM
Adapted from KM3NeT mDOM
24 × 3-inch PMTs
Diameter: 14 inch
Features
Doubled effective area rel. IceCube DOM
Uniform 4π sr effective area
Local coincidences (e.g. bkg. suppression)
Directional sensitivity
Improved photon counting
Challenge
Power and digitize 24 PMT channels using ≲ 3 W
PoS(ICRC2017)1047

## Slide 12: mDOM Multi-ToT Readout
comp A
Cyclone 5 FPGA
PM signal
comp B
comp C
comp D
sampling @ 600 MHz
channel 2
to channel 24
SERDES 1:4
4 bit
parallel processing @ 150 MHz
DAC adjustable thresholds
A. Kretzschmann (DESY)
SERDES 1:4
SERDES 1:4
SERDES 1:4
SERDES 1:4
8 bit
4 bit
4 bit
channel 2
to channel 24
channel 2
to channel 24
channel 2
to channel 24
ADC 250 MHz, 14 bit
∑
ADC
multi-ToT
Other readout designs under study:
Slow (~40 MHz) ADC + TDC
DRS4-based (switched capacitor array)
0.9 to 1.5 W for 24 channels (w/o ADC, FPGA)
depends on pulse-shaping
1.2 GHz sampling for lowest threshold 600 MHz for other thresholds

## Slide 13: mDOM Multi-ToT Readout: Measurement Setup
HV supply
dark box with PM, LED and auxiliary preamplifier
signal transmission (single-ended)
6 ch. analog front-end
pulsed LED
R12199-02 PMT w/ passive base
mainboard w/ FPGA
2nd channel used for triggering only
power divider: splits PM-signal to D.U.T. and scope

## Slide 14: mDOM Multi-ToT Readout: Three Example Waveforms
4 thresholds
time
1.67 ns

## Slide 15: mDOM Readout: Single PE Pulses
Leading Edge Time (rel. to LED trigger)
Time-over-Threshold
Jitter: 3 ns (TTSσ: 1.7 ns)
Very first measurement! Systematic characterization will follow
Afterpulses?

## Slide 16: The WOM (Wavelength-shifting Optical Module)

## Slide 17: WOM: Wavelength-shifting Optical Module
Basic concept
Wavelength shifters (WLS)
Light concentration
Features
Better UV sensitivity
  requires quartz housing
Large collection area
  easily scalable
Low noise rate (few Hz)
  due to small PMTs
Cost effective
Length: ~1.2 m Diameter: ~10 cm
PoS(ICRC2017)1052

## Slide 18: WOM: Efficiency
Efficiency to capture photons and transport them to the end of the tube
WLS paint: Bis-MSB + p-Terphenyl in Paraloid B-72
(convoluted with Cherenkov spectrum)
Wavelength (nm)

## Slide 19: WOM Status

## Slide 20: Summary
The IceCube-Gen2 facility will be nearly 10× larger than IceCube alone
  The IceCube Upgrade can be used as a R&D platform for IceCube-Gen2
New sensor designs can improve the sensitivity
Physics potential only starting to be explored
Currently in R&D phase: multiple approaches being evaluated
  sensors with segmented photocathode to improve directionality
  wavelength-shifting sensors to increase UV sensitivity

## Slide 21: Backup Slides

## Slide 22: Construction: Drill Site
Drill camp (5 MW hot water heater)
Hot water hoses
Hose Reel
IceTop Tanks
(with sun shields)
Drill speed ~2 m/minute
~40 hours to drill a hole
~12 hours to deploy a string

## Slide 23: The IceCube DOM: Block Diagram
NIM A 601 (2009) 294

## Slide 24: Antarctic Ice
IceCube construction yielded a wealth of data on the optical properties of ice
  Absorption length for Cherenkov light is large
Instrumented length can be extended above and below current volume
  25% gain in instrumented volume
arXiv:1412.5106 [astro-ph.HE]

## Slide 25: IceCube-Gen2 High Energy Array
Current benchmark detector design:
  Add 122 strings around the IceCube instrumented volume (240 m spacing)
  80 standard IceCube DOMs / string
  “Sunflower” geometry avoids corridors in geometry
Spacing: 240 m
Volume: 8.0 km3
Skiway
arXiv:1412.5106 [astro-ph.HE]

## Slide 26: Improved IceCube DOM (PDOM)
Keeps well-proven mechanical components of the IceCube DOM
Redesign of electronics utilizing modern technologies
10-inch HQE PMT
PoS(ICRC2015)1148
IceCube DOM
PDOM
PDOM Prototype

## Slide 27: D-Egg: Dual Optical Sensor in an Ellipsoid Glass for Gen2
2 × 8-inch HQE PMTs (e.g. Hamamatsu R5912-100)
  4π sensitivity
  coincidence
UV-transparent glass and gel
  more photons
Compact design
  ⌀: 300 mm
  reduces drilling cost
PoS(ICRC2015)1137
PoS(ICRC2017)1051

## Slide 28: KM3NeT Multi-PMT DOM: In-Situ Measurements
KM3NeT Coll.,
EPJ C 74 (2014) 3056
Number of PMTs hit on single DOM already allows isolation of muon sample
Occupancy reasonably well described by Monte Carlo

## Slide 29: Segmented OMs and Scattering in Ice
arXiv:1401.2046v2 [physics.ins-det]
Photons from bare muon
Direct, unscattered light
Photons sneaking in from the opposite direction

## Slide 30: mDOM Multi-ToT Readout: Block Diagram
Mainboard
PMT Base
serial DAC HV ctrl
serial DAC n thresholds
FPGA
HV supply
Amplifier
Power
Comms
No clock on PMT bases.
Time-stamping of leading and trailing edge time in FPGA.
(f)ADC
multi-ToT
24×
Discriminator
n×

## Slide 31: mDOM: PMT Options
Target gain: 5 × 106
Hamamatsu R12199-02 HA
  diameter 80 mm (cathode > 72 mm)
  TTS (FWHM) ≈ 4.5 ns
  max. QE: 25% @ 390 nm
  also available with SBA photocathode or in a 5 mm shorter version (R12199-01)
ETEL 9320 KFL
  diameter 88 mm (cathode 78 mm)
  TTS (FWHM) ≈ 4.5 ns
  max. QE: 30%
Potential other manufacturers: HZC, MELZ

## Slide 32: mDOM: Hamamatsu R12199-02 HA SBA
SBA photocathode, otherwise identical to R12199-02
peak QE 40%
dark rate measured for bare PMT
threshold 0.3 p.e.
≈ 60 Hz @ −30℃ (R12199-02: ≈ 40 Hz @ −30℃)
AG Kappes, U Münster
AG Kappes, U Münster

## Slide 33: Hamamatsu R12199-02 SBA: Afterpulsing
AG Kappes, U Münster
AG Kappes, U Münster

## Slide 34: Waveform Reconstruction with 63 Discriminators
Encouraging first results
  Input: 10 pulses, mean amplitude 3 p.e.
  ΔCharge < 1%
  Δt (first pulse) ≲ 1 ns
True pulse times vs. reconstructed
A. Kappes (U Münster)

## Slide 35: Optical Properties of South Pole Ice
WOM sensitive between 250 nm and 400 nm
Optical properties not very well known in the UV range
Experimental in-situ verification of models required
WOM
J. Geophys. Res. 111 (2006) D13203