## Slide 1
J. Teichert, A. Arnold, M. Bawatna,
P. Evtushenko, M. Gensch, B. Green,
S. Kovalev, U. Lehnert, P. Lu, P. Michel,
P. Murcek, H. Vennekate, I. Will, R. Xiang
THz User Operation with Short and High Charge Bunches
Driven by the ELBE SRF Gun
4th Annual MT Meeting, 12 – 14 June 2018, HZB Berlin

## Slide 2
OUTLINE
Introduction
Mg Photocathodes
Gun Parameters, Beam Transport and Short Pulses
THz Results
Summary

## Slide 3
New cavity - fine grain Nb,
produced, treated,
tested at JLab
Integration of a superconducting solenoid
1. Introduction - ELBE SRF Gun II
RRR 300
Nb cavity
large grain
Nb cavity

## Slide 4
retracted cathode for RF focusing
1.3 mm (adjustable ± 0.5 mm)
z
70%
 | CW RF measured 2014 | with CW beam at present
acceleration field | 10 MV/m | 8 MV/m
peak field on axis | 25.6 MV/m | 20.5 MV/m
cathode field | 15.4 MV/m | 14.4 MV/m
kinetic energy |  | 4 MeV
On-axis field profile (calculated with SUPERFISH)
Mg #214
1. Introduction - Cavity status
Berkeley VHF gun
186 MHz
20 MV/m cathode field
750 keV
100 kW HF power

## Slide 5
1. Introduction – ELBE User Facility
continuous wave operation (CW)
higher bunch charge
lower transverse emittance
short pulses
Advantages of SRF Gun II:
Beginning operation for users at ELBE in 2018:
with 200 pC1) and 100 kHz pulse rate:
THz production TELBE: >4 times higher THz power
neutron production nELBE: 2 times more neutrons
1) the previously used thermionic injector has a maximum of 80 pC
most important !

## Slide 6
cathode
Anode
window
transport chamber
Laser cleaning set-up at transport chamber
at SRF gun
using the UV drive laser (100 mW, 100 kHz CW)
laser ablation
Laser cleaning set-up - PC in transport chamber
2. Mg Photocathodes
Notes: - Transportkammer mit Platz für sechs Photokathoden,
- Quarzglas-Eintrittsfenster für den UV-Laserstrahl,
- HV-Durchführung zur ringförmigen Anode,
- Linse mit f = 250 mm,
- Eintrittsblende,
- Wellenplatte zur einstellbaren Drehung der Polarisationsrichtung,
- Polarisator,
- Fokussierlinse mit f = 200 mm,
- Mikrometertisch zum Positionieren der Fokussierlinse,
- Kippspiegel mit Schrittmotoren,
- Klappspiegel,
- Schneidkanten-Schlitzblende,
- Leistungsmesser

## Slide 7
2. Mg Photocathodes
Mg #214
Mg cathodes work routinely in gun
prepared by UV laser cleaning (drive laser)
best QE 0.3 %
low risk of cavity contamination
extremely long life time in 10-9 mbar vacuum
cleaning can be several times repeated

## Slide 8
3. 1. Gun parameters
In ELBE: pc> 40 MeV
4.5 MeV plus
all cavities on crest

## Slide 9
4. Gun performance
operational stability: 12 h shift, beam from cathode to dump in diagnostic beamline
12 h night shift
Idump= 20 µA
σrms= 0.2 µA
200 pC CW @ 100 kHz, 7 MV/m (Ekin= 3.5 MeV)
with current stabilization – compensation of long-term drifts
Cathode current -> NI cRIO -> laser polarizer
beamdump current

## Slide 10
acceleration
on-crest
energy
correlation
compression
form factor Gaussian pulses
undulator
radiation
Simulation
with long laser pulse with short laser pulse
8.3 ps rms 3.0 ps rms
ΔE [keV]
ΔE [keV]
t [ps]
t [ps]
σt (rms) = 0.82 ps
σt (rms) = 0.18 ps
3. 3. Short pulses
Coherent diffraction and undulator radiation (superradiant)

## Slide 11
4. THz Results
Successful experimental realization of the bunch compression schema
Optimization parameters
correlated energy spread: phases of cavities C3 & C4
chicane angle (dipole currents)
Compression and longit. space charge compensation: SRF gun laser phase
bunch charge dependancy
bunch chirp dependancy

## Slide 12
4. THz Results
THz radiation has produced and characterized for 0.3, 0.5, 0.8, 1.0 and 1.5 THz
better pulse energy stability

## Slide 13
THz Power | 0.3 THz tuning | 0.5 THz tuning | 0.8 THz tuning | 1.0 THz tuning | 1.5 THz tuning
20 % bandwidth | 77 mW | 215 mW | 145 mW | 150 mW- | 80 mW
total power | 480 mW | 600 mW | 480 mW | 350 mW | 320 mW
Results for 16 - 20 µA CW beam (160-200 pC) with SRF Gun
example values for thermionic injector @ 80 pC :
total power 117 mW 90 mW 140 mW 110 mW
4. THz Results

## Slide 14
4. THz Results
600 mW
@ 0.5 THz
In 2018
14 Shifts ARD/AP for THz production,
optimization, and measurements
3 Shifts for TELBE in March with successful
user experiment

## Slide 15
Mg PCs with 0.3 % QE are robust and safe for SRF guns.
The ELBE SRF Gun II operates with 8 MV/m (20.5 MV/m peak) and delivers 300 pC at Ekin = 4 MeV in CW.
Injector operation for ELBE has been demonstrated.
For 2018 application for user operation with 200 pC,
successful THz production with >4 times higher THz power,
and better pulse stability
Starting with full TELBE user beam time in run III + IV
Further important activities:
- SRF Gun III with higher gradient ->higher charge
- Photocathodes (Cs2Te, GaAs, GaN) & Cryomodule
within ARD SRF Gun Cluster
5. Summary

## Slide 16
Acknowledgements
Thank you for your attention!
Thanks to the ELBE team
A. Arnold, P. Zwartek, P. Lu, P. Murcek, H. Vennekate, R. Xiang, H. Büttig, P. Evtushenko, M. Freitag, M. Justus, M. Kuntzsch, U. Lehnert, P. Michel, C. Schneider, R. Steinbrück, K. Zenker,
and our co-workers
P. Kneisel, G. Ciovati JLAB, Newport News, USA
I. Will MBI, Berlin, Germany
T. Kamps, J. Kühn, M. Schenck, M. Schmeißer, G. Klemz,
J. Voelker, E. Panofski, HZB, Berlin, Germany
J. Sekutowicz, E. Vogel, F. Stephan, DESY, Germany
K. Aulenbacher, JGU, Mainz, Germany
M. Vogel, M. Schuhmacher, X. Jiang, Uni Siegen, Germany
R. Nietubyć NCBJ, Świerk/Otwock, Poland
U. van Rienen, E. T. Tulu, Uni Rostock, Germany