## Slide 1
Matter and Technologies 4. annual meeting 13.06.2018
Georgios Kourkafas, Thorsten Kamps, Guido Klemz, Julius Kühn, Axel Neumann, Martin Schmeißer, Jens Völker and the bERLinPro team
Commissioning results of the HZB SRF Gun for bERLinPro with a Cu cathode

## Slide 2: Overview of components & measurements
Laser
Cathode
Gun
e- diagnostics
  power, spot size & pulse duration
  cathode position
  QE scan & map
  Shottky scan
  dark current
  DC-bias scan
  RF gradient
  phase scan for momentum (spread) + beam size

## Slide 3: Timeline & incidents
Measurements timeline:
  First RF without cathode: 18–24.08.17
  1st cathode insertion (inner cathode position): 13.09.17
  Cathode removal, helium processing: 14–15.12.17
  2nd cathode insertion (outer cathode position): 19.12.17
  laser on: 22.12.17 – 15.01.18
Uncertain: RF calibration, solenoid strength, cathode position and cooling…
dark current measured
- solenoid short-circuit observed, - beam-profile monitor broke, - cavity accidentally vented
e- beam measurements
test of coldbox
DC-bias on
cathode warming frequency change
~ 0.7 mm
~ 0.7 mm
Courtesy: G. Klemz et. al

## Slide 4: Dark current summary
  First RF without cathode
  1st cathode insertion (inner cathode position + equipment failures)
  Cathode out & helium processing
  2nd cathode insertion (outer cathode position)
  e- beam operation (PLL + LLRF)
Chart: Dark current
| 9.0500000000000007 | 9.0500000000000007 | 8.35 | 7.77 | 7.263070055520684 | 6.7747122635719892 | 9.5808899643188372 | 9.2727417910944965 | 7.9941750058918073 | 8.1738418211305497 | 8.5558385631886082 | 8.790288507676971 | 9.7313055958808974 | 9.8204491880792002 | 9.9380635502735366 | 10.083152444613388 | 10.34
Dark current [nA] | 422.9712 | 351.5446 | 162.7587 | 60.6618 | 17.2341 | 3.5947 | 638.752 | 488.4198 | 94.5428 | 125.0107 | 214.8368 | 291.2644 | 673.2735 | 725.4471 | 798.7583 | 889.7265 | 1230.5377
Chart: Dark current
| 7.14
Dark current [nA] | 41.4473
Chart: Dark current
| 13.7 | 14.46 | 14.76 | 14.05 | 13.2
Dark current [nA] | 27 | 37 | 45 | 30 | 13
Chart: Dark current
| 5.9 | 6.5 | 7 | 7 | 7 | 7.52 | 7.52 | 7.99 | 8.52 | 9.02
Dark current [nA] | 1.2151 | 2.4378 | 13.5196 | 8.6689 | 8.4455 | 25.0848 | 33.7998 | 76.9677 | 124.6247 | 214.228
Chart: Dark current
| 7.99 | 7.11 | 7 | 7 | 7
Dark current [nA] | 22.4716 | 1.9991 | 14.5534 | 5.0009 | 3.6002
Chart: Dark current
| 7 | 8.5 | 7 | 7.5 | 6 | 6.2 | 5.9 | 5.4 | 5.8 | 6.2 | 6 | 6.2
Dark current [nA] | 4.9491 | 121.7979 | 4.806 | 20.0023 | 0.1609 | 0.16668 | 0.033096 | 0.0078256 | 0.083653 | 0.4121 | 0.1823 | 0.18667
deviation above 8 MV/m due to DC bias / cathode?
measuring different emitters which overlap above 7 MV/m ?

## Slide 5: Laser parameters
Power meter:
  After a cold-start ~10 minutes for stabilization
  Short-term fluctuation: +/- 0.3 % rms, +/- 1.5 % max
  Long-term drift: +/- 1.2 % rms, +/- 2.8 % max
Pulse duration (optical auto-correlator):
  long-term drift: ~ 4 h to stabilize to 0.6 ps rms (UV)
Transverse parameters: “virtual cathode” + front camera

## Slide 6: Quantum Efficiency maps
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
12.01 | 6.0 | +60 | n/a | -2 | -0.40
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
12.01 | 6.0 | +60 | n/a | -2 | -0.40
15.01 | 7.0 | +50 | n/a | -2 | -0.36
Laser: 1.75 mm diameter, 12.1 kHz rep rate

## Slide 7: Quantum Efficiency scans
In agreement with Cu measurements from other photo-injectors
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
12.01 | 6.0 | +40 | n/a | -2 | -0.40

## Slide 8: Photoemission scans
Date | Peak field (MV/m) | Laser power (mW) | DC bias (kV)
09.01 | 6.2 | 0.63 | -5
Date | Peak field (MV/m) | Laser power (mW) | DC bias (kV)
09.01 | 6.2 | 0.63 | -5
10.01 | 5.4 - 6.2 | 0.47 - 0.51 | -2
Date | Peak field (MV/m) | Laser power (mW) | DC bias (kV)
09.01 | 6.2 | 0.63 | -5
10.01 | 5.4 - 6.2 | 0.47 - 0.51 | -2
12.01 | 6.0 | 0.72 | -2

## Slide 9: Momentum scans

## Slide 10: Simulating the measured momentum
ASTRA indicates +35% peak RF field
Courtesy: J. Voelker
ASTRA 10.2 MV/m
Measurement 7.5 MV/m
ASTRA 7.3 MV/m
Measurement 5.4 MV/m

## Slide 11: Simulating the measured beam size
ASTRA indicates -25% solenoid strength
Courtesy: J. Voelker

## Slide 12: Summary & Outlook
Valuable experience and data from the commissioning of the SRF injector for bERLinPro with a Cu cathode:
  Laser performance
  Cathode position and DC-bias
  Gun performance & RF parameters
  Measurement procedures, diagnostics, controls, …
Consistent beam dynamics simulations – further analysis for (field) emission with DC-bias
Ongoing tests and improvements regarding:
  Cryo distribution system
  Cathode cooling
  Solenoid
Next goal: operation with CsK2Sb cathode at bERLinPro with an online simulation tool for live feedback

## Slide 13: THANK YOU FOR YOUR ATTENTION

## Slide 14
Variable Gun Parameter in ASTRA simulations:
-> Cathode position inside the cavity
-> DC Bias voltage for the cathode insert
-> RF gradient in the the cavity
-> field flatness between the gun cells
-> solenoid postion
-> solenoid strength
field calculation:
-> calculating RF and DC fields of the gun as function of the cathode position
-> field flatness (FF) is calculated by ASTRA
Start with energy calibration:
-> find cathode positions and FF values to describe both
measurements simultaneously , RF gradient free parameter
check transverse beam optics:
-> variate solenoid position and strength to achieve the same
beam sizes (as function of the phase) at FOM2 like the measurements

## Slide 15
energy calibration -> only for cathode positions of -1.7mm for both measurements
the same FF (FF-0.2) can be found to describe both distributions

## Slide 16
find the minimal parameter setting with the smallest for both measurements:

## Slide 17
LLRF (measurements) | final ASTRA field (main cell) | final ASTRA field (half cell) | final ASTRA field (cathode)
7.5MV/m | 9.433 MV/m | 10.177MV/m | 7.29MV/m
5.4MV/m | 6.721 MV/m | 7.251MV/m | 5.195MV/m
DC Bias voltage of 2kV results in an additional electric field on the
cathode surface of 0.413 MV/m

## Slide 18: Laser
UV & green wavelengths delivered
Controlled & measured beam parameters
  Spot size, location & shape (motorized position & aperture, “virtual cathode”)
  Pulse energy (λ/2-plate, power meter)
  Pulse duration (pulse stretcher, optical auto-correlator)
Cathode position monitoring
  x3 capacitive sensors (relative measurement, 4 mm range, µm precision)  useful during cathode transfer, cool-down, RF-induced heating
  optical system (visual inspection + absolute position measurement wrt cavity wall, ~ 0.5 mm precision)  useful during cathode transfer, with system-related difficulties…
Courtesy: G. Klemz et. al
692 mm
Distance [mm]
Time [hh:mm]
Insert retracted
Insert in Gun

## Slide 19: Dark current
Data not always measured with same machine settings:
Chart: Dark current @ 6.2 MV/m with -0.36 A solenoid
| -5 | -9.544828977272725E-4 | -0.50032335000000006 | -1.0003641666666669 | -1.500451573033708 | -2.0004293333333329 | -2.5003514782608689 | -3.0004217525773207 | -3.5004219780219796 | -4.0004453846153831 | -4.5003375342465732 | -5.0003060277778024
Dark current [nA] | 3.6622 | 0.15593 | 0.16104 | 0.16534 | 0.17681 | 0.18667 | 0.23173 | 0.31496 | 0.50866 | 0.92039 | 1.8517 | 3.718
  Solenoid
  DC bias
  Statistics
  Steerers (emitters)
  RF feed (PLL / Cornell LLRF)

## Slide 20: Momentum scans
Date | Peak on-axis field (MV/m) | Max momentum [MeV/c] | DC bias (kV) | Solenoid (A)
27.12 | 7.1 | 1.01 | -2 | -0.35
09.01 | 6.2 | 0.96 | -2 | -0.36
10.01 | 5.4 | 0.74 | -2 | -0.40
12.01 | 7.5 | 1.17 | -2 | -0.40
Chart: Maximum measured momentum vs. RF gradient
| 7.5 | 5.4 | 6.2 | 7.11
Momentum [MeV/c] | 1.17 | 0.74 | 0.96 | 1.01

## Slide 21: Cathode: -0.7 mm from warm cavity backwall
Courtesy: G. Klemz et. al
Cathode was retracted to -0.7 mm behind the cavity backwall at the warm state

## Slide 22: Cathode: -1.7 mm from cold cavity backwall
Cavity shrinks by ~1 mm away from the cathode holder after cool-down
Courtesy: G. Klemz et. al

## Slide 23: Quantum Efficiency maps
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
12.01 | 6.0 | +60 | n/a | -2 | -0.40
Date | Peak on-axis field (MV/m) | Relative RF phase (deg) | Momentum (MeV/c) | DC bias (kV) | Solenoid (A)
09.01 | 6.2 | +25 | 0.94 | -2 | -0.36
12.01 | 6.0 | +60 | n/a | -2 | -0.40
15.01 | 7.0 | +50 | n/a | -2 | -0.36
Laser: 1.75 mm diameter, 12.1 kHz rep rate
In agreement with Cu measurements from other photo-injectors

## Slide 24: Laser power
After a cold-start ~10 minutes required for stabilization
Short-term fluctuation (noise around 10 min. average): +/- 0.3 % rms +/- 1.5 % max
Long-term drift: +/- 1.2 % rms +/- 2.8 % max
Time (h)
Noise (mW)
Power (mW)
Courtesy: G. Klemz et. al

## Slide 25: Laser
Long-term drift: takes 4 h to stabilize to to ~2.1 ps FWHM (green light) => 1.5 ps FWHM (UV) => 0.6 ps RMS (UV)
Not archived during measurements

## Slide 26
transverse beam optics:
-> no simulation results were found with solenoid currents of
0.4Amp (as used in the measurements)
-> variable solenoid position and current to find the best values:
-> estimated solenoid position: 0.458 m from cathode (0.45m in simulation)
-> defined solenoid current in measurement: 0.4A, (0.3A in simulation)