## Slide 1: Applications of the Interferometric Beam Size Monitor at the BESSY II Storage Ring
Marten Koopmans
4th MT student retreat Berlin, 11th – 12th June 2018

## Slide 2: Content
  Introduction
  Interferometric Beam Size Monitor
    Theory
    Setup
    Measurements
  Summary
Notes: 2

## Slide 3: Introduction: BESSY VSR Upgrade
VSR upgrade of the BESSY II storage ring
  Variable pulse length Storage Ring
  VSR Fill Pattern of different bunch types, in length, current, transverse beam size
  Single and coupled bunch instabilities
  Bunch resolved diagnostics needed
A. Jankowiak et al., eds., “BESSY VSR - Technical Design Study”, Helmholtz-Zentrum Berlin für Materialien und Energie GmbH, Germany, June 2015. DOI: 10.5442/R0001
BESSY II Parameters | 
Energy | 1.7 GeV
Circumference | 240 m
Bending Radius | 4.35 m
Horizontal emittance | 5 nm rad
Max. Beam current | 300 mA
RF frequency | 500 MHz
max. RF voltage | 2 MV
Bunch length low- | 15 ps 2 ps
Mom. Comp. factor low- | 7.5 10-4 3.5 10-5
BESSY II Parameters | 
Energy | 1.7 GeV
Circumference | 240 m
Bending Radius | 4.35 m
Horizontal emittance | 5 nm rad
Max. Beam current | 300 mA
RF frequency | 500 MHz
max. RF voltage | 2 MV
 | 15 ps 2 ps
Notes: 3

## Slide 4: Bunch Resolved Measurements
  Present BESSY II Pinhole System
    Direct imaging only with X-rays
    Not very flexible system, long averaging
    Bunch resolved measurements difficult
  System using visible light
    Problem: higher resolution limit (few 100 µm) interferometry
  Interferometric beam size monitor
  Well understood, efficient technique
  Flexible
  Uses visible light Gateable
  Upgrade to bunch resolved system possible
Notes: 4

## Slide 5: Interferometric Beam Size Monitor

## Slide 6: Theory: Interference and Visibility
Interference pattern of double slit interferometer:
Interference pattern of double slit interferometer:
Visibility from coherence theory:
Where is the spatial coherence
1
0.6
Point source
Broad source
T. Mitsuhashi, ''Beam Profile and Size Measurement by SR Interferometer'‘, in: Beam measurement, Ed. by S. Kurokawa et al., pp. 399 – 427, World Scientific 1999.

## Slide 7: Theory: Beam Size from Interference
Interference pattern of double slit interferometer:
Visibility from coherence theory:
is given by Fourier Transform of the source (van Cittert-Zernike)
Gaussian beam, uniform slit illumination:
Beam size (rms) can then be calculated:
Method works in both transversal dimensions ()
– slit width
– slit separation
– distance camera to slit
– distance slit to source
– intensity at slit
– position on screen
– offset from
– wavelength
– phase
Notes: 7

## Slide 8: Setup at Diagnostics Beamline
Notes: 8

## Slide 9: Measurement Range
Parameter Ranges
  Double slit separation 7.5 mm to 25 mm
  Wavelength 400 nm to 800 nm
  Distance to source 16.1 m (fixed)
  Visibility Range 0.3 to 0.9
Statistical Errors (assuming 0.005):
Parameter | Range | Uncertainty | Relative beam size error
/ m | 16.09 | 0.84 | 5.2 %
/ mm | 7.5 – 25 | 0.1 | 1.3 – 0.4 %
/ nm | 400 – 800 | 1.6 | 0.4 – 0.2 %
 | 0.9 | 0.005 | 0.7 %
 | 0.3 | 0.005 | 2.6 %
Parameter | Range | Uncertainty | Relative beam size error
 | 16.09 | 0.84 | 5.2 %
 | 7.5 – 25 | 0.1 | 1.3 – 0.4 %
 | 400 – 800 | 1.6 | 0.4 – 0.2 %
 | 0.9 | 0.005 | 0.7 %
 | 0.3 | 0.005 | 2.6 %
(18.8 1.1) µm
(424 23) µm

## Slide 10: Live Beam Size Measurement
Python tool for online analysis
  Using EPICS environment from BESSY II
  Data archiving possible
Fitting:
Notes: 10

## Slide 11: Beam Size Measurement with Slit Separation Scan
Standard user operation, 250 mA
Interferometer: 400 nm
 | Horizontal / µm | Vertical / µm
-Polarisation | 54.32.9 | 49.52.6
-Polarisation | 53.82.8 | 49.82.7
 | Horizontal / µm | Vertical / µm

## Slide 12: Compare Std. User Measurements
Compare results from slit separation scans with pinhole systems and results from model (emittance std. user ~5 nm rad)
Similar beam sizes expected
Measured values higher than model (all systems)
Std. User | PINH3 / µm | Interferometer / µm | PINH9/ µm
Ver. | 84.4 | 49.52.6 | 51.3
Hor. | 75.0 | 54.32.9 | 65.9
Hor. Model | 44.5 | 44.2 | 48.1
Std. User | PINH3 / µm | Interferometer / µm | PINH9/ µm
Ver. | 84.4 |  | 51.3
Hor. | 75.0 |  | 65.9
Hor. Model | 44.5 | 44.2 | 48.1

## Slide 13: Measurements: Energy Ramp
Measuring horizontal beam size while ramping storage ring energy
Pinhole systems not designed for lower energy (16 keV)
Ramp down to 600 MeV
Measurement parameter: 25 mm, 550 nm
Current dependent beam instability for lower energies
Linear behavior (~0.0405 µm/MeV)
Notes: 13

## Slide 14: Beam Profile Measurements
Rotation of camera and double slit
  Theory:
  Rotary mounts for camera and double slit

## Slide 15: Beam Profile Measurements
Rotation of camera and double slit
  Theory:
  Rotary mounts for camera and double slit
Standard user mode

## Slide 16: Beam Profile Measurements
Rotation of camera and double slit
  Theory:
  Rotary mounts for camera and double slit
Low- mode

## Slide 17: Summary and Outlook
Successfully designed, installed interferometric beam size monitor
  Beam sizes measured from 30 to 250 µm with ~5% uncertainty
  Various applications for diagnostics and commissioning
Problem with extraction mirror, polarisation effects and vibrations limited resolution of system
Move to new beamline, upgrade setup (e.g. proper covering, …)
Future upgrade of system with fast ICCD camera or photodiode array for bunch resolved measurements
Notes: 17

## Slide 18: Thank you for your attention!