## Slide 1: Industrial Applications in compact-ERL at KEK - EUV light source for semiconductor lithography, 99Mo production for medical application, and Non-destructive inspection for nuclear security system-
Hiroshi KAWATA
(KEK, Japan)
Hiroshi KAWATA
(KEK, Japan)
Hiroshi SAKAI
(KEK, Japan)

## Slide 2: Contents
History of ERL Project in KEK: (CW super conductive accelerator)
KEK Project Implementation Plan (KEK-PIP)
industrial applications
  EUV-FEL for Future Lithography
  RI manufacturing facility for nuclear medical examination
  High resolution X-ray imaging device for medical use
  Nuclear security system
Summary

## Slide 3: History of ERL project in KEK
Fiscal Year
2005 Institute of Materials Structure Science in KEK decided to start the R&D of 5GeV ERL light source as a future light.
2006 Establishment of ERL Project Office in KEK
2007 The CDR on Compact ERL (cERL) was published
2008 The construction of the infra structure started.
2013 The construction of the cERL was completed and the commissioning of the ERL operation started. (0.01 mA)
2015 The commissioning of the cERL (1mA), bunch compression and high bunch charge operation (7.7pC/ bunch).
2016 The future light source was shifted to the ring-based accelerator, so that there is no back ground to continue the ERL R&D.
2017 ERL project Office was closed in KEK and “Utilization Promotion Team based on Superconductive Accelerator” was in KEK in order to find industrial applications based on superconductive accelerator.

## Slide 4: KEK Project Implementation Plan (KEK-PIP)
http://www.kek.jp/ja/NewsRoom/Release/20160802141100/
3-2. Other research projects carried out using general funds of KEK
The following projects have up to now been conducted mainly using general funds of KEK. They will be continued on the condition that greater efforts are made to obtain external funding.
▪ Simulation studies with the existing supercomputer (only up to summer of 2017)
▪ Industrial application of ERL technology
▪

## Slide 5
The Compact ERL (cERL)
Photocathode DC gun (JAEA)
The cERL contains all important technologies.
Injector cryomodule
Main-linac cryomodule
Beam dump
Recirculation loop
Injector diagnostic beamline
Merger
Dump chicane
The first arc
The second arc
Circumference: ~ 90 m
©Rey.Hori/KEK

## Slide 6
6
Picture of the cERL
Photocathode DC gun
Injector cryomodule
Main-linac cryomodule
Recirculation loop
Injector diagnostic beamline

## Slide 7
7
Construction and Commissioning of cERL
2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Refurbishment
of building
Clearing radioactive
materials
Construction of
radiation shielding
Commissioning of injector
Commissioning of cERL (with loop)
Commissioning/Operation
Construction
Construction of recirculation loop
Increasing the beam current
Commissioning of LCS system
Construction of
injector
Construction of LCS system
High bunch charge
R&D for Industrial application

## Slide 8: Back Ground
Super conducting accelerator gives us high current linac-based electron beam (~10mA) with high quality of the electron beam such as small emittance, Short pulses.
The unique performance gives us several important industrial applications as follows.
  EUV-FEL for Future Lithography
  RI manufacturing facility for nuclear medical examination
  High resolution X-ray imaging device for medical use
  Nuclear security system

## Slide 9: 1. EUV-FEL for Lithography (Back ground)
Technology node trend of Logic LSI and expected power on EUV light source

## Slide 10: Present Status and Future Development on EUV Lithography
Present Status
The technologies on EUV Lithography system based on LPP light source are progressing, now.
The system based on ~200 W LPP light source is starting point of the production phase.
Future Development
It is expected that these on ~1kW source will be necessary to realize the production less than 3nm node, too.
It is important to develop new type light source to realize higher power than ~1kW.

## Slide 11: Prototype design of the EUV-FEL
Fig. 2 Prototype design of the EUV-FEL
High Power EUV-FEL Light

## Slide 12: FEL Performance
e-
<gb>=1561.1
st=48.5 fs
sp/p=0.299 %
enx=1.98 mm·mrad
eny=0.71 mm·mrad
PFEL > 10 kW is achieved.
(PFEL=84 mJ x 162.5 MHz =13.7 kW, Iav=60pC x 162.5 MHz=9.75 mA)
FEL power without tapering: 12.9/25.8 kW @ 9.75/19.5 mA (162.5/325 MHz)
FEL power with 2% tapering: 14.4/28.8 kW @ 9.75/19.5 mA (162.5/325 MHz)
79.5 mJ
88.5mJ
<gb>=1561.1
st=48.5 fs
sp/p=0.299 %
enx=1.98 mm·mrad
eny=0.71 mm·mrad
Energy spread is increased.
BY N. Nakamura

## Slide 13: Rough estimation of the FEL radiation power
 | LCLS | SACLA | FLASH | Euro-XFEL | LCLSII | EUV-FEL
Type of linac | Normal conducting |  | Super conducting |  |  | 
Operation mode | Pulse |  | Long pulse |  | CW | 
Country | US | Japan | Germany | Germany | US | -------
ERL scheme | No | No | No | No | No | Yes
Repetition rate | 120 | 30～60 | <5000 | <27000 | 1M | 162.5M
Accelerate Energy （MeV) | 14300 | 6000～8000 | 1250 | 17500 | 4000 | 800 0.01@Injection
Minimum wave length (nm) | 0.15 | 0.08 | 4.2-52 | 0.05 | ~0.3 | 13.5
Power/pulse (mJ) | ~10 | ~10 | <0.5 | ~10 | ~1 | ~0.1
Power/s （W) | ~1 | ~1 | <0.6 | ~100 | ~1000 | >10000
Beam dump power （W) | ~1.5k | ~0.5k | ~6k | ~0.5M | ~1M | ~0.1M
Operation/ Construction/ Planning | Operation 2009 | Operation 2011 | Operation 2004 | Start the commissioning 2017 | Construction 2020 | Planning

## Slide 14: Expected LSI Fab based EUV-FEL

## Slide 15: EUV-FEL Light Source Study Group for Industrialization
Industrialization of High Power EUV light source based on ERL@KEK and FEL@QST
S. Ishihara (Leader)
H. Kawata et al.
R. Hajima
T. Kozawa
H. Kinoshita
M. Washio
Industries
N. Sei
I. Matsuda
Univ. of Hyogo
Waseda Univ.
Osaka Univ.
Utsunomiya Univ.
T. Higashiguchi
KEK

## Slide 16: 2nd EUV-FEL Workshop
Date: 12/ Dec. /2017 10:00-17:00
Site: Surugadai-kinenkan, Tokyo
Participants : 103 (Source group, tool & material venders, end users etc.)
http://pfwww.kek.jp/PEARL/EUV-FEL_Workshop2/program_eng.html
Invited Speakers
Michael Lercel (ASML)
"EUV industrialization for HVM and future outlook"
Tetsuya Ishikawa (RIKEN SPring-8 Center)
“Laser plasma amplification of SACLA XFEL
beam and its extension to EUV-FEL applications”
Masaharu Nishikino (QST)
“Research on the interaction of a SXFEL with
matter for EUV ultra-precision nano-fabrication”
Notes: We organized one-day workshop for EUV-FEL with source group, tool and material venders, and end users.

## Slide 17: Reduction of Source Size
Higher field gradient of Main SC cavities
  Increase of power consumption ∝ Eacc2/Q
  Development of High-Q SC cavity is essential.
Lower Beam Energy
  Shorter undulator period and stronger magnetic field
  Increase of current or energy conversion efficiency for the same FEL power
2-loop/2-turn ERL
  Optics design for CSR effect suppression
  Increase of current for the same FEL power

## Slide 18: SRF Challenges for Higher-Gradient
Key issue to achieve higher gradient in SRF cavities of CW operation is to suppress field emission caused by dust particles and so on.
Improvement for clean environments with dust free
Set-up of particle measurements in vacuum by using a vacuum particle counter
Test bench to confirm the higher gradient performance of SRF
Horizontal cryostat to improve particle contamination during assembly work

## Slide 19: SRF for Higher-Q
power consumption ∝ Eacc2/Q
One of essential factors to achieve higher Q values is to reduce a residual magnetic field around a cavity.
A solenoid coil for cancelling the residual magnetic field
1x 1010 2.5x 1010 @ 2K
Improvement of Q values from normal processing to nitrogen doping treatment
2.5x 1010 4x 1010 @ 2K
Preliminary DATA 2017

## Slide 20: Performance by Introducing Shorter Period Undulators (1)
The performance by introducing shorter period undulators; In-Vacuum Undulators (IVUs), Cryogenic Permanent Magnet Undulators (CPMUs)
Energy spread | 0.1 %
Charge | 60 pC/bunch
Bunch length | 100 fs
Peak current | 600 A
Average current | 9.75 mA
Normalized emittance (ex = ey) | 1.0  mm mrad
Beta func. (bx = by) | 5 m
Repetition | 162.5 MHz
Beam parameters assumed in the calculation
=u (1+K2/2)/2 2
Reduction of the accelerator energy

## Slide 21: Performance by Introducing Shorter Period Undulators (2)
FEL Output Power
PFEL= Pbeam
=1.6 r /(1+L)2
 : the one-dimensional FEL parameter,
L : the correction term due to the effect of an energy spread
Consequently, the introduction of the shorter period undulator gives us the reduction of the accelerator energy, however, the FEL output power also will be reduced.

## Slide 22: Double-Loop Configuration
Type A: Electron beam is accelerated twice by the same main-inac and the size can be reduced.
The total beam current in the main linac is doubly increased and it may make a problem caused by the higher-order-modes(HOMs).
Type B: Main-linac cavities are placed on both loop sides and the size can be reduced.
There is no problem of the HOMs like Type A.
Double number of main-linac cavities is required compared to the Type-A.
At the both cases, we have to carefully design the joint sections (Joint 1 and Joint2) to reduce the effect of CSR, which makes a damage of the electron quality and also arc sections (Arc 3, and Arc4) should be designed to be able to make bunch compression and decompression.

## Slide 23: Staging to realize the EUV-FEL light source for Lithography
EUV-FEL Prototype
Clean room with EUV exposure system
1st stage:
Development of the feasible technologies
2nd stage Phase 1:
Establishment of the EUV-FEL Lithography system
2nd stage Phase 2:
International Development Center on the processing of EUV-FEL lithography
cERL
kW-class Infrared FEL
EUV-FEL Prototype
The above concept should be important to realize the EUV-FEL high power light source for EUV Lithography.

## Slide 24
Concern about the stable supply of 99Mo / 99mTc
99Mo is almost 100% imported, even though the largest number of applications in nuclear medicine diagnosis
Problem of the stable air transportation
(Problem caused by volcanic eruption in the past)
Most 99 Mo is manufactured in nuclear reactor
Due to the aging of nuclear reactors, stable supply in the future is a big issue
A state of brain blood flow revealed by nuclear medicine diagnosis by 99 mTc
Development of RI manufacturing (99 Mo / 99 mTc) by using accelerator for stable supply
Required Specification
for accelerator
20 ~ 50 MeV electron beam
Several mA to 10 mA
2. RI manufacturing facility for
nuclear medical examination (99Mo/99mTc)
A few 10MeV Electron Beam
Bremsstrahlung
99Mo
Courtesy of K. Umemori

## Slide 25
Test Experiment to produce 99Mo in cERL is preparing
The test irradiation of electron beams to a multiple molybdenum target will be done at this fiscal year to produce 99Mo and check the yield of the production in order to realize a real machine with large electron beam power.
It is necessary to get several knowledge to design a target system for large irradiation power such as a practical technique for 99Mo production, target thermal design, shielding radiation design and legal procedures, etc. It is the final objective of this project.

## Slide 26: Mo99 Beamline Configuration (Under designing)
Mo 20MeV 10mA(maximum)
Asphalt BL
10MeV 10mA

## Slide 27: 3. High resolution X-ray imaging device for medical use From the view point of neurosurgery
Using a large synchrotron radiation facility
If we can make a compact high-resolution X-ray source in a hospital!
Potential of quasi-monochromatic X-rays for high resolution X-ray imaging by laser Compton scattering (LCS)
Laser Compton scattered X-ray source at ERL
LCS device
Quasi-monochromatic
X-rays for high resolution X-ray imaging
~6m
10m
Provided by the Department of
Neurosurgery, University of Tsukuba
Intravascular surgery of
neurosurgery
coil: Stuffed aneurysm and stop bleeding
Stent: Support stabilizing coil
Image under surgery
The stent can not be seen
High resolution
Stents can be clearly visualized
Courtesy of K. Hyodo

## Slide 28
3. High resolution X-ray imaging device for medical use Feasibility from the experimental result on cERL
Success of LCS at cERL (March/2014) (high resolution X-ray imaging)
(20MeV, 0.1 mA, 10kW laser Cavity)
http://www.kek.jp/ja/NewsRoom/Release/20150427150000/
Main issues for medical application
1) Too long exposure time
2) Too low Energy
X-ray Energy 7keV
Exposure time 600sec
X-ray Energy ~40 keV
Exposure time <0.1 sec
Result of March/2014
Starting point of medical application
(50MeV, 10 mA,
>100kW laser Cavity)

## Slide 29
4. Nuclear security system
(Non-destructive Detection and Measurement of Nuclear Material by Laser Compton Scattering Gamma Ray)
1) Deterrence of terrorism using nuclear material
2) Nuclear nonproliferation
· Confront terrorism with an international framework
(nuclear security summit)
· Border strategy to investigate the nuclear material is essential against nuclear terrorism.
Necessity of non-destructive detection and measurement
of nuclear material
· Melted fuel will be taken from Fukushima Nuclear Power plant from 2021
· Nuclear material measurement of melted fuel is essential
Courtesy of R. Hajima

## Slide 30
R. Hajima: ERL15

## Slide 31
R. Hajima: ERL15

## Slide 32: Summary
Super conducting accelerator gives us high current linac-based electron beam (~10mA) with high quality of the electron beam such as small emittance, Short pulses.
following important industrial applications are presented.
  EUV-FEL for Future Lithography
  RI manufacturing facility for nuclear medical examination
  High resolution X-ray imaging device for medical use
  Nuclear security system
The cost and size reductions at the accelerator system are also very important for industrial applications, so that the R&Ds for High Q and high temperature system of SRF are essential.