## Slide 1: The SRF Gun Project at SLAC
Bruce Dunham and Nora Norvell
With inputs from Theo Vecchione, and XJ Wang

## Slide 2
Motivation: We need a 3-4X reduction in emittance for the LCLS-II-HE project
Chart: Maximum Wavelength for 100 uJ
| 7 | 7.25 | 7.5 | 7.75 | 8 | 8.25 | 8.5 | 8.75 | 9
Nominal Emitt | 10.92 | 11.34 | 11.76 | 12.18 | 12.6 | 13.02 | 13.44 | 13.8075 | 14.175
75% Nominal Emitt | 12.6 | 13.23 | 13.86 | 14.4375 | 15.015 | 15.5925 | 16.17 | 16.7475 | 17.2725
50% Nominal emitt | 14.49 | 15.33 | 16.17 | 17.0625 | 17.9025 | 18.7425 | 19.5825 | 20.4225 | 21.2625
125% Nominal Emit | 9.45 | 9.765 | 10.1325 | 10.4475 | 10.71 | 11.025 | 11.2875 | 11.55 | 11.8125
Photon Energy (keV)
Electron Energy (GeV)
Emittance at Undulator
The emittance at the injector will need to be at least 4X lower than we can generate now to reach 20 keV (< 0.1 um needed)
LCLS-II Injector
Notes: You saw this figure earlier as part of the HE presentation, but it conveys the key point for this presentation
This plot shows the photon energy obtainable at 8 GeV for various emittances.
With the current LCLS-II injector, 12.8 keV at 8 GeV is predicted.
Lowering the beam emittance at the undulator provides harder x-rays
To reach 20 keV, need 0.1 um at the undulator, about 4X lower than we can do today
Developing a new injector to reach harder x-rays is much cheaper than doubling the linac energy or adding an SC undulator
Can imagine a staged approach, culminating in a new injector. Just changing the photocathode and laser may get us to the middle of the range

## Slide 3: Injector Requirements for future XFELs
The main goal for our injector R&D program is to develop an electron injector for future XFELs that enables the generation of x-rays > 20 keV at 8 GeV
The main requirements for the full injector are:
100 MeV beam energy
1 MHz repetition rate
eN =0.1 mm at 100 pC bunch charge (at the undulator)
eN <0.1 mm at 100 pC bunch charge (at the injector end)
ability to tailor the longitudinal phase space
photocathodes with a lifetime of at least 1 week
visible/IR drive laser preferred for enhanced laser shaping

## Slide 4: Recommissioning the 200 MHz ¼ Wave WiFEL Gun
Design parameters
45 MV/m gradient
4.0 MeV beam energy
1 um emittance @ 200 pC
Recommissioning goals
Validate hardware survived relocation
Replicate previous results
WiFEL system at Wisconsin
WiFEL system relocated at SLAC
Previously demonstrated performance
Q0 > 3e9
26 MV/m gradient w/o photocathode
12 MV/m gradient w/ Cu photocathode
1.1 MeV beam energy
0.7 μm emittance for 12 pC @ 1.1 MeV
1.5 μm emittance for 100 pC @ 1.1 MeV
Opportunity to demonstrate SRF gun technology for both LCLS-II HE and UED/UEM

## Slide 5: SLAC SRF Gun Design
Vacuum Vessel
Magnetic Shield
LN Shield
LHe Vessel
RF Cavity
Vacuum/Beam Pipe
RF Tuner
High TC Solenoid
RF Coupler
Photocathode Stalk

## Slide 6: SLAC SRF Gun Beamline Layout
Bend
Corrector
Corrector
Quadrupoles
Solenoid
Laser
beam
Faraday
Cup
Faraday
Cup
Profile
Monitor
Profile
Monitor
Profile
Monitor

## Slide 7: Six Months (and Several Safety Reviews) Later…
System Installed
~100 pC @ 1.1 MeV
& operating

## Slide 8: SLAC SRF Gun Project Team
Chris
Adolphsen
Bruce
Dunham
Keith
Jobe
Renkai
Li
Nora
Norvell
Tom
Peterson
John
Seabury
Theo
Vecchione
Xijie
Wang
Bob
Legg
Stephen
Weathersby

## Slide 9: Next Steps
We are applying for funds to purchase a 4K 100W closed-loop Helium System
Design and build a cathode load lock system
Replace the copper coating on the cathode tube
Fix the laser-RF synchronization
Add an accurate emittance measurement system