## Slide 1: TTC Hot Topic Common Questions
Hiroyuki Ao (FRIB), Marcelo Juni Ferreira (ESS), Hiroshi Imao (RIKEN) TTC Meeting at RIKEN, Wako, June 28, 2018

## Slide 2: Common Questions about Warm and Cold Transition (By R. Geng)
1. What is the design of warm beamline systems next to a cold SRF cryomodule? size (ID and length) and material of the beam pipe? type and capability of vacuum pumps? beam diagnostic instruments (such as BPM, wire scanner, beam viewer etc)? 2. What kind of gate valves are used to isolate the cavity string from the warm beamline system? fast valve or slow valve? under what conditions these valves are actuated? 3. Are NEG pumps used? if yes, how these pumps are activated? 4. What is the cleaning procedure for the warm beamline system? What is the QA/QC for the cleanliness/particulate count? 5. What kind of vacuum gauges are used for beamline vacuum monitoring? are they resistant to ionization radiation?

## Slide 3: Common Questions about Warm and Cold Transition (By R. Geng)
6. What kind of particulate monitoring has been done for controlling particulate generation and movement for individual components (pump, gate valve) and integrated warm beamline systems? 7. What have you learned from beam operation of SRF accelerators wrt particulate generation and movement and the impact to field emission characteristics? Cryo modules long term performance against warm section openings? or cryo-modules performances and specific beam instrumentations replacements?

## Slide 4
Answers

## Slide 5: cERL at KEK (by H. Sakai)
1. What is the design of warm beamline systems next to a cold SRF cryomodule? size (ID and length) and material of the beam pipe? type and capability of vacuum pumps? beam diagnostic instruments (such as BPM, wire scanner, beam viewer etc)? NEG coated chamber on SS-chamber was used. This diameter is 50mm-phi, length is about 1m. Screen monitor and BPM were set out of NEG coated chamber. 2. What kind of gate valves are used to isolate the cavity string from the warm beamline system? fast valve or slow valve? under what conditions these valves are actuated? Slow gate valve. It works when the one of CCG of all beam line increase 1*10^-5 Pa.

## Slide 6: cERL at KEK
3. Are NEG pumps used? if yes, how these pumps are activated? NEG coated chamber on SS-chamber was used. Activated by heater. 4. What is the cleaning procedure for the warm beamline system? What is the QA/QC for the cleanliness/particulate count? We made local clean boose beside the cryomodule and connected the NEG coated chamber. We believe that this clean boose is under ISO class 6. I think that this is not enough to keep perfectly clean. 5. What kind of vacuum gauges are used for beamline vacuum monitoring? are they resistant to ionization radiation? Cold Cathode Gauge (CCG).

## Slide 7: cERL at KEK
6. What kind of particulate monitoring has been dome for controlling particulate generation and movement for individual components (pump, gatevalve) and integrated warm beamline systems? No particulate monitoring system in the beam line up to now. We have radiation monitor beside the cryomodule to see the field emission increase.

## Slide 8: cERL at KEK
7. What have you learned from beam operation of SRF accelerators wrt particulate generation and movement and the impact to field emission characteristics? Cryo modules long term performance against warm section openings? or cryo-modules performances and specific beam instrumentations replacements? We saw the performance degradation during long-term beam operation under the beam operation. After opening the gate valve of warm section and after the 2 month beam operation, cavity performance degraded. Radiation monitor and PIN profile monitor is useful to monitor the field emission increase. And pulse processing by measuring the radiation of the radiation monitor and PIN profile monitor help the suppression field emission. We don't know why the degradation was occurred. But warm component such as GV, NEG-coated pump and/or outgassing come from the beam dump when the beam first hit the beam dump will make the cavity worse for long term beam operation. Details will be discussed elsewhere.

## Slide 9: FRIB at MSU (by H. Ao)
1. What is the design of warm beamline systems next to a cold SRF cryomodule? size (ID and length) and material of the beam pipe? type and capability of vacuum pumps? beam diagnostic instruments (such as BPM, wire scanner, beam viewer etc)? Beamline length ~3 m, inner diameter 40~47.5 mm, made of SUS. Entrance and exit of cryomodules are pumped down by a 75L/s ion pump, pressures achieved < 5E-9 Torr 2. What kind of gate valves are used to isolate the cavity string from the warm beamline system? fast valve or slow valve? under what conditions these valves are actuated?
Slow valve: Huntington GVAP-200-V, Pneumatic (threshold >5E-7 Torr) Fast valve: VAT Series 752 (threshold >2E-5 Torr)

## Slide 10: FRIB at MSU
3. Are NEG pumps used? if yes, how these pumps are activated? No NEG pumps in SRF regions 4. What is the cleaning procedure for the warm beamline system? What is the QA/QC for the cleanliness/particulate count? Warm (UHV) components also processed in cleanroom and installed with temporary plastic cover and filter unit
5. What kind of vacuum gauges are used for beamline vacuum monitoring? are they resistant to ionization radiation? Cold cathode gauge (Agilent IMG-300)

## Slide 11: FRIB at MSU
6. What kind of particulate monitoring has been dome for controlling particulate generation and movement for individual components (pump, gatevalve) and integrated warm beamline systems? Profile Monitor and FGV particle counts test were performed. Criteria are not verified experimentally (e.g. cavity vertical test)
7. What have you learned from beam operation of SRF accelerators wrt particulate generation and movement and the impact to field emission characteristics? Cryo modules long term performance against warm section openings? or cryo-modules performances and specific beam instrumentations replacements?
Not yet operated

## Slide 12: CEBAF at JLAB (by R. Geng)
1. What is the design of warm beamline systems next to a cold SRF cryomodule? size (ID and length) and material of the beam pipe? type and capability of vacuum pumps? beam diagnostic instruments (such as BPM, wire scanner, beam viewer etc)? 56 each segments of UHV beam pipe (stainless-steel tube and bellow), 35 mm bore diameter nominal, length ~ 1m. Conventional Ion pump (30L/s) and Differential Ion pump (30L/s) between adjacent modules. TSP’s in DP station at end of each linac. BMP (in each inter-CM warm beamline), wire scanners, beam viewers at various location in linacs. 2. What kind of gate valves are used to isolate the cavity string from the warm beamline system? fast valve or slow valve? under what conditions these valves are actuated? VAT mini UHV GV, 01032-UE44-ADU1. Open/close time 0.7 s. Fast valve (10 ms) at end of linacs. Actuation threshould 1E-7 Torr -> 5E-7 Torr

## Slide 13: CEBAF at JLAB
3. Are NEG pumps used? if yes, how these pumps are activated? 4 each installed in 2 CM’s since 2016. SAES Capacitorr® ZAO HV 200. Activation with NEG pump isolated from beamline UHV by a GV. 4. What is the cleaning procedure for the warm beamline system? What is the QA/QC for the cleanliness/particulate count? Standard UHV cleaning. Added low-particulate requirement since 2016. Particle counter + ionized nitrogen blowing for particulate Q/A/QC of individual components. Portable clean room in tunnel for connecting warm beamline to CM. Slow venting/pumping. 5. What kind of vacuum gauges are used for beamline vacuum monitoring? are they resistant to ionization radiation? Ion pump current converted to vacuum pressure.

## Slide 14: CEBAF at JLAB
6. What kind of particulate monitoring has been dome for controlling particulate generation and movement for individual components (pump, gatevalve) and integrated warm beamline systems? No offline testing has been done. No particulate monitoring system in the beam line.

## Slide 15: CEBAF at JLAB
7. What have you learned from beam operation of SRF accelerators wrt particulate generation and movement and the impact to field emission characteristics? Cryo modules long term performance against warm section openings? or cryo-modules performances and specific beam instrumentations replacements? Evidence of particulate generation from ion pump.
Evidence of particulate transportation in UHV beamline (Ti/Ta and perhaps others such as Cu etc).
Observation of “gradient degradation” (for the same “trip” rate).
Observation of sudden field emission turn on during beam operation.
( http://accelconf.web.cern.ch/AccelConf/ibic2017/papers/th1ab1.pdf )
Large loss in gradient due to leaks in warm UHV beamline (for example leak in viewer bellows).