## Slide 1: FRIB Beamline Integration Plan
Hiroyuki Ao
TTC Meeting at RIKEN, Wako, June 26 - 29, 2018

## Slide 2: Warm and Cold Transition in FRIB Linac
Red lines show “SRF particle-free” warm beam transports
Beamline length ~3 m, inner diameter 40~47.5 mm, made of SUS
Vacuum
    Entrance and exit of cryomodules pumped down by a 75L/s ion pump
    Pressures achieved < 5E-9 Torr
Diagnostics
  BPMs cleaned with SRF particle-free procedure
  Movable devices avoided as much as possible
Gate valve (Slow)
Fast gate valve
β=0.041
β=0.085
β=0.29
β=0.53
β=0.53
β=0.085 matching
β=0.53 Matching
Q1
(RFQ)
Linac Segment 1
Linac Segment 2
Linac Segment 3
(To target)

## Slide 3: Cold (SRF) Installation Progressing
Room temperature
Electron Cyclotron Resonance
Ion Source (ECR IS)
RFQ
Superconducting ECR IS
(Not yet)
Warm
Cold (SRF)
Vertical drop
LEBT
MEBT
β=0.041 cryomodule
D-station
β=0.041
β=0.085
β=0.29
β=0.53
β=0.53
β=0.085 matching
β=0.53 Matching
FGV
FGV
PMs
ARR02 beam commissioning includes the three β = 0.041 cryomodules (CMs) and the diagnostic station (D-station) in Linac Segment 1 (LS1)
(FGV actuated by P>2E-5 Torr)
Particle test performed to observe particle migration for profile monitors and fast gate valves

## Slide 4: Profile Monitor Particle Counts
A
B
C
D
E
G
F
H
I
J
K
L
Location | Particle Counts (0.3 um part./sq in)
A | 1.83, 0.17
B | 0.17, 0.33, 1.67
C | 0.33, 7.33, 0.17, 0.67
D | 0.0, 0.33
E | 0.0, 0.0
F | 7.33, 4.5, 19.33, 1.17, 3.5
Location | Particle Counts (0.3 um part./sq in)
G | 0.0, 0.0
H | 0.0, 0.0
I | 0.0, 5.67, 0.17
J | 0.0, 0.0
K | 0.17, 0.0
L | 5.83, 0.5
Slowly (<1 Torr/sec) pump out chamber to <1 Torr from downstream end of chamber
Actuate profile monitor 100 times
Slowly vent chamber with filtered, dry N2
Perform particle counts at end of beam pipe
Q6
Courtesy: I. Malloch
(PM)

## Slide 5: FGV Particle Counts
A
B
C
D
E
F
G
H
J
K
Q
P
O
N
M
L
I
Pump Cart
Location | Count
A | 24.19
B | 0.19
C | 11.35
D | 0.84
E | 0.39
F | 3.35
Location | Count
M | 1.68
N | 0.71
O | 0.19
P | 0.00
Q | 0.84
*All counts are 0.3 um part./sq in | 
Location | Count
G | 3.23
H | 1.68
I | 0.84
J | 2.39
K | 1.87
L | 3.55
Slowly (<1 Torr/sec) pump out chamber to <1 Torr from downstream end of chamber
Actuate fast gate valve only one time
Slowly vent chamber with filtered, dry N2
Perform particle counts at end of beam pipe
VAT Series 752
Q2, 6
Courtesy: I. Malloch

## Slide 6: GVs, CCGs
Gate Valves (Huntington)
  See TTC2017 at FRIB, B. Oja
CCGs (Agilent IMG-300)
  Radiation-resistant and bakeable to 250ºC during operation
  Range: 1 x 10-3 to 1 x 10-11 Torr
  Fluctuate less than 1E-8 Torr
Q5
1e-8 Torr

## Slide 7: Final Comments
Establishing cleanroom quality control and clean assembly procedures are well recognized as being critical to SRF accelerator performance
Sometimes initial beamline design/scope DOES NOT include mitigation plans for cold and warm transition regions… (e.g. gate valves, cold traps, …)
Beamline integration has been conducted considering combination of cost and performance (FRIB has added 5 additional GVs and particle count tests so far)

## Slide 8: Backup Slides

## Slide 9: UHV (Warm) Installation
Minimize contamination during “warm” installation
HPEA filter
PPE:
gloves, caps, masks, half-cleanroom garments

## Slide 10: Common Questions about Warm and Cold Transition (By R. Geng)
1. What is the design of warm beamline systems next to a cold SRF cryomodule? size (ID and length) and material of the beam pipe? type and capability of vacuum pumps? beam diagnostic instruments (such as BPM, wire scanner, beam viewer etc)? 2. What kind of gate valves are used to isolate the cavity string from the warm beamline system? fast valve or slow valve? under what conditions these valves are actuated? 3. Are NEG pumps used? if yes, how these pumps are activated? 4. What is the cleaning procedure for the warm beamline system? What is the QA/QC for the cleanliness/particulate count? 5. What kind of vacuum gauges are used for beamline vacuum monitoring? are they resistant to ionization radiation?
A. See slide 2
A. See slide 3
A. No
A. See slide 6

## Slide 11: Common Questions about Warm and Cold Transition (By R. Geng)
6. What kind of particulate monitoring has been done for controlling particulate generation and movement for individual components (pump, gate valve) and integrated warm beamline systems? 7. What have you learned from beam operation of SRF accelerators wrt particulate generation and movement and the impact to field emission characteristics? Cryo modules long term performance against warm section openings? or cryo-modules performances and specific beam instrumentations replacements?
A. Not yet
A. See slide 4 and 5