## Slide 1: Undulator radiation doses caused by synchrotron radiation
Shan Liu (DESY), Yuhui Li (European XFEL)
Radiation task force meeting, 17.05.2018

## Slide 2: Calculation of the Undulator SR properties for the input to BDSIM simulation
The 5D phase space (x, x’, y, y’, Eph) of the photons generated from each undulator is needed for BDSIM.
Basic ideas
The simulation is done for a single undulator segment instead of one continuous structure
The photon space is assumed identical to all undulators with 6m longitudinal shift

## Slide 3: Spectra simulation parameters
100pC
Optics is matched

## Slide 4: Energy dependent total flux --- Undulator Mode
SR Flux with respect to the photon energy
1D space distribution instead of 5D
For each harmonic the spatial distribution of the flux density is simulated: F.Density as function of (x’,y’)
F.Density distribution of (x,y) is constructed by the distribution of (x’,y’)

## Slide 5: 3D Angular distribution --- examples
1st Harm.
2nd Harm.
11th Harm.
12th Harm.

## Slide 6: Far zone: phase space (x’,y’) is proportional to (x,y)
The angular distribution along axis
The distribution is the same at 20m and 50 m from the source

## Slide 7: Investigation for the proper size and distance
0.08 mrad is chosen as observation angle
50 m is chosen as observation distance: 0.08mrad*50m = 0.4mm < radius of SR absorber

## Slide 8: SR output for BDSIM and the self consistence
4D Photon Phase space file format: for each harmonics
Flux sum from spatial distribution of each harmonics agrees with the simulation of energy dependent flux

## Slide 9: Input parameters for simulation in BDSIM
Start point is at 52.5m and the same SR distribution is added after each undulator section (6.1 m long)
Photon number for different photon energy is applied as “weight” factor in the simulation
x:y

## Slide 10: Simplified absorber geometry and simulated energy loss from SR
absorber aperture
(2a=9, 2b=8 mm ellipse, L=50mm)
absorber
undulator

## Slide 11: Simulated radiation dose from SR
1st mag. & pole with vacuum chamber (taken as Radfet)
undulator with vacuum chamber
Magnets and poles are put into BDSIM together with vacuum chamber as a single element (might be able to decouple them in the future)
Two simulations have been performed with and w/o magnets and poles (with same seed number)
Doses absorbed by vacuum chamber is subtracted afterwards
Dose level at the radfet location is rather low with the simplified absorber geometry (<2 Gy/C) comparing with the measured values (10-20 Gy/C)

## Slide 12: Absorber geometry update
Upadated absorber in BDSIM
L= 6+9+3+22.2 mm
absorber aperture
(2a=9, 2b=8 mm ellipse, L=3mm)
BPM and Quad. aperture
(ø 10 mm, L=22.2 mm)
undulator chamber aperture
(2a=15, 2b=8.8 mm ellipse, L=6+9 mm)
Drawings from T. Wohlenberg

## Slide 13: Simulated losses from SR with updated absorber geometry
3rd layer of absorber
(2a=9, 2b=8 mm ellipse, L=3mm)
L= 6+9+3+22.2 mm
undulator

## Slide 14: Simulated radiation dose from SR with updated absorber geometry
Significant radiation dose increase observed after updating absorber geometry!
1st mag. & pole with vacuum chamber (taken as Radfet)
undulator with vacuum chamber

## Slide 15: Comparison with measured radiation dose
Simulated radiation dose level is quite close to the measurements
Similar fluctuation of doses at Radfet position observed in measurements and simulation?
Averaged dose per undulator shows less fluctuation

## Slide 16: Conclusions and discussions
First simulation results shows that SR can cause similar level of doses as measured by the Radfets;
Radiation doses at radfet position highly depends on the absorber thickness;
Adding more components in the intersection (phase shifter, BPMs and air coils) may change the results;
Dependence on the orbit or misalignment is not studied -> check the difference on upper and lower Radfet?
Dependence on optics mismatch not simulated yet -> may change the spectrum distribution.

## Slide 17: You are welcome to join! Thank you!
Meeting with BDSIM developers on 28-29th May 2018:
  introduction to BDSIM (seminar on 29th May)
  discussions on 28th May:
    update of BDSIM version
    add hadronic process (damage due to neutrons)
    event biasing and output space saving
    adding more sampler point in one element (each mag. and pole w/o vacuum chamber)
    add more components in the intersection of undulator (e.g. phase shifter, bpm)
    simulation with SR, wakefield, beam-gas scattering, orbit offset or vacuum chamber misalignment