## Slide 1: Photon Run Coordinator

## Slide 2: SPB/SFX

## Slide 3: FXE

## Slide 4: Laser

## Slide 5: Vacuum
Nothing to report.

## Slide 6: Photon Diagnostics
XGMs: a) XTD2, XTD9, XTD10, and XTD1 XGMs are running 24/7 - Calibrations were checked for all XGMs b) After moving XTD9 XGM by 4 mm in the shutdown, measured beam position is now 4 mm closer to the center, and the measured energy is just slightly lower than XTD2 (as expected). The ratio of the XGM-intensities XTD9 / XTD2 measured over 1 hour today was 95%. c) Implementation of consequences of "Fresh bunch technique" for SASE1/SASE3 are under preparation, but not straight-forward. d) XGM in XTD6 will be surveyed and connected to the vacuum beamline on Friday 25.05. e) Developed new XGM data overview scenes in karabo, can replace the DOOCS SASE viewer, implemented now in SA1 + SA2
K-monochromators: Progress in XTD1/SASE2: successful commissioning and first 4-bounce operation of that Kmono (in multibunch mode)

## Slide 7: CAS

## Slide 8: Detectors

## Slide 9: Advanced Electronics
SPB:
  Update of PLC loop 8, all SPB loops now updated
• Fixing of names in gauges for PLC loop 2
tunnels:
  SASE1 error fixed for SPB_shutter_open signal (loop to be updated)

## Slide 10: ITDM
DAQ software
  Release of Pclayer 1.5.18 for karabo 2.2.3.5 (pipeline fix + Fast Data buffers release fix)
  Deployed and tested PcLayer 1.5.18 (Karabo 2.2.3.5) in SPBTST, FXETST, FXE and SPB production, acceptance test with FXE and SPB experts done
  Additional issue found and solved in PcLayer (version 1.5.19 already released). Version tested in SPB and to be deployed as soon as possible.
  FXE and SPB have now 4 Slow Data aggregators each:
  FXE distribution of data sources among DAs and data groups done with FXE experts
  SPB distribution of data sources among DAs and data groups partially done with SPB experts and should be concluded in the following weeks
  SASE1, SASE2, SASE3 data source groups modifications/additions/test were performed upon request.