## Slide 1: Photon Run Coordinator
machine is optimized with 9.3keV photon energy with stable beam of 1mJ with 60 pulses with 560kHz.
It is recommended not to use the first bunch but to kick the bunches within the first 15 us to TLD. This gives much better stability in electron beam orbit, photon beam pointing and photon pulse stability
SA1:
FXE day shift: User program and requested to have 60 pulses with photon energy 9.3keV with 560kHz.
SPB night shift: Focus on aligning the beamline and commissioning the detectors. Requested to have 60 pulses with photon energy 9.3keV and with 560kHz, 1.1MHz. On Sunday they would like to have 7.1keV photon energy.
SA3:
Parasitic commissioning of Soft-Mono is on going.
AE with coordination Vacuum group updated the GATT vacuum loop and PLC loop.
Issues:
Sunday: Cold compressor failure – now fixed. Laser interlock failure - has been fixed.
Sunday: Tuesday: Unable to change the photon energy with Undulators of SA1, later Suren has fixed this.

## Slide 2: SPB/SFX
Last week Beam time for Users experiment.
Commissioning ongoing (started yesterday night).
No Major issues to report.

## Slide 3: FXE

## Slide 4: Laser
SASE 1:
PP-laser has been operating for 4 weeks now without problems. Shift changes are done routinely and pulse / burst parameters as requested by experiments are delivered.
sporadic shutter error states occur mainly at FXE. These require a reset of the shutter. Independent tests with this type of shutter in our lab do not produce the error. We are currently suspecting issues with grounding and will also try to establish potential correlations with other events at times when shutter errors occur -> ongoing process.

## Slide 5: Vacuum
Nothing to report.

## Slide 6: Photon Diagnostics

## Slide 7: CAS

## Slide 8: Detectors

## Slide 9: Advanced Electronics
SASE3
Update of Gas Attenuator in order to include and improve some interlocks
Update EPS loop to correct some initial state for signals that are sent to Gas Attenuator loop.
SASE2
CRLs in XTD1 currently tested in the Tunnel. Some electrical issues have been discovered and they have being fixed during the tests. After finishing, the CRL will be included in SASE2 Motion loop 1.
SPB
Error of interlock triggered reported for two valves SPB_MKB_VAC/VALVE/VALVE_INLINE_4 and SPB_IRU_VAC/VALVE/VALVE_INLINE_1. After applying filters to the gauges involved in the interlocks, the problem seems to be solved. Anyway the gauges values are being recorded in Data logger in order to analyze them afterwards.

## Slide 10: ITDM
DAQ software
Release of Pclayer 1.6.1 for karabo 2.2.3.5 (performance issues enhancement)
Deployed and tested PcLayer 1.6.1 (Karabo 2.2.3.5) in SPBTST, FXE production, SPB production and all SASE's DAQ's.
Acceptance test with FXE and SPB experts done