Status report:
Electron trigger efficiencies from Z->ee events.
Stefan Mättig

---
Determining the trigger efficiency:
1.Monte Carlo:
       -Trigger simulation.
 -Use truth information to estimate the efficiency.
2.Tag and Probe:
-Use process with two known electrons	-> Z decays:
       -Select events with two good reconstructed electrons.
-Look at the invariant mass and select Z´s.
-Tag one electron for which the trigger has fired.
-Estimate the trigger efficiency by probing if the second	electron has been triggered too.
-not bias free!

---
CBNT 9550 events. pp collision with one Z->ee.
GENERATOR level:
        PRECUTS (for at least one electron)
  pt >10GeV, |h|<2,7

---
End of tracking |h|=2,5
No electron identification possible, pile up.

---
RECONSTRUCTION: Egamma container
-Contains energy, j,h of electromagnetic cluster.
-Contains information to seperate electrons from jets (IsEM-flag).
-Via trackmatch identification of electrons possible.
ptrec. >10GeV:
~50% of the events contain 2 Egamma objects.
Additional EM-cluster by radiated photon?
        truth matching
„lost“ electron in region |h|>2,7

---
selection of good reconstructed electrons:
-IsEM-flag: bit field, marks whether the candidate passed cuts or not
        (based on calorimeter and inner tracking system).
     See: https://twiki.cern.ch/twiki/bin/view/Atlas/ElectronGammaIsEM
Cluster based:
EtaRange
HadronicLeakage
MiddleSampling
FirstSampling IsEM==0
        good electron/photon
        Track based:
EtaRange
        HitsA0
 MatchAndEoP
  TRT
-selected items should have a track.
cut flow table:	generator level: EVENTS
        9550
        |h|truth <2,5 for both electrons: 5412
reconstruction:
Pt>10GeV; IsEM==0, 4476
     Pt>10GeV; IsEM==0; matched tracks=2: 1555 ?

---
Distributions of the selected electrons:
e+ e- back to back.
Electrons in inner detector.

---
Distributions of the selected electrons:
Tag and Probe method	in region
Mz +/- 10GeV.

---
Summary & Outlook:
- We took a look at the electrons. Compared reconstructed and generated distributions.
- For the tag & probe method, we selected events with the required two good electrons	and reconstructed the invariant mass to get a clean sample.
- We even discovered the detector in the sample:
NEXT STEPS:
- CBNT contains LVL1, LVL2 and EF information, algorithms for trigger decision need	to be implemented.
- Estimate the electron trigger efficiency with the MC and the Tag & Probe method for the	different trigger levels.
- Compare the results.

---
Em/Tau Trigger Block
    L1Em_nRoI - Number of e/gamma/tau RoIs in the event
    L1Em_RoIWord(L1Em_nRoI) - Raw RoI word (32 bits) encoding position and thresholds passed
    L1Em_Core(L1Em_nRoI) - Central 2x2 "RoI core" ET (em+had)
    L1Em_EmClus(L1Em_nRoI) - Em Cluster ET
    L1Em_TauClus(L1Em_nRoI) - Tau Cluster ET
    L1Em_EmIsol(L1Em_nRoI) - Em Isolation ET sum
    L1Em_HdIsol(L1Em_nRoI) - Outer Had Isolation ET sum
    L1Em_HdCore(L1Em_nRoI) - Inner Had Isolation ET sum
    L1Em_EmThresh(L1Em_nRoI) - Set of e/gamma thresholds passed (bitmask)
    L1Em_TauThresh(L1Em_nRoI) - Set of tau/hadron threshold passed (bitmask)
    L1Em_eta(L1Em_nRoI) - eta coordinate of RoI
    L1Em_phi(L1Em_nRoI) - phi coordinate of RoI
example:
LVL1 trigger isolation cuts for a 25GeV electron:
L1Em_EmIsol <= 3000
L1Em_HdIsol <= 2000
L1Em_HdCore <= 2000
L1Em_EmClus > 19000