## Slide 1: Beamline component alignment steps (NOT: Drill-hole marking)
Step 1: Design of component: Discuss mechanism of adjustment with MEA group. Preferred solution: DESY ‘Lenker’ system. Discuss number and positions of fiducials.
Step 2: Before installation: Tell to H. Sinn the position of this component in the beamline. He will generate a unique name e.g. SHUT.3335.T6HED. The component will be added to the facility-wide list ‘X-ray component list’, which contains the six coordinates of the component reference point in PD and other coordinate systems.
(WP73 Alfresco site, https://docs.xfel.eu/alfresco/d/a/workspace/SpacesStore/76bd0e9c-fe53-4622-8768-e628c8876178/X_ray_component_list_2_6.xlsx)
Step 3: Transfer measurement: Transport component to MEA measurement hutch in Petra3 experiment hall. Communicate to MEA, the component name (SHUT.3335.T6HED) and where the reference point for fiducials should be (standard solution: In the middle between entrance and exit flange)
Step 4: Alignment: After installation tell MEA that component SHUT.3335.T6HED is ready for alignment and arrange appointment. Typically the MEA survey team prefers to work by themselves, if all information is clear to them.

## Slide 2: Variations from standard process
(All of them lead to delays):
Step 2: Transfer measurement will be done without defined name from H. Sinn: A preliminary name is chosen and has to be cross-correlated later.
Step 3: Transfer measurement is done by vendor: Data have to be sent to Johannes Prenting of Markus Schlösser together with component name and technical drawings. Preferred is to have the measurement data as ASCII file. Otherwise data are entered manually by them into their database.
Step 3: Component to big to be transported to Petra: In exceptional cases transfer measurements can be done in the hutch (e.g. MID main instrument). This requires careful preparation and different personnel from MEA.
Step 4: Non-DESY alignment platform: MEA will typically refuse to do the manual alignment. Therefore one of your group has to be there do move the component according to their directions. In particular if motors need to be moved.

## Slide 3: Requests that will be typically refused
Telescope or theodolite-style alignments:
Marking of beam path on the floor or beam height on the wall
Alignment to reference edges on component
Alignment to ‘middle of flange’ in hutch (considered to be part of transfer measurement)
Based on poor preparation:
‘On-the-fly transfer’ measurements in the hutch or tunnel
Alignment of components without transfer measurement and without (PD) coordinates of the reference point