## Slide 1: Magnets
XFEL Operator Training

## Slide 2: Conventions: Dipoles (Incl. Correctors)
The XFEL has a right-handed coordinate system. z points downstream.
Where does this corrector deflect the electron beam?
Which sign does its field/strength/kick have?
UP
+

## Slide 3: Conventions: Quadrupoles
Is this quadrupole focusing or defocusing in the horizontal plane?
DEFOCUSING
What is the sign of its gradient/strength/integrated strength?
–

## Slide 4: Conventions
Dipoles and correctors with a positive field deflect electrons to the left (in positive x direction) or up (in positive y direction).
Quadrupoles with a positive generalized field are horizontally focusing for electron beams.
Usually, positive fields are driven by positive currents, but there are exceptions.

## Slide 5: Controlling Magnets... From the Cockpit

## Slide 6: Controlling Magnets... From a Stand-Alone Panel

## Slide 7: Controlling Magnets... From a Stand-Alone Panel

## Slide 8: Controlling Magnets... From the ML Server Panel

## Slide 9: Magnet Middle Layer Server
Magnet Name
Power Supply Circuit Name
<type>.<zpos>.<section>
SOL* – Solenoids
C* – Correctors
B* – Dipoles
Q* – Quadrupoles
S* – Sextupoles
O* – Octupoles
CB* – Correction/trim coils on dipoles (additional windings)
PS circuit names are similar: <type>.<ID>.<section>

## Slide 10: Many Magnets Can Share The Same Circuit
There is one device for each magnet
... even if multiple magnets share the same power supply
BL.48I.I1
BL.48II.I1
BL.50I.I1
BL.50II.I1
BL.1.I1
BL.3.I1
BL.4.I1
Laser Heater Chicane
Magnet Names
Power Supply Names

## Slide 11: Main Taskbar > Magnets

## Slide 12: The Magnet Overview Panel

## Slide 13: Current, Field, Strength, Gradient, Kick, Momentum, ...
... and other sophisticated words like “hysteresis” and “remanence”!

## Slide 14: Magnet ML: Physical Parameters
current
(gen.) field
calibration data
(gen.) strength
nominal momentum
(gen.) kick
effective magnetic length
Dipole
Quadrupole
Sextupole
Octupole
rad
rad/m
rad/m²
rad/m³
[B] = T
[g] = T/m
T/m²
T/m³
[1/ρ] = 1/m
[k] = 1/m²
[m] = 1/m³
[r] = 1/m4

## Slide 15: Magnet ML: Calibration & Hysteresis

## Slide 16: Dealing with Hysteresis
Current
Magnetic Field
upward ramp
downward ramp
“The magnet can cleanly ramp upwards.”
“The magnet can cleanly ramp downwards.”
klick down

## Slide 17: Dealing with Hysteresis
Current
Magnetic Field
upward ramp
downward ramp
“The magnet needs to be cycled.”
Uncycled magnets use an averaged calibration curve.

## Slide 18: Cycling & Degaussing
Current
Magnetic Field
Degaussing (Demagnetization)
Force the magnet out of its hysteresis curve so it has zero field at zero current. Ramp up and down with slowly decreasing currents.
Cycling
Force the magnet (back) onto its hysteresis curve. Ramp to maximum and minimum current a few times.

## Slide 19: Main Taskbar > Magnets

## Slide 20: Magnet Energizer
The combobox on the right selects a group of magnets:
Sections or subsections: I1M, B1, T2, …
All magnets that need to be ON to transport the beam to a certain dump: MAG_I1D, MAG_T4D, …
All magnets through which the beam passes on the way to a certain dump: OP_I1D, OP_T4D, …

## Slide 21: Magnet Energizer
This combobox selects what happens when „Set to beam energy“ or „Set to energy…“ is used:
Keep current (no scaling): Only the energy setting is changed, the magnet current stays the same. No impact on the beam, but the calculated kick is different.
Keep strenght (scaling): The magnet current is changed so that is has the same effect on a different beam. Use this when changing the beam energy.

## Slide 22: Main Taskbar > Magnets

## Slide 23: PS Monitor And Control (“PS MoCo”)
Low-level view on power supplies
Uses power supply circuit names
Has a search function for magnet names, circuit names, and MKK circuit numbers (menu Edit/Search...)
Use only for troubleshooting or if you‘re part of MKK!

## Slide 24: Main Taskbar > Magnets

## Slide 25: The “Good Old” PS Control
Please don’t use it – or only as a last resort for troubleshooting, if you know what you’re doing.
It handles only “DESY-type” magnets.
This means: It does not show all magnets.
IT DOES NOT SHOW ALL MAGNETS!