## Slide 1: LArTPC Charge-Light Matching and PID with Wire-Cell
Xin Qian
BNL
On behalf of the Wire-Cell team

## Slide 2: Introduction
Event reconstruction can be viewed as unfolding/fitting problem
  Likelihood function cannot be (easily) written
    E.g. general pattern recognition
    When good data is available, machine learning techniques are expected to have clear advantages in solving this type of problem
  Likelihood function can be (approximately) written
    A computing problem to maximize likelihood
    Provide essential insights/feedbacks with imperfect data
    Example I: Charge-light matching in LArTPC
    Example II: track trajectory and dQ/dx fitting in LArTPC
SLAC/DL
BNL/Wire-Cell

## Slide 3: LArTPC Charge-Light Matching
Side view
Top view
Front view
After Charge-Light Matching
Procedure | Neutrino : Cosmic Muons
Trigger | 1 : 800
PMT filter (late light rejection) | 1 : 200
Many-to-many charge-light Marching | 1 : 7
After 3D Imaging

## Slide 4
Matching Hypotheses
Clustering
3D Image
Light Reconstruction
Hypotheses Selection
4.8 ms drift window
20-30 TPC activities
All possible hypotheses
One flash  many or zero TPC clusters within corresponding active volume (activities in inactive volume)
One cluster  at most one flash (inefficiency in the light system)
Light signal proportional to (reconstructed 3D) charge
Known light acceptance given position
Predicted vs. Measured light pattern with Compressed Sensing
Matching Principle

## Slide 5: PMT Light Flash Reconstruction
Employ signal processing techniques (see H. Wei’s talk) for PMT waveform
Key is to handle the late light
  70% of overall light being long component (~1.5 us) for M.I.P.
Integration window to fully encapsulate late light
Raw
Deconvolved
Late light unfolding

## Slide 6: Light Signal for Michel Electron
Compressed Sensing technique was used to unfold the late light
Light signal of Michel electrons is sometimes visible

## Slide 7: Interaction Clustering
LArTPC is a fully active detector
  Design of cold electronics with anti-aliasing filter respects this feature
In principle, clustering based on connectivity and distance is straight forward
In practice, additional challenges
  Dead channels
  Noise filtering and signal processing
  Real coincidence in ionization electron arrival time

## Slide 8: Challenges in Clustering (I)
Gap as a result of Noise Filtering
Gap as a result of Signal Processing
Projected Induction V view
Drift Time
Projected Induction U view
Drift Time
(Left) coherent noise subtraction may remove signal when the S/N is small
(Right) signal recovery for prolonged track in the induction wire plane is a difficult task

## Slide 9: Challenges in Clustering (II)
Gaps as a result of non-functional channels
Grey regions are with two non-active wire planes (2/3)
In average about 10% dead channels in MicroBooNE  3% dead regions requiring 2/3 planes in image reconstruction
Random Coincidence in ionization electron arrival time
Before separation
After separation

## Slide 10: Example of Actual Algorithm for Clustering
Many advanced techniques, such as graph theory operations (Dijkstra’s shortest distance, connected components, minimal spanning tree), Kalman-filter, 3D and 2D k-d trees, are used to obtain a robust results in a quick and efficient way

## Slide 11: Core Charge-Light Matching Algorithm
Overall test statistics to be minimized
Comparison of the measured and predicted light pattern
Each Charge Cluster can only be used once
Observed light flash may not correspond to any charge cluster
Compressed sensing to select the best pairs
Aggressively pursue charge-light matching
Additional cuts to examine the “light mismatch” events

## Slide 12: Performance
Side view
Top view
Front view
MicroBooNE Simulation
In Progress
Completeness: overlap over true
Purity: overlap over reco [ghost, over-clustering, etc.]
The Geant4-based simulation for neutrino interactions with above 90% accuracy in Charge-Light Matching
CC interactions
in active volume

## Slide 13: Application of Matching: Space Charge Boundary
After correcting t0 for all cosmic muons in one event
Anode
Cathode
E field (X)
Rejection of in-beam-time through-going muons (TGM) with correct active volume boundary
Drift direction (X)
Vertical Direction (Y)
Vertical Direction (Y)
Beam Direction (Z)
Vertical Direction (Y)
Again, challenges on the dead and inefficient channels (NF and SP)
Neutrino : Cosmic ~ 1 : 1 after TGM rejection

## Slide 14: Particle Identification in LArTPC: Track Trajectory and dQ/dx fitting

## Slide 15: Unique Particle ID capability in LArTPC
Gap Identification + dE/dx to separate e/γ for νe charge-current interaction
Comparison of PMCS and PRange to separate low-energy e/µ for νe charge-current interaction
Michel e
Stopped muon
Dead ch.
Also, the identification of the Bragg peak can help to reject stopped Cosmic muons

## Slide 16: Principle of the Fit
Come up with a 3D track hypothesis (3D trajectory points and dQ/dx)
Predict the deconvolved signals on all projection views
Minimize the difference between the observation and prediction
V view
U view
W view
Inspired by the Projection Matching Algorithm (R. Sulej and D. Stefan)

## Slide 17: Simplified Prediction of the Deconvolved Signal
dQ/dx at generation
diffusion
Electron at anode plane
Induced current on wires
Convolve with field res.
Convolve with elec res.
Digitized amplified current
Signal Processing Chain
Deconvolved signal
At signal processing stage, we have two additional effects:
Software filters (time and wire dimension)
Usage of position-averaged overall response function
Simplified model
Pixel # in 2D Projections
Charge
Full process of signal formation and signal processing is complex (more details in H. Wei’s talk)  significant burden in computation
A simplified model was developed

## Slide 18: Trajectory Fitting
Choice of test statistics
  Avoid nonlinear fit of Gaussian function  take advantage in linear algebra
  Similar to an unbinned likelihood
Choice of regularization
  Cases of two non-responsive wire planes
Unknowns
Measurements
Displacement to truth information
Notes: https://www.phy.bnl.gov/twister/bee/set/692f6401-5e2d-45e1-94ba-b1f510db4b1b/event/1/

## Slide 19: dQ/dx Fitting
Smearing coefficients are fixed with the determined trajectory
  Linear Algebra can be used in the fit
Regularization(s) are necessary
  Regularization on the smoothness
  Additional regularization needed for the cases of compact projection view

## Slide 20: PID Performance on Monte Carlo

## Slide 21: Issues in the Real Data
Imperfect detector response
Dead channels
Inefficient channels
  Noise filtering  isochronous tracks
  Signal processing  prolonged tracks
Difficult topologies
Isochronous tracks
Compact projection view (e.g. vertical cosmic muons)

## Slide 22: Graph Formation with Dead Channels
Link:
Original Image
First round retiling with known dead channels
Second round retiling with inefficient channels
Link:
3D view
3D view
X-V view
X-Z view
Y-Z view
X-V view
Link:

## Slide 23: Seed in Trajectory Fitting
Seed is crucial to limit the number of DOF (degrees of freedom) and the define the region of interest for each charge-weighted center
  (low-threshold) 3D points are ordered in a graph
  Shortest path (between two points) in a graph gives the initial guess of the seed
  Further refinement considering the high-charge points (Steiner-Tree, as gaps are expected)

## Slide 24: Examples of Seeds in Trajectory Fitting

## Slide 25: Example: Isochronous and Compact Track
Compact in W view
U View
V View
Dead chs.
Dead chs.
Before Improvements
After Improvements
In Progress

## Slide 26: Example: Stopped Muon
Compact in W view
U View
V View
Bragg peak
Dead chs.
U View
V View
W View
Before Improvements
After Improvements
In Progress

## Slide 27: Example: Proton Candidate
Before Improvements
After Improvements
W view
U View
V View
Dead chs.
In Progress

## Slide 28: Example: Two vs. One MIP
W view
U View
V View
1 MIP
2 MIP
Dead chs.
Before Improvements
After Improvements
In Progress

## Slide 29: Summary of Wire-Cell Reconstruction
LArTPC Signal Formation
Noise filtering and Signal Processing
slicing
tiling
deconvolving
3D Imaging
solving
clustering
TPC/Light Matching
matching
fitting
recognizing
Trajectory and dQ/dx fitting for PID
3D pattern recognition
Improved TPC signal simulation (long-range and fine-grain)
JINST 12 P08003
JINST 13 P07006, P07007
Robust usage of induction wire planes
JINST 13, P05032
MicroBooNE imaging paper under preparation
2D projections3D problem independent of event topology
MicroBooNE neutrino selection paper under preparation
Charge/Light matching
Precision PID?
Need to revisit