## Slide 1: Laser diagnostics
Christian Rödel, Matt Zepf
LUXE meeting at DESY, 8.11.2018
Helmholtz-Institute Jena
Notes: generelle Sprachwahl

## Slide 2: Motivation
SLAC Experiment E144:
electron laser collision
46.6 GeV electron beam energy
Laser intensity
106 positrons above background
experimental evidence for non-linear Breit-Wheeler effect
D.L. Burke et al, Phys. Rev. Lett. 79, 1626 (1997)
Measurement of intensity distribution or normalized field strength a is crucial for testing theories of strong-field QED
Notes: pure photon photon colllider

## Slide 3: Intensity measurement
Typically in the high intensity laser community Intensity as power density
Indirect measurements (typically not on-shot and not in focus !!):
  Pulse energy from near-field profile
  Pulse duration from near-field profile
  Focus area from attenuated focus

## Slide 4: Intensity measurement
Near-field measurements
High intensity laser pulse
few J
30 fs
15 cm beam diameter
Off axis parabolic mirror
F/#=2
Focal length = 30 cm
Turning mirror
leakage
Electron beam
Gamma beam
Near field diag
Far field diag
Movable far field diagnostics
Attenuated duplicated
Laser pulse

## Slide 5: Intensity measurements
1st step: on-shot near-field characterization
  Measurement of near-field profile (leakage of turning mirror) -> telescope and camera, get pulse energy and near-field distribution
  Measurement of pulse duration from nearfield (leakage, pick off mirror ?) -> “Spider”, “FROG”, “Wizzler”, etc.
  Measurement of wavefront, angular chirp and other spatiotemporal couplings of the light field (leakage ?) -> wavefront sensor (e.g. Phasics “SID4”), field correlator

## Slide 6: Intensity measurements
2nd step on-shot far-field characterization
  Intensity distribution
  Imaging spectrometer for wavefront rotation / angular chirp, etc
Measurement of intensity at focus (attenuated), correlation with leakage diag
  Above threshold ionization (2Up and 10Up cutoff) http://people.physics.tamu.edu/ggp/Publications/027-advances02.pdf
2Up
10Up
Photoelectrons
(log scale)

## Slide 7: Experimental a0 diag
Gamma ray profile gives a0 (W. Yan et al, Nature Photonics 11, 2017)

## Slide 8: Experimental a0 diag
Transverse spreading of electrons in high-intensity laser fields
  Green, Harvey, Phys. Rev. Lett. 112, 164801 (2014)
  shoulder of electrons might provide a0 and QED effects

## Slide 9: Experimental a0 diag
Measuring the gamma spectrum of Compton scattered photons
  Problem of building a good spectrometer in the gamma range (MeV), CsI stack ?
  Maybe calorimeter and low charge mode ?

## Slide 10: Conclusion
Diagnosing high intensity laser pulses is not trivial and requires some dedicated work
Much experience in the Helmholtz Association of diagnosing high intensity laser pulses: Andi Mayer (DESY), Uli Schramm (HZDR), Malte Kaluza (HI Jena), Christian Rödel (HI Jena), Matt Zepf (HI Jena), Vincent Bagnoud (GSI Darmstadt), Toma Toncian (XFEL), ...
Kick-off meeting of experts from the high intensity laser community required -> beginning of next year