## Slide 1: FLASH Refurbishment and FLASH 2020+
FLASH: the first soft X-ray FEL operating two undulator beamlines simultaneously
Siegfried Schreiber
DESY
Betriebsseminar Travemünde
21-Feb-2019

## Slide 2: FLASH Layout 2019
5 MeV
150 MeV
1250 MeV
Bunch Compressors
450 MeV
Accelerating Structures
RF Stations
Lasers
RF Gun
Fixed Gap Undulators
sFLASH
Photon Diagnostics
THz
FLASH1
FLASH2
FLASHForward
Albert Einstein
Kai Siegbahn
Variable Gap
FEL Experiments
TESLA type superconducting accelerating modules 1.3 GHz
FLASH1 fixed gap undulators
3rd harmonic sc module 3.9 GHz
Normal conducting 1.3 GHz RF gun
Ce2Te cathode / 3 injector lasers
FLASH1 Albert Einstein Hall
Extraction to FLASH2
FLASH2 variable gap undulators
FLASH2 Kai Siegbahn Hall
315 m

## Slide 3: FLASH Parameters 2019
Stable parameter set delivered to users
http://photon-science.desy.de/facilities/flash/publications/scientific_publications
Energy (µJ)
Bunch number
FEL Radiation Parameter FL1 / FL2
Wavelength range (fundamental) 4.2 – 51 nm / 4 – 90 nm Average single pulse energy 1 – 500 µJ / 1 – 1000 µJ Pulse duration (FWHM) < 30 – 200 fs Peak power (from av.) 1 – 5 GW Pulses per second 10 – 5000 Spectral width (FWHM) 0.7 – 2 % / 0.5 – 2 % Photons per pulse 1011 – 1014 Average Brilliance 1017 – 1021 B* Peak Brilliance 1028 – 1031 B*
* photons/ s/ mrad2/ mm2/ 0.1%bw

## Slide 4: Mid-term refurbishments
2017 – 2020+

## Slide 5: Main Refurbishments
“Big” refurbishments
Two new modules → 1.35 GeV ………………………………………………………………………………………………..….
Next generation injector laser → improved beam quality ……………………………………..…………………………
Low charge diagnostics → for short pulses ……………………………………………………………………………………
Polarized photons for FLASH2 → for new type of experiments ………………………………………………………………
Other main refurbishments
Machine protection …………………………………
Coupler interlock electronics ……………………………………………………………………………….
Fast arrival time stabilization with warm RF cavity …………………….……………..
TDS FLASH2 to measure and monitor bunch and photon pulse duration ………………………………………….
THz undulator FLASH2 ……………………………………………………………………………………………………….
Waveguide upgrades ………………………………………………………………………………………..…………
Fast intra-train orbit feedback …………………………………………………………………….
Projects
BPMs finished
BAMs started
Started
Toroids/BLMs/Finished
Installed
Postponed
Started
2017 2018 2019 2020
Started
Started
Scheme in discussion
Design started
: indicates installation time
New project

## Slide 6: Other refurbishments
A long washing list
 | Task | Status | 
E1 | Injector laser | on-going | *
E2 | Optical synchronization system | on-going | *
E3 | Afterburner FLASH2 | design in discussion | *
E4 | TDS FLASH2 | on-going | *
E5 | THz undulator FLASH2 | postponed | 
E6 | Bunch compressor FLASH2 | on-going | *
E7 | Magnet controls | started | 
E8 | Vacuum controls | starting | 
E9 | Screen stations FLASH1 | started | 
E10 | Upgrade LLRF | proposed | 
E11 | Upgrade RF master oscillator | proposed | 
E12 | Coupler interlocks | on-going | *
E13 | RF-gun (exchange) | prepared | 
E14 | ACC39 (exchange 1 cavity) | cavity 5 to be prepared | 
E15 | Personnel interlock system (waveguides) | started | 
E16 | Radiation shield Bogengang | started | 
E17 | Pumping stations 1 and 2 | proposed | 
E18 | Cooling towers | proposed | 
E19 | Cryogenics refurbishment | starting | *
E20 | Modulator 3.9 GHz | proposed | 
E21 | Fast orbit feedback | proposed | 
E22 | Controls (network switches) | started | *
E23 | Fast intra-train compression feedback | proposed | 
E24 | sFLASH (new EEHG chicane) | started | 
Concerning the priority:
All tasks are important to keep FLASH operating
None of the tasks are yet urgent, its mostly preemptive refurbishments
Tasks are worked on, when resources are available
For a few more important and cost intense tasks, measures have been taken to assure funding (*)

## Slide 7
New Modules

## Slide 8: Refurbishment of old accelerator modules
Replace accelerator modules ACC2 and ACC3 with refurbished XFEL type modules (PXFEL2 and PXFEL3)
We have good cavities with high gradients: >100 MeV energy gain are expected
Cavities have already been assigned to the modules
5 MeV
150 MeV
1250 MeV → 1350 MeV
450 MeV → 550 MeV
RF Gun
M3*** Type II
M1* M7 Type I/II
M4/M5/M6/PXFEL1 Type III
Type I feedlines
Type I to III transition
PXFEL 2/3 Type III
He
ACC1
ACC2
ACC3
ACC4
ACC5
ACC6
ACC7
Modules

## Slide 9: Refurbishment of old accelerator modules
Presently ACC2/3 is feed by RF-6 in the cryo-annex
A new station RF-1 will be installed in hall 3 close to the modules (10 MW klystron)
New waveguide distribution similar to PXFEL1/XFEL
Option: optimized waveguides at ACC4/5 to gain another 100 MeV
RF and waveguides
RF-6
RF-1
ACC2/3
ACC4/5

## Slide 10
Injector Laser

## Slide 11: New Generation Photoinjector Laser Development
Simple and robust architecture
1 ms trains (10 Hz, 1 MHz)
Flexible pulse pattern within one train – for both, FL1 and FL2
  two different aperture sizes
  charges
  pulse durations
Very similar to now
  with modern laser technology
  flexibility in one system
  longitudinal pulse shaping
  option 4.5 MHz
Project Goals
Oscillator development: low phase noise nonlinear fiber loop mirror oscillator
Amplifier development: High power fiber-rod amplifier module
Longitudinal pulse shaping development: Tests with high resolution spectral pulse shaper

## Slide 12: New injector laser rooms
To be installed close to the gun
The old laser rooms need to be replaced
However, to do this and to install and commission the new laser within a 6 month shutdown is too risky
Thus, we do not want to uninstall the present lasers before the new ones are ready to go
Size: about 100 qm
Laser heater: room replacing TOSYlab
Large enough to keep space for future laser developments
New injector laser room
Present laser room and synch hut
laser heater
ACC1
ACC2
ACC3

## Slide 13
Diagnostics

## Slide 14: Upgrade Beam Diagnostics
Upgrade charge measurement (toroids)
  New XFEL type toroids, data acquisition with MTCA (108 MHz ADCs)
  Improved resolution: smaller than 1 pC
  New TPS (toroid protection system, to prevent charge losses)
Upgrade electronics and hardware for machine protection system (MPS)
  Required to fully explore the multi beamline features
  New MTCA based standard, similar to XFEL
New electronics for most BPMs
  In order to get a much better resolution also for low charges
New hardware and electronics for BAMs
  To cope with short bunches with low charges
Profile monitors (OTR screens)
  BC2/3: we keep the vacuum chambers with OTR screens, new optics
  Other will be replaced by XFEL type screen stations – already realized in FLASH2 and one station in FLASH1
Better resolution especially for low charge operation
Upgrade finished
Upgrade finished
Upgrade finished
Upgrade started summer 2018
Upgrade postponed to 2020

## Slide 15: New BPM electronics
Better resolution – mainly for low charges
Goal: higher resolution also for low charge beams
10 µm
100 pC
10 pC
10 µm
100 pC
10 pC
old
old
new
new

## Slide 16: Upgrade BAM and Synchronization Systems
New BAM pick-ups with an improved sensitivity especially for low bunch charges have been installed.
New electronics is being commissioned piece by piece
Priority to ensure slow and fast intra-train arrival time feedbacks for users
Expected resolution <10 fs rms
The new set-up will also allow separate arrival time feedbacks for both beamlines, FL1 and FL2
Beam Arrival Time Monitor
Measurement & Stabilization of the Electron Bunch Timing
All-Optical Laser-to-Laser Synchronization
Phase Drift Compensation of the
RF-Reference used for Acceleration
UBC2
DBC2
DBC3
ACC7

## Slide 17: Upgrade BAM and Synchronization Systems
The synchronisation lab has been completely refurbished
New links are being installed
The synchronisation signals are now distributed through new polarisation-maintaining optical fibres
Expected reduction of jitter of signal transmission from 3 fs to 0.5 fs
A few links mandatory for FLASH operation have already been installed and commissioned
The number of possible links will increase from 8 to 24.
Further optical links will be installed step by step.
The full new system is expected to be available in 2020.
SynchLab
 | Status 2017 | Upgrade plan 2018/2019
No. of Clients | 7 | 20
No. of spare links | 0 | 4
Laser-to-Laser (L2L) Synchronization | 2 | 6 (extension by further 4)
Bunch Arrival Time Monitors (BAM) | 3 | 7
Optical Reference Modules (REFM-Opt) | 0 | 3

## Slide 18
Fast RF Feedback with BACCA

## Slide 19: Fast RF Feedback Cavity
* new electronics to process the NRF cavity * new electronics to process the BAM signals
NRF cavity
BAM
Correction of arrival time fluctuations which are too fast to be corrected by the narrow bandwidth (~ kHz) superconducting cavities
Goal is to push the arrival time stability well below 10 fs (~1 fs)
Fast corrector: large bandwidth normal conducting S-band cavity (~1 MHz, ~kW) controlled by a high-speed digital system (latency <1 µs)
Suppress the residual beam energy fluctuations towards dE/E~10-6
Arrival time measured in DBC2 with new high resolution low charge beam arrival time monitors
BACCA
334 mm

## Slide 20
FLASH2

## Slide 21: FLASH2
BC
TDS
TDS
Bunch compressor downstream extraction
  Component design and construction on-going
  Installation planned summer 2019
  Better control of CSR due to less strong compression at lower energies
PolariX-TDS (X-band transversely deflecting structure) downstream undulators
  Installation planned in 2020
  To reduce cost, we share one RF-station with FLASHForward
Installations 2019-2020
TDS at FLASH2

## Slide 22: PolariX TDS
Development of a new X-band (12 GHz) deflector
In cooperation with CERN and PSI
New feature: variable polarization
DESY will use these cavities for SINBAD, FLASHForward and FLASH2
MIN group formed a new X-band RF technology section
Polarizable X-band Transverse Deflection Structure
Courtesy of A. Grudiev, CERN
Collaboration contract signed
X-band Klystron and Modulator at DESY
Commissioning in Linac II (MIN)
Prototype cavity shipped PSI to CERN for RF tests (conditioning)
Prototype to be installed at FLASHForward in summer 2019
FLASH2 cavities in 2020
TDS shipped from PSI to CERN February 2019

## Slide 23: FLASH 2020+
Within the DESY 2030 strategy

## Slide 24: The XUV and Soft X-Ray FEL Landscape
SHINE (2023)
FLASH – the only high repetition rate XUV and soft X-ray FEL
Wilfried Wurth Photon Science

## Slide 25: Unique FLASH Features
High repetition rate ( = high average brillance)
Two almost fully independent FEL lines
Excellent timing synchronization
Mix of open ports and state-of-the-art dedicated endstations
Integrated THz source (phase stable with respect to FEL)
Advanced photon diagnostics
The first soft X-ray FEL operating two undulator beamlines simultaneously

## Slide 26: User Wishlist (Workshop Sept. 2017) vs. Upgrade Plans
“Dream Facility” | FLASH2020+ goals | FEL Line
fundamental up to O-K-edge | cover up to 6 decades of electromagnetic spectrum (mm to nm) with coherent radiation for multi-color experiments  novel undulator schemes | FLASH2
variable polarization | variable polarization | FLASH1 and 2
flexible pump-probe schemes (THz  XUV) | provide flexible laser- and FEL based schemes for multi-color pump-probe experiments | FLASH1 and 2
few fs- and sub-femtosecond Fourier-limited pulses | laser manipulate electron bunches in burst mode with up to 1 MHz rate  external seeding with high rep. rate | FLASH1
 | enable dynamic studies with attosecond precision | FLASH2
100kHz CW | Long-term goal (2030+) | FLASH@XFEL

## Slide 27: Expand Photon Energy Range  Element Specificity
XUV/Soft X-Ray Important Element Specific Resonances
Catalysis, Biochemistry, Energy Science, Information Technology Functional Materials (Magnetism, high_Tc, …), Life Science …..
Wavelength [nm]
N-K-edge
C-K-edge
S-L-edge
Si-L-edge
O-K-edge
3d-transition metals-L-edges
3d-M-edges
Water-window
Photon energies [eV]
FLASH
FLASH2020+

## Slide 28: FLASH within the DESY 2030 strategy
Our Strategy for the Future
Page 40:
… The FLASH2020+ development program of the two FEL lines and the accelerator includes
the operation of two independent FEL lines (FLASH1 and FLASH2) with variable magnet structures (undulators) for trend-setting new lasing concepts and „seeding“ with a high repetition rate
the extension of the wavelength range in the fundamental to the oxygen K-edge, in order to reach the important elements for energy research and to cover the whole water window for biological questions (*)
flexible pump/probe schemes for time-resolved experiments (*)
variable polarization for the investigation of the light-induced switching of magnetic storage media; and
shortest pulses up to the attosecond range.
(*) Original document in German, I have corrected the English translation to fit with the scientific content expressed in German

## Slide 29: FLASH 2020+
Preparation phase for FLASH2020+
  Six Task Forces (TF): TF1 accelerator, TF2 FEL beamline: seeded, TF3 FEL beamline: SASE and new schemes, TF4 Lasers, TF5 Experiments, TF6 Data
Conceptual Design Report (Spring 2019) followed by a Technical Design Report
Steps towards FLASH2020+
Upgrade linac many refurbishment projects, increase beam energy, upgrade compression scheme
Installation of new undulators with variable gap for FLASH1 with a seeding option
Seeding with high repetition rate 100 kHz+ high repetition rate seed laser
New configuration of undulator structures at FLASH2 for novel lasing concepts

## Slide 30
Task Forces

## Slide 31: Task Force Accelerator
Current status | 
Increase beam energy to 1.35 GeV | 
Run linac at fixed working points (usually max and intermediate, exceptionally low energy) | 
Include laser heater upstream of bunch compressor 2 (required for seeding) | 
Modified bunch compression scheme - add two new bunch compressors (FL1 and FL2) at final energy to improve beam quality and to gain more flexibility in tuning of both lines | 
Examples of tracking simulations with improved compression (with CSR, cavity wakes, and space charge, 100 pC)
→ much better performance expected
FLASH1
FLASH2

## Slide 32: FLASH: Laser heater 1st bunch compressor
Move bunch compressor by ~ 1.5 m to make place for the laser heater
Keep matching section with four screens, all quads with own power supply
Accelerator modules are not moved
Heater laser
Short Undulator
Present
Modified
Laser heater chicane
Required for a future seeding beamline
Modified matching section

## Slide 33: FLASH: Modification of bunch compressor BC3
Change S-chicane to a C-chicane and include matching section (2 additional quads)
Present
Modified
Allow matching in BC3

## Slide 34: New C-chicane bunch compressors
In FLASH1 and FLASH2 beamlines
FLASH1: we replace the dogleg with a C-chicane bunch compressor
  This move the beamline towards the tunnel center by 40 cm
  This gives the opportunity to renew the launching into the photon beamlines and to decouple the THz beamline from the photon beamline
FLASH2: add a C-chicane downstream extraction

## Slide 35: Task Force FLASH1 undulator beamline
Variable Gap Undulators and Seeding
New layout within existing FLASH1 footprint
Bunch Compressor / Matching Section / Modulator 1 / EEHG Chicane / Modulator 2/ HGHG Chicane / Radiator / Afterburner / TDS / Dogleg / THz undulator
Radiator (proposal)
1.15 m APPLE III, 8 mm gap, 50 mm period, Magnetic length: 16.8 m (16 sections, filling < 66%).
Sequence: Undulator/chicane/Undulator/Quad/chicane/BPM/Undulator/chicane/Undulator/Quad/chicane/Screen
Target specs |  |  | 
 | SASE | Seeding (10Hz) | Seeding (100kHz+)
Polarization | Linear/Variable | Variable | Variable
Wavelength | 4 – 90 nm | HGHG: 20 (10?) – 90 nm | HGHG: 20 (10?) – 90 nm
 |  | EEHG: 4 – 20 nm | EEHG: 4 – 20 nm

## Slide 36: Task Force FLASH2 Line
Novel Lasing Concepts
BC
3 m
Uas
0.5 m
Kicker
1 m
TDS or dechirper
2 m
U1
20 m
U2
2 m
U2 (U3?)
25 m
2.5 m
Ulsca
1 m
THz(OAB)
4 m
compact
chicanes
(R56 ~ 100 µm)
Total length of elements about 60 m + ~20 m for quads, steerers, BPMs (already included in U1, U2)
U1: period 3.5 cm, Krms = 2.55
U2: period 2.7 cm, Krms = 1.45
Main FEL modes
(for fixed energy 1.35 GeV):
Harmonic lasing (5th in U1 and 3rd in U2): 1.2 – 2 nm
Frequency doubling (chicane or reverse taper): 1.2 – 2 nm
HLSS: 2 – 6 nm
SASE: 2.3 – 18 nm
Two colors: 4.5 – 18 nm (U1) and 2.3 nm – 6 nm (U2)
compact
chicanes
(R56 ~ 100 µm)

## Slide 37: Attosecond Science at FLASH
Novel lasing schemes
Wavelength 5 nm
pulse length 50-70 asec (FWHM)
pulse energy 5 nJ
contrast above 98%
Scaling of XUV HHG laser sources
C.M. Heyl et al., J. Phys. B: At. Mol. Opt. Phys. 50 (2017) 013001
Exploit novel ideas based on laser-electron beam manipulation
„attoFLASH“
M. Dohlus et al., PRSTAB 14 (2011) 090702

## Slide 38: Proposed layout FLASH2020+

## Slide 39
FLASH2020+ Expected Parameters
**Simulations not finished: value is estimation
*Shared between FLASH1 and FLASH2
 | FLASH1 (Seeded) | FLASH1 (SASE) | FLASH2 | 
Wavelength range | 4 – 60 | 3.2 – 60 | 1.3 – 84 | nm
Pulse energy | <100** | <1000 | <1000 | mJ
Pulse duration (FWHM) | 30 | 5 - 200 | 0.1 – 200 | fs
Spectral width | Fourier limited | 0.5 - 2 |  | %
Pulses per second* | 10 – 5000 | 10 – 5000 | 10 – 5000 | 
0.75 and 1.35 GeV assumed as energy points

## Slide 40: The future XUV and Soft X-Ray FEL Landscape
SHINE (2023)
FLASH – the only seeded high repetition rate XUV and soft X-ray FEL
FLASH 2020+

## Slide 41: Summary

## Slide 42: Summary
Upgrades/refurbishments
Low charge electron beam diagnostics → finished
BAMs and synchronization system → started summer 2018
BACCA: Arrival time stabilization with a warm RF cavity → in commissioning
Many other upgrades/refurbishments are on-going or even finished: timing, MPS, coupler interlocks, cryo, magnet server, screens, VME crates, servers, personnel interlock …
Refurbishment of two old accelerator modules → 2020/21
Next generation photocathode laser → 2020/21
TDS at FLASH2 → 2019/20

## Slide 43: Summary
FLASH2020+ development program
Includes: operation of two independent FEL lines (FLASH1 and FLASH2)
  with variable magnet structures (undulators) for trend-setting new lasing concepts
  seeding with a high repetition rate
  extension of the wavelength range to the oxygen K-edge (540 eV/2.3 nm)
  flexible pump-probe schemes for time-resolved experiments
  variable polarization
  shortest pulses up to the attosecond range