## Slide 1: Operation and SASE tuning statistics
FLASH: The first soft X-ray FEL operating two undulator beamlines simultaneously
Juliane Rönsch-Schulenburg &
Katja Honkavaara
Beschleunigerbetriebsseminar Travemünde
Februar-21, 2019

## Slide 2: FLASH Operation Statistics 2018

## Slide 3
FLASH1 Operation 2018
Chart: 
| User | MDE+PDE | ARD
 | 4188.5 | 2109.8 | 804.65
FEL user operation 59% 4189 h
Studies and user preparation 30% 2110 h
Accelerator R&D 11% 804 h
Chart: 
| SASE | Tuning+Set-up | Down | Blitz
 | 3426.35 | 616.85 | 145.3
SASE delivery 81.8% 3427 h
Tuning + Set-up 14.7% 617 h
Down 3.5% 145 h
FLASH1: 7103 operating hours
7103 operation hours
of which 4189 h FEL user operation
scheduled maintenance 59 h
scheduled shutdowns 1445 h
exchange RF-gun RF-window 100 h
cryo maintenance 53 h

## Slide 4
Chart: 
| User | MDE+PDE | ARD
 | 2269 | 3239.25 | 1322.7
FEL user operation 33% 2269 h
Studies and user preparation 48% 3239 h
Accelerator R&D 19% 1323 h
2030 h User Experiments
239 h Methods and Instr. Dev.
FLASH2 Operation 2018
FLASH2: 6831 operating hours
Chart: 
| SASE | Tuning+Set-up | Stand-by | Down
 | 1820.65 | 338.65 | 52.15 | 57.55
SASE delivery 80.3% 1821 h
Tuning + Set-up 14.9% 339 h
Down 2.5% 57 h
Stand-by 2.3% 52 h
6831 operation hours (stand-by 1014 h)
of which 2269 h FEL user operation
scheduled maintenance 60 h
scheduled shutdowns 1717 h
exchange RF-gun RF-window 100 h
cryo maintenance 52 h

## Slide 5: FLASH Downtime Statistics 2018

## Slide 6: Downtime 2018
A: RF-6 (interlock card)
B: Magnet controls
C: LLRF (ACC23), Magnet PS / Magnet controls
D: Major power cut
E: Power glitch (1 s)
F: Cryogenics, Vacuum (SSK), RF-gun IR-detector
G: RF-gun window
H: Photon beamline
I: Cryogenics
J: LLRF (ACC23), RF-2, operating, photon beamline
K: Photon beamline
L: Photon beamline
Chart: 
Week
5
10
25
30
40
15
20
35
50
45
4%
B
C
D
F
Downtime (%)
E
A
G
H
I
J
RF-gun window exchange
FLASH1: Total down 3.7%
FLASH2: Total down 3.4%
K
L
1
Shutdown
Shutdown

## Slide 7: Downtime 2018 (zoom)
A: RF-6 (interlock card)
B: Magnet controls
C: LLRF (ACC23), Magnet PS / Magnet controls
D: Major power cut
E: Power glitch (1 s)
F: Cryogenics, Vacuum (SSK), RF-gun IR-detector
G: RF-gun window
H: Photon beamline
I: Cryogenics
J: LLRF (ACC23), RF-2, operating, photon beamline
K: Photon beamline
L: Photon beamline
Chart: 
Week
5
10
25
30
40
15
20
35
50
45
4%
B
C
D
F
Downtime (%)
E
A
G
H
I
J
FLASH1: Total down 3.7%
FLASH2: Total down 3.4%
K
L
1
Shutdown
Shutdown
2%
1%

## Slide 8: Downtime Reasons 2018
P11: January – June 2018
FLASH Linac : 3533 operating hours
P12: July – December 2018
FLASH Linac: 3570 operating hours
Chart: 
| RF-Stations P11 | RF-Stations P12 | RF-gun P11 | RF-gun P12 | LLRF P11 | LLRF P12 | Magnets + Magnet controls P11 | Magnets + Magnet controls P12 | Controls P11 | Controls P12 | Timing P11 | Timing P12 | Cryogenics P11 | Cryogenics P12 | Power glitches + cuts P11 | Power glitches + cuts P12 | Water P11 | Water P12 | Air conditioning P11 | Air conditioning P12 | Injector Lasers P11 | Injector Lasers P12 | Kickers P11 | Kickers P12 | Vacuum components P11 | Vacuum components P12 | Operating P11 | Operating P12 | Others P11 | Others P12 | Photon beamlines P11 | Photon beamlines P12
FLASH Linac | 15.55 | 7.85 | 3.55 | 25.9 | 9.95 | 10.2 | 18.8 | 2.3 | 7.3 | 5.3 | 0 | 1.7 | 5.7 | 2.5 | 33.75 | 0.4 | 4 | 3.5 | 0 | 0 | 0 | 0 | 1.5 | 0 | 4.6 | 0 | 7.7 | 5.8 | 3.35 | 3 | 1.4 | 2.35
FLASH1 | 0 | 0 | 0 | 0 | 0 | 0 | 7.6 | 0.5 | 1.4 | 0.85 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.45 | 1.1 | 0 | 0 | 0 | 3.85 | 0.8 | 0.2 | 0.55 | 11.75 | 43.9
FLASH2 | 0 | 0 | 0 | 0 | 0 | 5.8 | 0.6 | 0.5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.35 | 3.35 | 1.15 | 2 | 1.1 | 3.45 | 0 | 0 | 0.4 | 2.2 | 0.3 | 1.9 | 0 | 2.3
Downtime (hours)
RF-Stations
RF-Gun
LLRF
Magnet PS + Magnet Controls
Controls
Timing
Cryogenics
Power Cuts +
Power Glitches
Water
Air conditioning
Injector Lasers
Kickers
Vacuum components
Operating
Others
Photon Beamlines
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
P11 P12
FLASH Linac down
Only FLASH1 down
Only FLASH2 down
Notes: This year 2 power cuts -> ~10h already

## Slide 9: FLASH Tuning

## Slide 10
FLASH1 Operation 2018
Chart: 
| User | MDE+PDE | ARD
 | 4188.5 | 2109.8 | 804.65
FEL user operation 59% 4189 h
Studies and user preparation 30% 2110 h
Accelerator R&D 11% 804 h
Chart: 
| SASE | Tuning+Set-up | Down | Blitz
 | 3426.35 | 616.85 | 145.3
SASE delivery 81.8% 3427 h
Tuning + Set-up 14.7% 617 h
Down 3.5% 145 h
FLASH1: 7103 operating hours
7103 operation hours
of which 4189 h FEL user operation
scheduled maintenance 59 h
scheduled shutdowns 1445 h
exchange RF-gun RF-window 100 h
cryo maintenance 53 h

## Slide 11: FLASH1 operation statistics in the user runs of the last years
Chart: user run statistics
| 2014 | 2015 | 2016 | 2017 | 2018
SASE delivery (%) | 0.74446 | 0.78286 | 0.80749 | 0.80156 | 0.8181
down (%) | 0.042148 | 0.043963 | 0.03462 | 0.032036 | 0.034614
set-up (%) | 0.21339 | 0.17318 | 0.15789 | 0.16641 | 0.14729

## Slide 12: FLASH1 operation statistics in the user runs of the last years
Chart: user run statistics (FLASH1)
| 2014 | 2015 | 2016 | 2017 | 2018
SASE delivery (%) | 0.74446 | 0.78286 | 0.80749 | 0.80156 | 0.8181
down (%) | 0.042148 | 0.043963 | 0.03462 | 0.032036 | 0.034614
set-up (%) | 0.21339 | 0.17318 | 0.15789 | 0.16641 | 0.14729
Chart: requested number of bunches (FLASH1 / user shifts in percent)
| 2015 (June-Dec.) | 2016 | 2017 | 2018 | 2019 (Jan.-June)
1-30 | 0.61714 | 0.43307 | 0.53648 | 0.45638 | 0.44615
31-399 | 0.20571 | 0.2126 | 0.12017 | 0.16107 | 0.12308
≥ 400 | 0.17714 | 0.35433 | 0.34335 | 0.38255 | 0.43077
Notes: Stability becomes more and more an issue

## Slide 13: FLASH1 + FLASH2 User Operation
Chart: 
| FL1 | FL2 | FL1 | FL2 | FL1 | FL2 | FL1 | FL2 | FL1 | FL2 | FL1 | FL2 | FL1 | FL2 | FL1 | FL2 | FL1 | FL2
Series 1 | 4.4 | 0.2 | 0 | 0.4 | 2.3 | 0.3 | 0.3 | 3.6 | 4.5 | 0.25 | 0.25 | 15.85 | 24 | 0.2 | 0.2 | 24 | 0.55 | 20.1 | 20.1
Series 2 | 3.5 | 4.2 | 1.9 | 0.2 | 5.75 | 1.45 | 0.1 | 1 | 5.65 | 1.6 | 0.05 | 6.55 | 1 | 4.65 | 0.05 | 0.15
Series 3 | 16.1 | 1.25 | 0.2 | 21.5 | 17.95 | 4.4 | 0.25 | 18.5 | 1.85 | 4 | 8.1 | 17.25 | 5.15 | 0.15 | 3.85 | 3.75
Series 4 | 4.25 | 21.5 | 17.85 | 0.45 | 0.15 | 6.15 | 17 | 1.8
Series 5 | 14.1 | 1 | 4.1 | 0.5 | 0.65 | 0.7
Series 6 | 2.75 | 0.5 | 0.5 | 12.65
Series 7 | 0.2 | 1.2 | 2.5 | 0.05
Series 8 | 0.15 | 10.3 | 8.5 | 3.45
Series 9 | 0.6
Series 10 | 1.15
Series 11 | 0.1
Series 12 | 13.65
FL1: Delivery: 85%, Tuning + Set-up: 11%, Down: 4%
FL2: Delivery: 84%, Tuning + Set-up + Stand-by: 15 %, Down: 1 %
A
A
B
B
A
A
B
B
B
FL1: 30 nm, 1 bunch, 220 pC
FL2: 50 nm, 60 - 80 b 200 kHz, 90 pC, L3
A:
FL1: 13.4 nm, 1 bunch, 280 pC, THz
FL2: 21.3 – 21.7 nm, 1-100 b 40/200/250 kHz, 60 - 80 pC, L3
B:
SASE Delivery
Set-up+Tuning
Down (Machine failures)
Stand-by
Time (h)
Night shift
Afternoon shift
Morning Shift
Sun
Wed
Tue
Thu
Fri
Mon
Sun
Mon
Sat
7h00
15h00
23h00
07h00
18.3. – 26.3. 2018
Notes: This means a typical run without changing the users lasting 2 days:
Setup: ~ 7h (mainly in the beginning)
Down: ~ 1.5 h
SASE delivery; ~ 39.5h

## Slide 14: Typical FLASH1 User Operation

## Slide 15: Setup-Prozedur

## Slide 16: FLASH setup
Shift docu
Setup preparation (open FLASH2 undulators, remove RF-slopes & RF-steps, switch off feedbacks, switch off FLASH2 undulator optics)
Gun-phase scan and on-crest phase scan of modules
Check virtuell cathode (not need for every setup)
Set bunch pattern for FLASH 1 & 2
Sequencer (load machine file)
Setup LLRF (or check)
Restore charge & compression
Restore transmission / orbit
Reduce losses
Measure and correct Dispersion
SASE tuning
Check wavelength
scaling (if needed)
Special SASE tuning (short pulses, pointing, long bunch trains, high charge (mainly used for THz), High Pulse Energy …)

## Slide 17: FLASH setup
Special SASE tuning:
  Long pulse trains maximum length
  Short pulses (tuning time and time for LOLA measurement required)
  High or Low energy (>1.1 GeV or <0.45 GeV, LLRF adjustment needed)
  High Pulse Energy
  Bandwidth narrow & large (chirps)
  high charge (>0.5 nC) / THz
  Large difference between FLASH1 and 2
  Strict pointing requirements
  Chirps on the beam
  Double bunches
  Third & fifth harmonics

## Slide 18: standard setup
task | min. time (min) | typ. time (min) | max. time (min)
Shift documentation | 10 | 15 | 20
Preparation setup | 1 | 2 | 5
Gun-phase scan | 12 | 20 | 45
Phase scan of modules | 10 | 15 | 40
Set bunch pattern | 1 | 2 | 5
Sequencer (load machine file) | 15 | 20 | 30
Setup (or check) LLRF (<1.1 GeV) | 5 | 10 | 30
Restore charge & compression | 5 | 10 | 15
Restore transmission / orbit | 0 | 15 | 40
Reduce losses | 0 | 30 | 60
Dispersion | 0 (not done) | 10 | 15
SASE tuning | 30 | 90 | 150
Check wavelength | 11 | 15 | 20
 | 1:40 | 4:14 | 8:15

## Slide 19: Standard + special setup
task | min. time (min) | typ. time (min) | max. time (min)
scaling |  |  | 
Sequencer | 10 | 15 | 25
Setup (or check) LLRF | 5 | 10 | 20
Restore transmission / orbit | 0 | 5 | 15
Reduce losses | 0 | 15 | 30
Dispersion | 0 | 5 | 10
SASE tuning | 30 | 60 | 90
Check wavelength | 11 | 15 | 20
Time scaling once | 0:56 | 2:05 | 3:30
LOLA setup / measurement | 20 | 30 | 45
SASE tuning special requirements | 30 | 90 | 210
Setup + scaling once + special tuning | 3:26 | 8:19 | 16:00
task | min. time (min) | typ. time (min) | max. time (min)
Shift documentation | 10 | 15 | 20
Setup preparation | 1 | 2 | 5
Gun-phase scan | 12 | 20 | 45
Phase scan of modules | 10 | 15 | 40
Set bunch pattern | 1 | 2 | 5
Sequencer (load machine file) | 15 | 20 | 30
Setup (or check) LLRF | 5 | 10 | 30
Restore charge & compression | 5 | 10 | 15
Restore transmission / orbit | 0 | 15 | 40
Reduce losses | 0 | 30 | 60
Dispersion | 0 | 10 | 15
SASE tuning | 30 | 90 | 150
Check wavelength | 11 | 15 | 20
Time for simple setup | 1:40 | 4:14 | 8:15

## Slide 20: What can we optimize ?
task | min. time (min) | typ. time (min) | max. time (min)
scaling |  |  | 
Sequencer | 10 | 15 | 20
Setup (or check) LLRF | 5 | 10 | 20
Restore transmission / orbit | 0 | 5 | 15
Reduce losses | 0 | 15 | 30
Dispersion | 0 | 5 | 10
SASE tuning | 30 | 60 | 90
Check wavelength | 11 | 15 | 20
Time scaling once | 0:56 | 2:05 | 3:25
LOLA setup / measurement | 20 | 30 | 45
SASE tuning special requirements | 30 | 90 | 210
Setup + scaling once + special tuning | 3:20 | 8:19 | 15:35
task | min. time (min) | typ. time (min) | max. time (min)
Shift documentation | 10 | 15 | 25
Setup preparation | 1 | 2 | 5
Gun-phase scan | 12 | 20 | 45
Phase scan of modules | 10 | 15 | 40
Set bunch pattern | 1 | 2 | 5
Sequencer | 15 | 20 | 30
Setup (or check) LLRF | 5 | 10 | 30
Restore charge & compression | 5 | 10 | 15
Restore transmission / orbit | 0 | 15 | 40
Reduce losses | 0 | 30 | 60
Dispersion | 0 | 10 | 15
SASE tuning | 30 | 90 | 150
Check wavelength | 11 | 15 | 20
Time for simple setup | 1:34 | 4:14 | 7:55

## Slide 21: FLASH setup - conclusion
  What can we optimize at the current situation?
  Setup times for user operation can only be improved significantly with current FLASH layout by optimizing the scheduling, means reducing the numbers of setups, unfortunately this is limited by constraints on experimental side, like in manpower, experiment setup time & sample exchange time, …
  For the success of the experiment the present scheduling seems the best compromise
  From the variable gap undulators in FLASH1 we would gain:
  we have only two or three fixed beam energies and thus a new setup is not required so often
  we don’t need to scale files, because wavelength changes are realized by opening and closing the undulators