## Slide 1: Tests on Chess 2 ASIC
Yubo HanIHEP , Dionisio Doering, Pietro Caragiulo, Larry Ruckman, Camillo Tamma, Su Dong

## Slide 2: Pixel description

## Slide 3: Outline
Review:
  A sharp peak with correct time information of Qinj observed
  Pre-amp (preliminary) optimization based on the sharp peak
Tests: (the uniformity of pixels in one matrix)
  Check Trimming
    Changing the VPTtrim value from 1~15
    If Difference of results from different pixels varies with VPTrim
  Check performance of the whole matrix
    Validation of the stream readout
    Distribution of the “BL”, Noise level, signal level
    Updates on decoding and processing code

## Slide 4: Check Trimming: varies VPTrim
Trimming’s goal: to have even BL/TH among pixels in one matrix
Board #01: std resistance (200Ohm/cm)
Counts number vs threshold
One random pixel : (41,21)
BL = 0.7V
Bias voltage: -30V
Qinj : +2V (0~2V)
[50ns width, no delay]
VPTrim : 1~15
No big change observed

## Slide 5: Check Trimming: difference between 4 pixels
If the difference between 4 pixels changes with different VPTrim
(37,18),(37,20),(37,22),(37,24)
Same testing configuration
Enable one pixel at a time
VPTrim: 1,6,9,11
Slightly different (too small to know if we could benefit from it)

## Slide 6: Validation of the stream readout
Enable one pixel: (41,21). (Same test configuration)
3-d map (see from the row direction) col-row-threshold
The Counts vs threshold
Qinj
No Qinj
Qinj
No Qinj
Clear Difference between Qinj and noQinj

## Slide 7: Validation of the stream readout
How many pixels we could read at a time
Gradually increase the testing pixels up to 11
(41,21)+(1,21),(5,21),(9,21),(13,21),(17,21),(21,21),(25,21),(29,21),(33,21),(37,21)
Read 1000 frame at each Threshold step
Two 3-d plot with 6 and 11 pixels enabled shown on the right
(already see difference actual “BL”)

## Slide 8: Validation of the stream readout
How many pixels we could read at a time
Gradually increase the testing pixels up to 11
(41,21)+(1,21),(5,21),(9,21),(13,21),(17,21),(21,21),(25,21),(29,21),(33,21),(37,21)
Read 1000 frame at each Threshold step
Counts vs Threshold of pixel (41,21) of different number of pixels enabled at a time
8 pixels (could be changed)

## Slide 9: Testing all the pixels in Matirx 1
Tests to loop over all the pixels:
Matrix 1 (Matrix 2 has an extremely hot pixel)
Qinj +2V [50ns width no delay]
Bias: -30V (0.81mA)
BL=0.7V(868) Threshold sweeping: 818~976 (step:2)
1000 frames at each threshold
Enable 8 pixels at a time(in different row)
  (0,0),(15,0)……(112,0)
  (1,0),(16,0)……(113,0)
  …
  (15,0),(30,0)……(127,0)
Data: 512 files (65GB)
Update the data processing scripts to a c++ package (much faster)

## Slide 10: Tests on all the pixels
#01 board (200 Ohm/cm)
Plots : The total Counts number with Qinj (map)
Column = 3-10 is known dead region for this device
Higher Counts at right bottom corner
Temperature related?

## Slide 11: Tests on all the pixels
Comparing the actual BL level
Configuration:
BL = 0.7V(868)
Plots: threshold value for left edge at 800/1000 Counts
nonuniform distribution different with total Counts number distribution.
~0.016V(20) difference in general

## Slide 12: Tests on all the pixels
Trying to get the signal level
BL = 0.7V(868)
Plots: threshold value for right edge at 800/1000 Counts
nonuniform distribution
Higher at right bottom corner
~0.024V(30) difference in general

## Slide 13: Tests on all the pixels
To get the signal size
Plots: TH_2-TH_1
TH_1: start from lower threshold (800/1000)
TH_2:start from higher threshold (800/1000)
nonuniform distribution
Higher at right bottom corner
~24mV(30) in general

## Slide 14: Tests on all the pixels
Set The counts requirement to 500/1000
TH_2-TH_1 ~40mV(50) (slightly bigger)
TH_1
TH_2
Range

## Slide 15: Tests on all the pixels: Qinj off
NoQinj
Tests on half of the pixels
100 frames per threshold
Plot: Total Counts number

## Slide 16: Tests on all the pixels: Qinj off – threshold with Counts of 50/100
Range: noise level of each pixels
Range ~ 8mV(10) in general
TH_1
TH_2
Range

## Slide 17: Tests on all the pixels: Qinj off – threshold with Counts of 100/100
Range ~ 4mV(5) in general
TH_1
TH_2
Range

## Slide 18: Summary and next
Tests about the Trimming function -> seems not working
Validate that the stream readout could see the sharp peak
Test with 8 pixels enabled at a time looping over whole matrix
  The actual BL distribution
  The signal and noise level distribution
  …
Next:
  If the delay of latching the data related to the misaddress problem
  More performance study of pixels from different part of the matrix
  Mask bad performance pixels ……

## Slide 19: Backup: No Qinj – Counts number
TH_2
Increase the counts requirement to get over the peak at threshold=900
Or just block those pixels

## Slide 20: BACKUP
Counts vs threshold
Pixel： (41,21)