Alignment with beam halo MC
Andrea Parenti (DESY)
01.09.2009

---
Outline
Distributions from 229 Beam Halo (BH) events (3.4 M)
Tracker alignment, to module level, with Minimum Bias (MB) events (u, w, γ parameters in endcaps)
As above, also with Beam Halo tracks
Tracker alignment, to module level, with Minimum Bias events (u, v, γ parameters in endcaps)
Concluding remarks

---
Beam Halo: track selection
New beam halo sample:
  - CMSSW 229
  - /store/mc/Winter09/TkAlBeamHalo/ALCARECO/STARTUP_V11_StreamALCARECOTkAlBeamHalo-v4/
  - 3.4M events
Track selection:
  - pMin = 10.	(no ptMin cut)
  - etaMin = -999.	/ etaMax = +999.
  - nHitMin = 6	/ nHitMin2D = 2
  - chi2nMax = 50.
660k selected tracks

---
Selected tracks: distributions
Track momentum p:
Track transverse momentum pt:

---
Selected tracks: distributions
Track reduced χ2:
Track # of hits:

---
Minimum bias: track selection
Minimum bias production by Gaelle:
  - CMSSW 22X
  - /castor/cern.ch/user/b/boudoul/221/TkAlMinBias/
  - 5.3M events
Track selection:
  - ptMin = 2.5
  - etaMin = -999.	/ etaMax = +999.
  - nHitMin = 9	/ nHitMin2D = 3
  - chi2nMax = 50.
4.9M selected tracks

---
Configuration file
Tracker parameters:
#--- Pixel
'PixelHalfBarrelDets,rrr00r',
'TrackerTPEModule,111001',
#--- TIB
'TIBSSDets,101111',
'TrackerTIBModuleUnit,101111',
#--- TOB as reference
'TOBSSDets,101001',
'TrackerTOBModuleUnit,101001',
#--- TID/TEC
'TIDDets,101001,endCapSS',
'TrackerTIDModuleUnit,101001',
'TECDets,101001,endCapSS',
'TrackerTECModuleUnit,101001'
(Thanks to Gero for providing it!)
Starting geometry: IDEAL_V12::All

---
Alignment: TID
MB only:
MB + BH:
Δu	= 22 μm
Δw	= syst mov's
Δγ	= 70 μrad
Δu	= 12 μm ↓
Δw	= syst mov's
Δγ	= 130 μrad ↑

---
Alignment: TEC
MB only:
MB + BH:
Δu	= 18 μm
Δw	= syst mov's
Δγ	= 61 μrad
Δu	= 22 μm ↔
Δw	= syst mov's
Δγ	= 130 μrad ↑

---
Some remarks
By using Minimum Bias:
  - Δw is not well constrained
By using Beam Halo:
  - Δu gets better in TID, changes a little in TEC
  - No change in Δw structure
  - Δγ got worse
Next try: align u, v, γ parameters in TID/TEC
  - tried on Minimum Bias only, for the time being (see next slides)

---
Alignment: TID & TEC
MB only, TID:
MB only, TEC:
Δu	= 10 μm
Δv	= 44 μm
Δγ	= 71 μrad
Δu	= 23 μm
Δw	= 53 μm
Δγ	= 62 μrad

---
Concluding remarks
Performed an alignment of tracker to module level, with minimum bias and beam halo, starting from ideal geometry
  - some parameters slightly better, other worse...
Next steps:
  - decrease pMin in beam halo (eg 10 → 5) to get more tracks
  - align u, v, γ in TID/TEC with MB and BH events
  - if results are encouraging, start from misaligned geometry

---
Additional slides

---
Alignment: all tracker
MB only:
MB + BH:

---
Alignment: TID
MB only:
MB + BH:

---
Alignment: TEC
MB only:
MB + BH: