## Slide 1: Vorstellung & Projektziele
Prof. Dr.-Ing. Michael Karagounis
13.02.2019 Heidelberg
Interessensgemeinschaft für
Mikroelektronik & Eingebettete Systeme
Kick-Off Verbund Tracking

## Slide 2: Berufliche Stationen
Professor für Elektronik, Fachhochschule Dortmund
  Analog/Digital CMOS Design
  Bauelemente & Schaltungen
  Mikrocontroller Programmierung
Professor für Grundlagen der Elektrotechnik, Hochschule Hamm-Lippstadt, Hamm
RF Designer, Intel Mobile Communications GmbH, Duisburg
  PLL für GNSS Frontend in TSMC 28 nm
Analog/Mixed Signal CMOS IC Designer, EPOS GmbH & Co. KG, Duisburg
  Digital Controlled Voltage Regulator in TSMC 65 nm
Promotion zum Dr.-Ing. , Prof. Wupper (Fernuni Hagen), Prof. Wermes (Uni Bonn)
  Dissertation: „Analog Integrated CMOS Circuits for the Readout and Powering of Highly Segmented Detectors in Particle Physics Applications“

## Slide 3: Laborvorstellung
IMES: Interessengruppe für Mikroelektronik und eingebettete Systeme
Laborgruppe besteht aus 3 Professoren, 2 technische Mitarbeiter, 5 Doktoranden
Mitgliedschaft bei Europractice und Mosis
EDA Cluster
  2 Linux Server (1 TB RAM, 24 Kerne)
  15 Linux PCs
EDA Software
  15 Cadence Lizenzen
  10 Mentor Lizenzen
  3 (Analog) +1(Digital) Synopsys Lizenz
Designkits für verschiedene Technologien
  TSMC, UMC, Globalfoundries, AMS
Forschungsprojekte
  Shunt-LDO Regler für Serial Powering bei ATLAS und CMS (RD53)
  DCS Controller Chip für den ATLAS Pixel-Detektor (ATLAS / Uni Wuppertal)
  VULCAN Photomultiplier Readout-Chip (JUNO / Forschungszentrum Jülich)
  Time-of-Flight Sensorik (ELMOS AG)
  Optische Winkelmessung (Adivco Microelectronics)

## Slide 4: Forschungsthemen im Rahmen des Tracking Verbundes
Verbesserungen des Shunt-LDO Reglers für Serial Powering
  Verbesserung der Reglereigenschaften durch bessere Biasing-Schaltungen
  Schutzschaltungen gegen Überspannung & Überlast
  Low-Power Mode für die Installationsphase
  Startup
  Stabilisierung ohne externen Kondensator (capless)
Vollintegrierter DC/DC Wandler mit Wandlungsfaktor 4
  Hochfrequenz Buck-Converter unter Verwendung interner Induktivitäten & Wire-Bonds
  Switched-Capacitor Wandler
DCS Controller Chip für das Kontrollsystem des ATLAS Pixeldetektors
  CAN zu I2C Brückenchip
  CanOpen kompatible Brückenlogik
  Strahlenharte 5V Regler
  Strahlenharte CAN Driver/Receiver
  Strahlenharter / SEU toleranter Mikrocontroller (MIPS, ARM, RISC-V)

## Slide 5: Shunt-LDO Regulator Concept
The Shunt-LDO regulator combines the functionality of an LDO voltage regulator with the capability of a shunt regulator to drain a constant current
Two control loops: 1) constant output voltage 2) constant current flow through the regulator
k : 1

## Slide 6: V/I Characteristic

## Slide 7: Modifications to Bias Scheme
External resistor Riref to improve radiation tolerance of main reference current Iref
Configurable Rofs resistor for high Vofs voltage in low power mode
Vofs startup circuit for startup with low input currents in low power mode
Vref
Vofs

## Slide 8: Under Shunt Protection
overload current situation is considered as undershunt current scenario
  high load current reduces shunt current
In undershunt current case Vref is reduced
minimum voltage defined by current source
  Vmin=2.3µA x 150kOhm=350mV
additional injected current (1-2µA) can be configured by DAC setting
At shunt current lower < 11 mA additional current is disabled

## Slide 9: Under Shunt Current Limitation Nominal Simulation
Vin
Vout
Vref
Ishunt
Iload(negative)

## Slide 10: Overvoltage Protection Voltage Clamp
voltage clamp implemented as shunt regualtor
Operated in parallel to SLDO
takes all excess current in case Vin =>2v

## Slide 11: Rectification Circuit and Low Power Mode Interface
C1=100nF
C2=1pF
C3=1pF C4=10pF R2=10MΩ R4=10MΩ
Rectification circuit with 2x multiplication circuit
AC signal is inverted and applied to a transistor in parallel two one of Rofs resistiors
  Inverter is supply by Vpre using a resistor instead of PMOS to avoid SEU issues

## Slide 12: AC rectifier operation
UD2
UD3
UC4
AC input signal with 1.2V peak to peak amplitude and 1MHz frequency

## Slide 13: Switching between High-Power and Low-Power at 1 A input current
Isup
Vin
Vofs
Vout
AC

## Slide 14: Vofs Startup Circuit
wide-swing cascode current mirror with low-vt NMOS transistors draw current first
standard cascode current mirror wit reg-vt PMOS transistrs drain current later
  difference between current is injected to Rofs
Low-VT NMOS
Reg-VT PMOS

## Slide 15: Vofs Startup Circuit Simulation
IstartN
IstartP
Vin
VofsHalf
Iextra

## Slide 16: DCS Controller Chip Purpose
serves as gateway between the CAN bus of the DCS computer and the SCB bus to which the PSPP chips are connected to
placed at Patch Panel 0 (PP0) at the End of Sub-structure card (EoS)
CAN has been chosen for communication due to robustness and reliability
provides local monitoring functions (temperature) for the installed location
c
.
a
.
100
m
Pixel
-
Module
Pixel
-
Module
Pixel
-
Module
Pixel
-
Module
Pixel
-
Module
PSPP Chip
PSPP Chip
PSPP Chip
PSPP Chip
PSPP Chip
I
0
c
c
U
0
DCS
Controller
DCS
Computer
CAN
SCB

## Slide 17: DCS Controller Chip Blocks
CAN Protocol Unit
CAN Receiver
CAN Driver
SCB Protocol Unit
SCB Receiver
SCB Driver
Bridging Logic
Voltage Regulators
Power-On Reset
ADC
Oscillator

## Slide 18: 3.3V CAN Driver with levelshifter
Levelshifter
CAN Driver needs 3.6V CMOS signal to switch transistor M6
Levelshifter translates EN signal from 1.2V to 3.6 V voltage level
Levelshifter consists of lower and upper part
Lower part is a switchable resistive voltage divider
Divison ratio depends on switching state
Lower part shifts signals above 2.4 V
Upper part is classical levelshifter circuit
Creates CMOS signal switching between 2.4V and 3.6V
CAN Driver

## Slide 19: 3.3V CAN Receiver
Resitive voltage division by 1/3 for CAN level to 1.2V CMOS level adaption
  non-symmetric voltage divider for recessive state detection
Rail-to-Rail comparator stage (concept reuse from FE-I4)

## Slide 20: Power Supply Architecture
Three linear regulators for the required supply volages of 1.2V, 2.4V and 3.6V
  The higher the output voltage the smaller the number of cascoded pass-device transistors
The 1.2V regulator supplies also the amplifier of the 2.4V and the 3.6V regulator
The 1.2V regulator requires a startup-circuit circuit
  due to feedback loop from regulator output voltage to amplifier supply voltage
x 7 Pass-Devices
x 5 Pass-Devices
x 3 Pass-Devices
Common Supply Rail

## Slide 21: Complete 1V2 Regulator Circuit
Startup Circuit
Error Amplifier
Error Amplifier Biasing
Pass-Device Biasing
ESR Compensation

## Slide 22: Zusammenfassung & Ausblick
Shunt-LDO Regler & DCS Controller Chip
  Anspruchsvolle Projekte mit wenig Ressourcen unter hohem Zeitdruck
  Bei SLDO: Robustheit & Sicherheitsmaßnahmen im Vordergrund
  Bei DCS Controller: strahlenharte Schaltungen bei 5V Betrieb
Raum für innovative Themen & Ideen
  Reduktion der Anzahl externer Komponenten bei Spannungsreglern
  SEU-/strahlenharte Mikrocontroller

## Slide 23: Parallel vs Serial Powering Scheme I
Modules are connected in parallel
Powered by constant voltage source
Total supply current scales with the number of modules
Large supply currents affect efficiency
IR drops on power cables
DC/DC conversion decreases supply current and increases efficiency
DC/DC conv. has high material budget

## Slide 24: Parallel vs Serial Powering Scheme II
Modules are connected in series
Powered by constant current source
Total supply current is defined by maximum load current of a single module
Total supply voltage across the chain scales with the number of powered modules
Regulator circuitry required to generate constant supply voltage out of constant current

## Slide 25: The Serial Power Commandments
You shall prevent the break of the serial powering chain
You shall avoid hot spots
You shall distribute power equally across the chips and the module
You shall avoid single point of failure
You shall introduce redundancy
You shall operate several regulators in parallel

## Slide 26: Shunt Regulator Operation Principle
Voltage regulation by current steering
Current flow through load defines
Referenced voltage
Excess current is shunted by M1

Very steep voltage to current characteristic
Small voltage source output impedance J
Unbalanced current distribution across parallel placed regulators L
Parallel placed regulators generate different
  voltage reference variations
  error amplifier offset
  resistor mismatch
  ground shifts
Current will flow through regulator with small
Regulator may be destroyed due to overload cond.