## Slide 1: REDUNDANT CPU ON MTCA SYSTEM WITH PCI EXPRESS NON TRANSPARENT BRIDGE
L.Petrosyan (DESY)

## Slide 2: PCI Express NTB
NTB used to connect two independent address/Host domains
A Non-Transparent bridge consist of two back-to-back PCIe endpoints, a Virtual and Link side endpoints.
NTB isolates Address spaces of different Hosts by appearing as an endpoint to each side
NTB Provides:
Allow to have second CPU on MTCA system (7th MicroTCA Workshop)
Allow to have redundant CPU on MTCA system (now)
Upstream
PortA
Downstream PortB
Virtual Side
NTB
PortC
Link Side
Host 1
Host 2

## Slide 3: NTB FAILOVER
To protect against a failing Host taking the entire system down, a backup Host can be in place, ready to take over.
Upstream
PortA
Downstream PortB
Virtual Side
NTB
PortC
Link Side
Host 1
Host 2
Upstream
PortC
Downstream PortB
Virtual Side
NTB
PortA
Link Side
Host 1
Host 2
The passive Host2 is waiting for the active Hos1t to fail.
When the Virtual side Host1 fail, passive Host2 initiates the sequence:
Configure PortA to be the NT Port and PortC to be the Upstream Port
Reset Upstream Port Secondary Bus
Re-enumerate the hierarchy and start operation.

## Slide 4: Redundant CPU Test
NAT MCH with PEX8748 PCIE Switch
Host1 in Slot 1 (PCIE Switch Port19)
Host2 in Slot 8 (PCIE Switch Port16)
PCIENTBV – PCIE NTB device driver is running on both CPUs

## Slide 5: Redundant CPU Test
Virtual Side Host1(Upstream Port)
LOAD DRIVER
DETECKT SIDE
USER.NOTIFY
START/STOP
FAILOVER
START
COUNTER
USER.CMND
RESENT COUNTER
DELAY
LOAD DRIVER
DETECKT SIDE
USER.NOTIFY
Link Side Host2 (NTB Port)
GET START
GET COUNTER
INCREMENT
COUNTER
DELAY
RECONFIGURE
PCIE SWITCH
NOTIFY USER
REBOOT
USER.NOTIFY
NTB SCRATCH REG.
REBOOT_NOTIFIER
Is START
NO
Is COUNTER 0
NO
Fail checking could be started-stopped by user or by OS, for example, when the system is going to be rebooted
Force Ports reconfiguration
Configure.
Upstream Port as NTB
NTB Port as Upstream
Do not start failover while the Host1 is not loaded

## Slide 6: Redundant CPU Test
Virtual Side Host 1.
All AMC cards are visible from this side
NTB Endpoint in slot 8 (Port 16, 10:00.0)
Link Side Host 2.
Only NTB Endpoint is visible

## Slide 7: Redundant CPU Test
Heartbeats messages on the Link Side Host2 NTB devise driver
Using NAT MCH Diag tool, we can see the PCIE Switch Upstream Port Register is changed
Host1 is OK
Host1 Fail
Port 19 Upstream, Port 16 NTB
Port 16 Upstream, Port 19 NTB

## Slide 8: Redundant CPU Test
After the Host1 fail is detected, the NTB device driver has reconfigured the PCIE switch and rebooted the CPU
Now Host 2 is Upstream host, and we can see all AMC modules from this host.
The same picture we had before on Host1

## Slide 9: Info
The source codes can be found on https://github.com/MicroTCA
The information and Linux packages can be found on a DOOCS web page http://doocs.desy.de
Mail doocs@desy.de
THANK YOU