## Slide 1: XFEL Beam Distribution Kicker System
LUXE Workshop
Frank Obier
Hamburg,16.04.2019

## Slide 2: Layout of Accelerator
TLD
T4D
T5D
SASE1
SASE3
SASE2

## Slide 3
A Typical Pattern for User Operation
| XFEL Beam Distribution Kicker System | Frank Obier, 16.04.2019
… driving SASE1, SASE2, and SASE3 simultaneously.
TLD
Pilot bunches for Feedbacks
SASE1
SASE3
kicked bunches to suppress lasing in SASE1
TLD
Gap for the rise time of beam distribution
kicker KL
SASE2
KS Kickers
KL Kickers
TL
T5D
T4D
Experiments
SASE2
SASE1
SASE3

## Slide 4
| XFEL Beam Distribution Kicker System | Frank Obier, 16.04.2019
Pulse current KS Kicker
KS Kickers
KL Kickers
TL
T5D
T4D
Experiments
SASE2
SASE1
SASE3
A Typical Pattern for User Operation

## Slide 5
| XFEL Beam Distribution Kicker System | Frank Obier, 16.04.2019
Pulse current KL Kicker
KS Kickers
KL Kickers
T5D
T4D
Experiments
SASE2
SASE1
SASE3
TL
A Typical Pattern for User Operation

## Slide 6
A Typical User Pattern form 15.04.2019

## Slide 7
A Typical User Pattern form 15.04.2019
bunch train with 556 bunches

## Slide 8
A Typical User Pattern form 15.04.2019
504 bunches go to the Dump

## Slide 9
A Typical User Pattern form 15.04.2019
1 bunch for SASE 2
29 bunches for SASE 1
22 bunches for SASE 3
kicked bunches to suppress lasing in SASE1

## Slide 10
A Typical User Pattern form 15.04.2019
1 bunch for SASE 2
29 bunches for SASE 1
22 bunches for SASE 3

## Slide 11
 | Dumpkicker KS | Beam Distribution Kicker KL
Kicker typ | Stripline Kicker (50Ω) | Air-core coil kicker
Pulse frequency | 0-4.5MHz | 0-10Hz
Pulse length | 30ns | 14-600us
Pulse form | rectangular | rectangular
Rise time | 14ns | 14µs
Fall time | 15ns | 10µs
Max. pulse voltages | 5kV | 200V
Max. pulse current | 100A | 600A
Amplitude stability | 1.5% | 3*10-4
Kick angle per kicker | 0.0723mrad | 0.113mrad
Kicker active length | 2m | 0,93m
Energy | 17.5GeV | 17.5GeV
Kick angle total | 0.506mrad | 0.523mrad
Number of kicker for total kick angle | 7 | 5
Number of installed kicker | 10 | 6
Specification

## Slide 12
Kicker design:
a strip line kicker inside of vacuum
a small reflectance factor, to match the kicker impedance to 50 ohm.
with the geometry of the conductor, and the distance between the conductor and the cage you can match the kicker impedance to 50Ω.
Design Collaboration with PSI
KS Kicker (Dump Kicker) for XFEL
2m

## Slide 13
XFEL Installation Area of the KS Kicker

## Slide 14
fours version of pulser
KS (Dump) Pulser from Company FID GmbH

## Slide 15
Pulse current of KS Kicker Pulser (FID GmbH)
10ns
25ns
13ns

## Slide 16: Overlay of 1500 pulses with a spacing of 1MHz
Variable pulse pattern / Pulse voltages 4.5kV
XFEL Pulser (FID)
good stability of flat-top
good stability of flat-bottom
Test pattern 1500 Pulse „variable train“
Trigger generator

## Slide 17: Beam Distribution Kicker (KL)
Kicker design:
kicker was realized a air coil outside beam vacuum
the geometry and the material was optimized to reduce the eddy current
coating material of ceramic chamber is stainless steel 1.4541 (titan stabilised)
a small reduction of the magnetic field by the sputtered chamber (thickness is 1µm)
Conductor Vacuum chamber

## Slide 18: XFEL Installation Area of the Beam Distribution Kicker
Material PEI 1000

## Slide 19
Data:
Voltage U= 80V
Pulse current Imax=600A
Pulse length t= 1ms
8 Mosfet parallel
9 capacitor (450V 2200µF)
200µs/div
200A
Constant current source
Charge power supply
+
-
Current set point
Actual current value
8x Mosfet layer
Kicker
Damping
resistor
Capacitor
OP
+15V
-15V
Sensing resistor
Pulse length
Start up booster
Pulse length
Start up Booster
Pulse current
Principle Layout of the Pulser

## Slide 20: Rise and fall Time of the Pulse Current
Rise time = 10µs
Fall time =14µs

## Slide 21
| XFEL Beam Distribution Kicker System | Frank Obier, 16.04.2019
Measurement of pulse stability of KL Kicker Pulser
SA2 intensity at the beginning of the flat –top
SA2 intensity at the end of the flat -top

## Slide 22
Timing optimization of KL Kicker Pulser

## Slide 23
| XFEL Beam Distribution Kicker System | Frank Obier, 16.04.2019
 | Dumpkicker KS | Beam Distribution Kicker KL | LUXE Kicker | LUXE Kicker
Kicker typ | Stripline Kicker (50Ω) | Air-core coil kicker | Air-core coil kicker | Ferrite Kicker
Pulse frequency | 4.5MHz | 10Hz | 10Hz | 10Hz
Pulse length | 30ns | 14-600us | 1us | 2us
Pulse form | rectangular | rectangular | sine | sine
Rise time | 14ns | 14µs |  | 
Fall time | 15ns | 10µs |  | 
Pulse voltages | 5kV | 200V | 16000V | 4000V
Pulse current | 100A | 600A | 4800A | 1200A
Amplitude stability | 1.5% | 3*10-4 | 1*10-3 | 1*10-3
Kick angle per kicker | 0.0723mrad | 0.113mrad | 0,823mrad | 0,823mrad
Kicker active length | 2m | 0,93m | 0,93m | 0,93m
Energy | 17.5GeV | 17.5GeV | 17.5GeV | 17.5GeV
total Kick angle | 0.506mrad | 0.523mrad | 0.823mrad | 0.823mrad
Number of kicker for total kick angle | 7 | 5 | 1 | 1
Number of installed kicker | 10 | 6 | 1 | 1
Specification of LUXE Kicker
Test with a Ferrite kicker after Summer Shutdown 2019

## Slide 24
1,2µs
I=2,5kA
4kV → 1.25kA Ferrit Kicker
8kV → 2.5kA
10kV → 3.1kA
16kV → 5.0kA Air-core coil Kicker
FLASH Diagnostic Kicker for the CRISP Experiment

## Slide 25: Thank you

## Slide 26
Frank Obier
Department MIN
E-mail frank.obier@desy.de
Phone 040/8998-3050

## Slide 28
A Typical User Pattern form 15.04.2019

## Slide 29
A Typical User Pattern form 15.04.2019
bunch train with 556 bunches

## Slide 30
A Typical User Pattern form 15.04.2019
504 bunches go to the Dump

## Slide 31
A Typical User Pattern form 15.04.2019
1 bunch for SASE 2
51 bunches for SASE 1
1 bunches for SASE 3
kicked bunches to suppress lasing in SASE1

## Slide 32
A Typical User Pattern form 15.04.2019
1 bunch for SASE 2
51 bunches for SASE 1
1 bunches for SASE 3