## Slide 1: LUXE beam line design considerations
Florian Burkart (MPY1)
LUXE workshop
Hamburg, 16.04.2019

## Slide 2: Outline
01 Beam Parameters
02 Experimental layout
03 Special topics
  Spectrometer Dipole
  Photoconverter foil
04 Location at the XFEL
  XSDU1
  XTD20
05 Lattice and beam optics
06 Outlook and conclusion

## Slide 3: Beam parameters
Option 1: collide electron beam with laser pulse
Option 2: collide electron beam with foil  photon generation  collide photons with laser pulse
Electron beam parameters:
Electron energy: 17.5 GeV
Bunch intensity: up to 1 nC ( 6.25E9 e-)
Bunch length: 80 fs
Spotsize @ IP: s = 5 mm
Repetition Rate: 1 – 10 Hz
Laser beam parameters
Energy: 0.35 J / 7 J,
Power: 10 TW / 200 TW
Laser Intensity : 10 x1019 W/cm2,
Wavelength: 800 nm
Crossing angle: 0.3 radians
Focus in x-y-direction: 10 mm
Pulse length: 35 fs
1 bunch operation!
Goal: Fully transparent for XFEL operation

## Slide 4: General layout
Dump
17.5 GeV e−
Linac
Dipole
Kicker & Septa
Dipole
1bunch
Kick out one bunch and send it to the experimental area.
Experimental Area Hall
Triplet

## Slide 5: Electron - Laser Collision
Triplet
Laser
pulse
IP
Mirror
Mirror
γ
Dipole
PDET
EDET
E < 16 GeV
e−
e+
γCAL
Dipole
e+
e−
γ
CAL
Dump
~5 m
~ 20 m
~15 m
tbd
electrons

## Slide 6: Photon - Laser Collision
Collimation
γCAL
Dipole
e+
e−
γ
CAL
Triplet
Photon converter
Dipole
Counter
Counter
E < 16 GeV
e−
e+
γ
Laser
pulse
Mirror
Mirror
Dipole
PDET
EDET
E < 16 GeV
e−
e+
Dump
5 m
15 m
10 m
5 m
tbd
IP
electrons

## Slide 7: General infrastructure requirements for LUXE
Electron beam line (> 20 m )
  Magnets (Fast kickers, septa, triplet, spectrometer)
  Beam instrumentation
  Collimator
  Photoconverter
  Single bunch beam dump.
Space for ~ 150 sqm Laserlab
Laser and laser beam transport system
Detectors
General infrastructure:
  Crane, power, water cooling, ventilation, IT
  Shielding
  Integration into XFEL Control and MPS system

## Slide 8: General infrastructure requirements for LUXE
Electron beam line (~ 80 m)
  Magnets (Fast kickers, septa, triplet, spectrometer)
  Beam instrumentation
  Collimator
  Photoconverter
  Single bunch beam dump.
Space for 150 sqm Laserlab
Laser and laser transport
Detectors
General infrastructure:
  Crane, power, water cooling, ventilation, IT
  Shielding
  Integration into XFEL Control and MPS system

## Slide 9: Spectrometer Magnet
Massive Device:
1500 A
2.24 T
7500 kg
10 cm aperture
1m length

## Slide 10: Photoconverter and a 17.5 GeV electron beam
1E5
1E4
1E3
100
10
1
tol(dQ/dm): tolerable instantaneous energy deposition per pulse: ~24J/g (Tungsten), including stress in the material.
Limit at 1nC: the beam s at the foil should be >40µm,
deposited heat of 1 bunch is mostly smeared out before
the next bunch arrives 100ms later (10Hz).
35µm Tungsten Foil
Michael Schmitz
38

## Slide 11: What has changed in the last 8 months?

## Slide 12: Possible location at the XFEL
HED
MID
FXE
SPB
SQS
SCS
SASE 1
3 – 24 keV
SASE 2
3 – 24 keV
SASE 3
0.26 – 3 keV
photon tunnel
electron bend
undulator
electron dump
electron tunnel
electron switch
experiments
LINAC
17.5 / 14 / 10.5 GeV
~
~
~

## Slide 13: Schematic CAD Integration
Kicker/Septa
Bend
Triplet
IP
Dump

## Slide 14: Location Considerations – XSDU1
XSDU1
Modification of beam line – downtime to be evaluated.
Potential impact on legal situation (additional extraction/beam dump, beam line)  „risk“ of plan-approval procedure.
Maybe radiation towards XTD7  additional shiedling required.
New building at the surface.
Background from beam dump.
Already studied (optics, HW, …).

## Slide 15: Possible location at the XFEL
HED
MID
FXE
SPB
SQS
SCS
SASE 1
3 – 24 keV
SASE 2
3 – 24 keV
SASE 3
0.26 – 3 keV
photon tunnel
electron bend
undulator
electron dump
electron tunnel
electron switch
experiments
LINAC
17.5 / 14 / 10.5 GeV
~
~
~

## Slide 16: Accelerator Design
XTD20
Start point of the second fan for XFEL
TD1
TD2
TD20
dump

## Slide 18: Location Considerations – XTD20
XTD20
Uses existing building and beam line design.
Major modification of extraction beam line - downtime to be evaluated.
Extraction and beam line already included in plan-approval.
Laser beam line transport via XS1 shaft.
Early implementation of the beam extraction for future XFEL upgrade and/or test beam area.
Additional demonstration of the flexibility of the facility.
New option to be studied.

## Slide 19: Accelerator Design
Fast kicker magnets
Septa
TD20
Nina Golubeva

## Slide 20: Tunnel Infrastructure

## Slide 21: Support structure at the ceiling

## Slide 23: Kicker magnets

## Slide 24: Lattice Design downstream of the third septum

## Slide 25: Final focus
Preliminary!

## Slide 26: Triplet Magnet Parameters
Gradient: 100 T/m
Length: 10 cm
Aperture: 16 mm

## Slide 27: LUXE @ XFEL MAC
Presented at the XFEL MAC: MAC is very interested and will follow any future development of LUXE with interest.
Recommendation: evaluate risk for XFEL user operation.
Main challenge: Fit construction into XFEL schedule.
 Installation within a XFEL shutdown. No pertubation of XFEL operation.

## Slide 28: LUXE status
XTD20 lattice design ü
LUXE final focus beam design ü
Start the discussion with the DESY technical groups. ü
  Radiation protection
  MEA (installation of the beam line in the tunnel)
  ZM1 (central construction department – integration into CAD model, design and construction of support structures)
  MVS (vacuum group)
At the moment: no showstoppers visible. ü
Include also power, water cooling, safety and access system, beam instrumentation, control groups. ongoing
Preliminary estimate of timeline and ressources. ongoing
Prepare hardware table.
Preparation of installation schedule – hopefully within 2 XFEL shutdowns.

## Slide 29: LUXE and the interest of other groups
DESY radio protection showed interest in a fixed –target testbeam area.
DESY is interested in using testbeams at XFEL.

## Slide 30: Conclusion
LUXE as QED basic research – would enlarge the scientific scope of XFEL.
Theory and accelerator community is very interested in conducting this experiment at the XFEL.
DESY and XFEL directorate supportive.
Design consideration with input from various DESY technical groups.
Layout and achievable parameters look feasible.
New possible location of the experiment found in XTD20.
Major modification of extraction beam line needed.
Early implementation of the beam extraction for future XFEL upgrade and/or test beam area.
Integration, Installation and Design studies ongoing.

## Slide 31: Acknowledgements:
Winfried Decking, Beate Heinemann,
Reinhard Brinkmann, Ralph Assmann, Evgeny Negodin,
Norbert Tesch, Wolfgang Clement,
Nina Golubeva, Vladimir Balandin,
Markus Hüning, Frank Obier, Michael Schmitz
Lutz Lilje, Torsten Wohlenberg
Markus Körfer, Dennis Lenz
Cornelius Martens, Roland Platzer

## Slide 32: Thank you

## Slide 33
Dr. Florian Burkart
Department: MPY1
E-Mail: florian.burkart@desy.de
Phone: +49 40 8998 3039